## Slide 1: JVET-K0274 Reduced complexity bilateral filter
J. Ström, P. Wennersten, J. Enhorn, D. Liu, K. Andersson and R. Sjöberg
Ericsson Research
Jacob Ström
2018-07-09

## Slide 2: Refresher
transform coefficients
decoded residual
prediction
clip to [0, 1023]
recon- struction
bilateral filter
new recon- struction

## Slide 3: Background
The bilateral filter was included into JEM at the Hobart meeting
Feedback: predicting from filtered coefficients may put filter in critical path for hardware implementation for small intra blocks
previous block
current block
prediction

## Slide 4: Background
prediction
The bilateral filter was included into JEM at the Hobart meeting
Feedback: predicting from filtered coefficients may put filter in critical path for hardware implementation for small intra blocks
Thus filtering may need to be done in parallel for the closest pixels
previous block
current block
filtered in parallel

## Slide 5: Background
prediction
The bilateral filter was included into JEM at the Hobart meeting
Feedback: predicting from filtered coefficients may put filter in critical path for hardware implementation for small intra blocks
Thus filtering may need to be done in parallel for the closest pixels
This in turn means many instantiations of the look-up table (LUT).
previous block
current block
filtered in parallel

## Slide 6: Example JVET-F0096
Number of pixels filtered in parallel | weight-LUT storage needed | per-sample storage needed (division LUT) | Total size for LUTs
1 middle pixel | 4 * 2202 | 1*581 | 9389
1
2
3
4

## Slide 7: Example
1
Number of pixels filtered in parallel | weight-LUT storage needed | per-sample storage needed (division LUT) | Total size for LUTs
1 middle pixel | 4 * 2202 | 1*581 | 9389
1 edge pixel | 3 * 2202 | 1*581 | 7187
1
2
3
4
3
2

## Slide 8: Example
1
Number of pixels filtered in parallel | weight-LUT storage needed | per-sample storage needed (division LUT) | Total size for LUTs
1 middle pixel | 4 * 2202 | 1*581 | 9389
1 edge pixel | 3 * 2202 | 1*581 | 7187
1 corner pixel | 2 * 2202 | 1*581 | 4985
1
2
3
4
3
2
2
1

## Slide 9: Examples
1
Number of pixels filtered in parallel | weight-LUT storage needed | per-sample storage needed (division LUT) | Total size for LUTs
1 middle pixel | 4 * 2202 | 1*581 | 9389
1 edge pixel | 3 * 2202 | 1*581 | 7187
1 corner pixel | 2 * 2202 | 1*581 | 4985
4 edge pixels | 7 * 2202 | 4*581 | 17738
1
2
3
4
3
2
2
1
1
2
3
4
5
6
7

## Slide 10: Examples
1
Number of pixels filtered in parallel | weight-LUT storage needed | per-sample storage needed (division LUT) | Total size for LUTs
1 middle pixel | 4 * 2202 | 1*581 | 9389
1 edge pixel | 3 * 2202 | 1*581 | 7187
1 corner pixel | 2 * 2202 | 1*581 | 4985
4 edge pixels | 7 * 2202 | 4*581 | 17738
8 edge pixels | 15*2202 | 8*581 | 37678
1
2
3
4
3
2
2
1
1
2
3
4
5
6
7

## Slide 11: LUT reduction
LUT is two-dimensional, with one row for each qp.
0 1 2 3 4 5 6 7 8 9 ...
Intensity difference
qp
255, 237, 191, 133, 80, 42, 19, 7, 2, 1, 0
255, 248, 227, 196, 159, 122, 89, 60, 39, 24, 14, 7, 4, 2, 1, 0
255, 252, 242, 227, 208, 185, 161, 136, 112, 90, 71, 54, 40, 29, 21, 14, 10, ...
255, 255, 255, 254, 253, 252, 251, 249, 248, 246, 244, 241, 239, 236, 233, 230, 227, ...
255, 255, 255, 255, 255, 254, 254, 254, 253, 253, 252, 251, 251, 250, 249, 248, 248, ...
18
19
20
33
51

## Slide 12: LUT reduction
LUT is two-dimensional, with one row for each qp.
0 1 2 3 4 5 6 7 8 9 ...
Intensity difference
qp
255, 237, 191, 133, 80, 42, 19, 7, 2, 1, 0
255, 248, 227, 196, 159, 122, 89, 60, 39, 24, 14, 7, 4, 2, 1, 0
255, 252, 242, 227, 208, 185, 161, 136, 112, 90, 71, 54, 40, 29, 21, 14, 10, ...
255, 255, 255, 254, 253, 252, 251, 249, 248, 246, 244, 241, 239, 236, 233, 230, 227, ...
255, 255, 255, 255, 255, 254, 254, 254, 253, 253, 252, 251, 251, 250, 249, 248, 248, ...
18
19
20
34
51

## Slide 13: LUT reduction
Rows are just stretched versions of each other
Example
  LUTqp34(x) = LUTqp51(2*x)
  Take every second value of black curve to get blue curve
We use powers of two:
  LUTused(x) = LUTbase(x << k)
Leaves a large gap between the black and blue curve
We therefore use four base tables row
  e.g., LUTused(x) = LUTbase3(x << k)

## Slide 14: LUT reduction
LUT is two-dimensional, with one row for each qp.
0 1 2 3 4 5 6 7 8 9 ...
Intensity difference
qp
255, 237, 191, 133, 80, 42, 19, 7, 2, 1, 0
255, 248, 227, 196, 159, 122, 89, 60, 39, 24, 14, 7, 4, 2, 1, 0
255, 252, 242, 227, 208, 185, 161, 136, 112, 90, 71, 54, 40, 29, 21, 14, 10, ...
255, 255, 255, 254, 253, 252, 251, 249, 248, 246, 244, 241, 239, 236, 233, 230, 227, ...
255, 255, 255, 255, 255, 254, 254, 254, 253, 253, 252, 251, 251, 250, 249, 248, 248, ...
18
19
20
33
51

## Slide 15: Resulting storage needs
LUT is made up of four LUT base-rows of 235, 206, 178 and 150 eight-bit values. (769 bytes)
4 bytes to tell the size of each base-row (4 bytes)
2 bits to tell which base row is used and 3 bits for the shift value (2+3)*34/8 = 22 bytes
21 distanceFactor parameters of 8-bits each = 21 bytes
Total LUT size = 769+4+22+21 = 816 bytes
Previous LUT size 2783 bytes – a reduction by 71%

## Slide 16: LUT results
Previously
Number of pixels filtered in parallel | weight-LUT storage needed | division-LUT storage needed | Total size for LUTs
1 middle pixel | 4 * 2202 | 1*581 | 9389
1 edge pixel | 3 * 2202 | 1*581 | 7187
1 corner pixel | 2 * 2202 | 1*581 | 4985
4 edge pixels | 7 * 2202 | 4*581 | 17738
8 edge pixels | 15*2202 | 8*581 | 37678

## Slide 17: This proposal
Reduces size of LUT from 2202 to 816 bytes
Number of pixels filtered in parallel | weight-LUT storage needed | division-LUT storage needed | Total size for LUTs
1 middle pixel | 4 * 795 | 1*581 | 3761
1 edge pixel | 3 * 795 | 1*581 | 2996
1 corner pixel | 2 * 795 | 1*581 | 2171
4 edge pixels | 7 * 795 | 4*581 | 7889
8 edge pixels | 15*795 | 8*581 | 16573

## Slide 18: This proposal
Reduces size of LUT from 2202 to 816 bytes
Uses Qualcomm’s approximation from JVET-J0021 to get rid of division-LUT
Number of pixels filtered in parallel | weight-LUT storage needed | division-LUT storage needed | Total size for LUTs
1 middle pixel | 4 * 795 | 1*581 | 3761
1 edge pixel | 3 * 795 | 1*581 | 2996
1 corner pixel | 2 * 795 | 1*581 | 2171
4 edge pixels | 7 * 795 | 4*581 | 7889
8 edge pixels | 15*795 | 8*581 | 16573

## Slide 19: This proposal
Reduces size of LUT from 2202 to 816 bytes
Uses Qualcomm’s approximation from JVET-J0021 to get rid of division-LUT
Number of pixels filtered in parallel | weight-LUT storage needed | division-LUT storage needed | Total size for LUTs
1 middle pixel | 4 * 795 | 1*21 | 3201
1 edge pixel | 3 * 795 | 1*21 | 2406
1 corner pixel | 2 * 795 | 1*21 | 1611
4 edge pixels | 7 * 795 | 4*21 | 5649
8 edge pixels | 15*795 | 8*21 | 12093

## Slide 20: This proposal
Reduces size of LUT from 2202 to 816 bytes
Uses Qualcomm’s approximation from JVET-J0021 to get rid of division-LUT
Also uses Qualcomm’s non-localized inter filtering (JVET-J0021, JVET-K0384).
Number of pixels filtered in parallel | weight-LUT storage needed | division-LUT storage needed | Total size for LUTs
1 middle pixel | 4 * 795 | 1*21 | 3201
1 edge pixel | 3 * 795 | 1*21 | 2406
1 corner pixel | 2 * 795 | 1*21 | 1611
4 edge pixels | 7 * 795 | 4*21 | 5649
8 edge pixels | 15*795 | 8*21 | 12093

## Slide 21: This proposal
Reduces size of LUT from 2202 to 816 bytes
Uses Qualcomm’s approximation from JVET-J0021 to get rid of division-LUT
Also uses Qualcomm’s non-localized inter filtering (JVET-J0021, JVET-K0384).
Number of pixels filtered in parallel | Previous storage requirements | Proposed storage requirements | Change
1 middle pixel | 9389 | 3201 | -66%
1 edge pixel | 7187 | 2406 | -67%
1 corner pixel | 4985 | 1611 | -68%
4 edge pixels | 17738 | 5649 | -68%
8 edge pixels | 37678 | 12093 | -68%

## Slide 22: Results
VTM BD rates
  -0.33% / -0.81% / -0.59% for AI / RA / LD
VTM decode run times
  104% / 103% / 103% for AI / RA / LD
VTM encode run times
  102% / 108% / 102% for AI / RA / LD -- RA results updated to 104% with reuse of computation
BMS BD rates
  -0.33% / -0.52% / -0.60% for AI / RA / LD
BMS decode run times
  101% / 101% / 101% for AI / RA / LD
Old filter gain over JEM:
  -0.41% / -0.48% / -0.48% for AI / RA / LD

## Slide 23: Gain vs run time (adding to VTM)
better
(a=5)

## Slide 24: Complexity per sample
 | compare | add/sub | abs() | mult | LUT fetch | shift
calc dIR, dIB |  | 2 |  |  |  | 
update LUT argument |  | 10 | 6 | 2 |  | 2
LUT fetch | 2 |  |  |  | 2 | 2
mult w/ dIR, dIB |  |  |  | 2 |  | 
summation of terms |  | 3 |  |  |  | 
final filtering |  | 1 |  |  |  | 1
sum | 2 | 16 | 6 | 4 | 2 | 5

## Slide 25: Complexity per sample
 | compare | add/sub | abs() | mult | LUT fetch | shift
calc dIR, dIB |  | 2 |  |  |  | 
update LUT argument |  | 10 | 6 | 2 |  | 2
LUT fetch | 2 |  |  |  | 2 | 2
mult w/ dIR, dIB |  |  |  | 2 |  | 
summation of terms |  | 3 |  |  |  | 
final filtering |  | 1 |  |  |  | 1
sum | 2 | 16 | 6 | 4 | 2 | 5
can be changed to only shift

## Slide 26: Complexity per sample
 | compare | add/sub | abs() | mult | LUT fetch | shift
calc dIR, dIB |  | 2 |  |  |  | 
update LUT argument |  | 10 | 6 |  |  | 2
LUT fetch | 2 |  |  |  | 2 | 2
mult w/ dIR, dIB |  |  |  | 2 |  | 
summation of terms |  | 3 |  |  |  | 
final filtering |  | 1 |  |  |  | 1
sum | 2 | 16 | 6 | 2 | 2 | 5
4 fixed shifts 1 variable shift of 0..4 steps

## Slide 27: Complexity per sample
 | compare | add/sub | abs() | mult | LUT fetch | shift
calc dIR, dIB |  | 2 |  |  |  | 
update LUT argument |  | 10 | 6 |  |  | 2
LUT fetch | 2 |  |  |  | 2 | 2
mult w/ dIR, dIB |  |  |  | 2 |  | 
summation of terms |  | 3 |  |  |  | 
final filtering |  | 1 |  |  |  | 1
sum | 2 | 16 | 6 | 2 | 2 | 5
4 fixed shifts 1 variable shift of 0..4 steps

## Slide 28: Variant: avoiding filtering for 4x4 intra blocks
We got feedback that hardware implementation would be facilitated if filtering of small intra blocks could be avoided.
Therefore we ran a test avoiding filtering for 4x4 intra blocks.
  VTM results filtering all intra blocks: -0.33% (AI) / -0.81% (RA) / -0.59 % (LD)
  VTM results no filtering for 4x4 intra: -0.31% (AI) / -0.81% (RA) / -0.62% (LD)
  BMS results filtering all intra blocks : -0.33% (AI) / -0.52% (RA) / -0.60% (LD)
  BMS results no filtering for 4x4 intra: -0.31% (AI) / -0.52% (RA) / -0.61% (LD)

## Slide 29: Variant: avoiding filtering for 4x4 intra blocks
We got feedback that hardware implementation would be facilitated if small intra blocks could be avoided.
Therefore we ran a test avoiding filtering for 4x4 intra blocks.
  VTM results filtering all intra blocks: -0.33% (AI) / -0.81% (RA) / -0.59 % (LD)
  VTM results no filtering for 4x4 intra: -0.31% (AI) / -0.81% (RA) / -0.62% (LD)
  VTM results no filtering 4x4, 4x8, 8x4: -0.24% (AI) / -0.76% (RA) / -0.63% (LD)
  BMS results filtering all intra blocks : -0.33% (AI) / -0.52% (RA) / -0.60% (LD)
  BMS results no filtering for 4x4 intra: -0.31% (AI) / -0.52% (RA) / -0.61% (LD)

## Slide 30: Worst cases
I
I
= intra block
= inter block
P
Previous worst case
I
4
4
I
I
I
Avoiding filtering 4x4 intra
I
4
4
I
I
I
New worst case
P
4
4
I
P
= extra latency due to filtering

## Slide 31: Summary
Table size has been greatly reduced
RA gain for VTM is -0.81%
RA gain for BMS is -0.52% (was -0.48% for JEM bilateral filter)
No division or division table.
Late contributions:
  Latency problem ameliorated by avoiding filtering of 4x4 intra blocks
    No change in VTM/BMS gains
  Multiplication in LUT argument calculation can be replaced by >>3

## Slide 32: Proposal
We suggest to adopt JVET-K0274 into VTM.

## Slide 33: Detailed results VTM AI
 | Over VTM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.25% | 0.09% | 0.05% | 97% | 106%
Class A2 | -0.31% | -0.06% | 0.10% | 109% | 105%
Class B | -0.32% | 0.09% | 0.01% | 104% | 103%
Class C | -0.39% | -0.06% | -0.21% | 100% | 104%
Class E | -0.39% | -0.45% | -0.32% | 101% | 104%
Overall | -0.33% | -0.06% | -0.07% | 102% | 104%
Class D | -0.40% | -0.07% | 0.00% | 105% | 102%

## Slide 34: Detailed results VTM RA
 | Random Access over VTM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.55% | -0.16% | -0.20% | 109% | 104%
Class A2 | -0.88% | -0.40% | -0.33% | 108% | 104%
Class B | -1.01% | -0.05% | -0.13% | 109% | 102%
Class C | -0.68% | -0.14% | -0.39% | 106% | 102%
Class E |  |  |  |  | 
Overall | -0.81% | -0.17% | -0.25% | 108% | 103%
Class D | -0.63% | -0.26% | -0.23% | 105% | 101%

## Slide 35: Detailed results VTM LD
 | Low Delay over VTM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.25% | 0.09% | 0.05% | 97% | 106%
Class A2 | -0.31% | -0.06% | 0.10% | 109% | 105%
Class B | -0.32% | 0.09% | 0.01% | 104% | 103%
Class C | -0.39% | -0.06% | -0.21% | 100% | 104%
Class E | -0.39% | -0.45% | -0.32% | 101% | 104%
Overall | -0.33% | -0.06% | -0.07% | 102% | 104%
Class D | -0.40% | -0.07% | 0.00% | 105% | 102%

## Slide 36: Detailed results BMS AI
 | All Intra over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.14% | -0.13% | -0.18% | 103% | 101%
Class A2 | -0.35% | -0.19% | 0.07% | 110% | 101%
Class B | -0.25% | -0.07% | -0.22% | 99% | 101%
Class C | -0.53% | -0.25% | -0.30% | 103% | 102%
Class E | -0.38% | -0.38% | -0.44% | 102% | 101%
Overall | -0.33% | -0.19% | -0.22% | 103% | 101%
Class D | -0.37% | 0.05% | -0.09% | 97% | 102%

## Slide 37: Detailed results BMS RA
 | Random Access over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.24% | -0.10% | -0.12% | 106% | 101%
Class A2 | -0.58% | -0.42% | -0.04% | 106% | 102%
Class B | -0.60% | -0.05% | -0.29% | 106% | 101%
Class C | -0.60% | 0.00% | -0.51% | 101% | 100%
Class E |  |  |  |  | 
Overall | -0.52% | -0.12% | -0.26% | 105% | 101%
Class D | -0.52% | -0.08% | -0.59% | 99% | 100%

## Slide 38: Detailed results BMS LD
 | Low delay over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.47% | 0.38% | 0.98% | 104% | 101%
Class C | -0.69% | 0.50% | 0.48% | 110% | 102%
Class E | -0.70% | -0.28% | -0.19% | 105% | 99%
Overall | -0.60% | 0.26% | 0.52% | 106% | 101%
Class D | -0.73% | 0.39% | -0.08% | 98% | 101%

## Slide 40: Getting the filter weight F0096
sample to be filtered
samples involved in filtering
= absolute difference in intensity

## Slide 41: Getting the filter weight JVET-J0021 / this contribution
sample to be filtered
samples involved in filtering
= absolute difference in intensity
average

## Slide 42: Getting the filter weight JVET-J0021 / this contribution
sample to be filtered
samples involved in filtering
= absolute difference in intensity

## Slide 43: Getting the filter weight JVET-J0021 / this contribution
sample to be filtered
samples involved in filtering
= absolute difference in intensity

## Slide 44: Getting the filter weight this contribution
sample to be filtered
samples involved in filtering
= absolute difference in intensity
should be subtracted
should be added
Instead of calculating one intensity difference, we need to calculate three intensity differences.
Then do one subtraction and one addition, and average.

## Slide 45: Cycle analysis
First cycle:
  Calculate three green absolute differences
  Remove sum of red arrows from previous value

## Slide 46: Cycle analysis
First cycle:
  Calculate three green absolute differences
  Remove sum of red arrows from previous value
Second cycle:
  Add three green arrows to previous value and shift
Third cycle:
  Apply LUT
Fourth cycle:
  Multiply by
Fifth cycle:
  Add to influence value
Sixth cycle:
  Multiply with distance value and shift
Seventh cycle
  Add with to original pixel

## Slide 47: New result with shorter LUTs
During the presentation of JVET-K0274, it was brought to our attention that SIMD-enabled software implementations will struggle with look-up tables (LUTs) larger than 16 bytes.
Therefore, we have reimplemented the filter with 34 LUTs of size 16 (one for each QP).
Since only one qp is used per block, this means only one LUT of size 16 per block, which should be suitable for efficient SIMD execution.
New VTM BD-rate figures are:
  -0.33% / -0.78% for AI / RA (low delay still running)
Compare to:
  -0.33% / -0.81% for AI / RA for JVET-K0274

## Slide 48: Cycle analysis

## Slide 49: Cycle analysis
cycle | operations
1 | Green arrow differences
2 | Black arrow differences and abs() of green arrows
3 | Sums of green arrows and abs() of black arrows
4 | Sums of black arrows
5 | Form 3x3 averages and shift
6 | Apply LUT (16 8-bit values)
7 | Multiply by dI
7+n | Add to influence value
8+n | Multiply by distance value and shift
8+n+m | Add with to original pixel
9+n+m | First column of eight pixels is available
10+n+m | Second column of eight pixels is available
11+n+m | Third column of eight pixels is available
12+n+m | Fourth column of eight pixel is available
13+n+m | Fifth column of eight pixels is available
14+n+m | Sixth column of eight pixels is available
15+n+m | Seventh column of eight pixels is available
16+n+m | All pixels are available

## Slide 50: Cycle analysis 8 parallel edge pixels
cycle | operations
1 | Green arrow differences
2 | Black arrow differences and abs() of green arrows
3 | Sums of green arrows and abs() of black arrows
4 | Sums of black arrows
5 | Form 3x3 averages and shift
6 | Apply LUT (16 8-bit values)
7 | Multiply by dI
7+n | Add to influence value
8+n | Multiply by distance value and shift
8+n+m | Add with to original pixel
9+n+m | First column of eight pixels is available
10+n+m | Second column of eight pixels is available
11+n+m | Third column of eight pixels is available
12+n+m | Fourth column of eight pixel is available
13+n+m | Fifth column of eight pixels is available
14+n+m | Sixth column of eight pixels is available
15+n+m | Seventh column of eight pixels is available
16+n+m | All pixels are available

## Slide 51: Cycle analysis 8 parallel edge pixels
+
+
+
+
+
+
+
+
+
+
cycle | operations
1 | Green arrow differences
2 | Black arrow differences and abs() of green arrows
3 | Sums of green arrows and abs() of black arrows
4 | Sums of black arrows
5 | Form 3x3 averages and shift
6 | Apply LUT (16 8-bit values)
7 | Multiply by dI
7+n | Add to influence value
8+n | Multiply by distance value and shift
8+n+m | Add with to original pixel
9+n+m | First column of eight pixels is available
10+n+m | Second column of eight pixels is available
11+n+m | Third column of eight pixels is available
12+n+m | Fourth column of eight pixel is available
13+n+m | Fifth column of eight pixels is available
14+n+m | Sixth column of eight pixels is available
15+n+m | Seventh column of eight pixels is available
16+n+m | All pixels are available

## Slide 52: Cycle analysis 8 parallel edge pixels
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
cycle | operations
1 | Green arrow differences
2 | Black arrow differences and abs() of green arrows
3 | Sums of green arrows and abs() of black arrows
4 | Sums of black arrows
5 | Form 3x3 averages and shift
6 | Apply LUT (16 8-bit values)
7 | Multiply by dI
7+n | Add to influence value
8+n | Multiply by distance value and shift
8+n+m | Add with to original pixel
9+n+m | First column of eight pixels is available
10+n+m | Second column of eight pixels is available
11+n+m | Third column of eight pixels is available
12+n+m | Fourth column of eight pixel is available
13+n+m | Fifth column of eight pixels is available
14+n+m | Sixth column of eight pixels is available
15+n+m | Seventh column of eight pixels is available
16+n+m | All pixels are available

## Slide 53: Cycle analysis 8 parallel edge pixels
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
cycle | operations
1 | Green arrow differences
2 | Black arrow differences and abs() of green arrows
3 | Sums of green arrows and abs() of black arrows
4 | Sums of black arrows
5 | Form 3x3 averages and shift
6 | Apply LUT (16 8-bit values)
7 | Multiply by dI
7+n | Add to influence value
8+n | Multiply by distance value and shift
8+n+m | Add with to original pixel
9+n+m | First column of eight pixels is available
10+n+m | Second column of eight pixels is available
11+n+m | Third column of eight pixels is available
12+n+m | Fourth column of eight pixel is available
13+n+m | Fifth column of eight pixels is available
14+n+m | Sixth column of eight pixels is available
15+n+m | Seventh column of eight pixels is available
16+n+m | All pixels are available

## Slide 54: Cycle analysis 8 parallel edge pixels
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
LUT
LUT
LUT
LUT
LUT
LUT
LUT
LUT
cycle | operations
1 | Green arrow differences
2 | Black arrow differences and abs() of green arrows
3 | Sums of green arrows and abs() of black arrows
4 | Sums of black arrows
5 | Form 3x3 averages and shift
6 | Apply LUT (16 8-bit values)
7 | Multiply by dI
7+n | Add to influence value
8+n | Multiply by distance value and shift
8+n+m | Add with to original pixel
9+n+m | First column of eight pixels is available
10+n+m | Second column of eight pixels is available
11+n+m | Third column of eight pixels is available
12+n+m | Fourth column of eight pixel is available
13+n+m | Fifth column of eight pixels is available
14+n+m | Sixth column of eight pixels is available
15+n+m | Seventh column of eight pixels is available
16+n+m | All pixels are available

## Slide 55
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
LUT
LUT
LUT
LUT
LUT
LUT
LUT
LUT
cycle | operations
1 | Green arrow differences
2 | Black arrow differences and abs() of green arrows
3 | Sums of green arrows and abs() of black arrows
4 | Sums of black arrows
5 | Form 3x3 averages and shift
6 | Apply LUT (16 8-bit values)
7 | Multiply by dI
7+n | Add to influence value
8+n | Multiply by distance value and shift
8+n+m | Add with to original pixel
9+n+m | First column of eight pixels is available
10+n+m | Second column of eight pixels is available
11+n+m | Third column of eight pixels is available
12+n+m | Fourth column of eight pixel is available
13+n+m | Fifth column of eight pixels is available
14+n+m | Sixth column of eight pixels is available
15+n+m | Seventh column of eight pixels is available
16+n+m | All pixels are available