## Slide 1: Non-CE9: DMVR without Intermediate Buffers and with Padding
Semih Esenlik
Ivan Krasnov, Zhijie Zhao, Jianle Chen

## Slide 2: Problems with DMVR in BMS
Intermediate interpolation requires additional buffers
DMVR in BMS increases memory BW
Prediction 0 by interpolation
Prediction 1 by interpolation
Buffer0
Buffer1
Perform SAD search
Re-do interpolation
Weighted Average
DMVR according to BMS
Memory BW increase is proportional to Search Range
CU height
CU width
Problem addressed by proposal

## Slide 3: Proposed solution
The initial MV and the candidate MVs are all rounded to nearest integer before SAD search. Inverse rounding is applied to selected MV candidate.
  No interpolation filtering is necessary before SAD search
Padding is applied before final interpolation filtering
  Memory BW is same as regular MC.

## Slide 4: Proposed DMVR design
Step 1
Initial motion vector
Step 2
All candidate points are rounded to nearest integer
Apply bilateral matching on integer coordinates
Step 3
Revert the application of rounding
Step 4
Final refined MV
Best matching integer point
Use padded samples for DCTIF MC
Final MV – Initial MV = [1pixel, 0]
Step 5
Horizontal interpolation
Final MC using refined MV

## Slide 5: Test conditions
The proposed solution is implemented on top of CE9.2.9.
  Bilateral Matching with MV difference mirroring
  Search Range is 2 pixels
  Half-pel on
  Number of maximum MRSAD search = 13

## Slide 6: Experimental Results
Experimental results of proposal
Implemented on top of CE9.2.9 (SR=2, half-pel on)
Experimental results of proposal
Implemented on top of CE9.2.9 (SR=2, half-pel on, spatial MV prediction from refined MV is disabled)
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -2.63% | -2.09% | -2.34% | 106% | 122% | 0.07% | 0.02% | 0.05% | 100% | 101%
Class A2 | -4.09% | -3.90% | -3.95% | 106% | 130% | 0.09% | 0.10% | 0.13% | 100% | 101%
Class B | -2.07% | -1.99% | -1.95% | 109% | 128% | -0.09% | -0.11% | -0.06% | 100% | 101%
Class C | -1.48% | -1.73% | -1.80% | 110% | 129% | -0.07% | 0.00% | 0.01% | 100% | 101%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | -2.43% | -2.32% | -2.39% | 108% | 128% | -0.01% | -0.01% | 0.02% | 100% | 101%
Class D | -1.62% | -1.79% | -1.86% | 113% | 130% | -0.15% | -0.13% | -0.13% | 100% | 100%

## Slide 7: Supplementary results (results of CE9.2.9)
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -4.76% | -3.60% | -4.07% | 106% | 125% | -1.23% | -0.84% | -1.11% | 99% | 102%
Class A2 | -7.82% | -6.94% | -7.10% | 105% | 136% | -1.95% | -1.51% | -1.66% | 98% | 101%
Class B | -4.06% | -3.35% | -3.48% | 108% | 132% | -1.20% | -0.99% | -0.99% | 99% | 100%
Class C | -2.69% | -2.78% | -2.81% | 109% | 133% | -0.93% | -0.82% | -0.81% | 98% | 100%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | -4.59% | -3.97% | -4.14% | 107% | 132% | -1.29% | -1.02% | -1.10% | 98% | 101%
Class D | -3.00% | -2.85% | -3.13% | 112% | 134% | -1.28% | -0.99% | -0.99% | 99% | 100%
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -2.74% | -2.16% | -2.44% | 108% | 126% | -0.03% | -0.08% | -0.07% | 100% | 102%
Class A2 | -4.60% | -4.23% | -4.32% | 108% | 134% | -0.23% | -0.14% | -0.16% | 100% | 101%
Class B | -2.50% | -2.27% | -2.26% | 110% | 133% | -0.40% | -0.34% | -0.27% | 100% | 101%
Class C | -1.88% | -1.99% | -1.97% | 111% | 134% | -0.43% | -0.27% | -0.24% | 100% | 102%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | -2.80% | -2.57% | -2.63% | 109% | 132% | -0.30% | -0.23% | -0.20% | 100% | 102%
Class D | -2.23% | -2.14% | -2.28% | 114% | 136% | -0.78% | -0.61% | -0.61% | 100% | 102%
Coding gain of CE9.2.9 (SR=2, half-pel on)
Coding gain of CE9.2.9 (SR=2, half-pel on, spatial MV prediction from refined MV is disabled)

## Slide 8: Conclusion
2 important issues related to decoder side MV refinement techniques are addressed.
  Extra interpolation before SAD search and associated buffers
  Memory bandwidth increase
Proposed to be included in VVC.

## Slide 9
Thank You
www.huawei.com