## Slide 1: JVET-K0281
Inter-Component Context Modelling for Coded Block Flag

## Slide 2: Proposal
Coded Block Flag (CBF) for Cr Component (included in JVET-K0071, CE7-1.2)
Two probability models for Cr-Cbf
Probability model used is determined by value of Cb-Cbf
  ctxIdCr = coded_block_flag[ Cb ]
Extension to Coded Block Flag of Cb Component
Only for intra-coded CUs
Modification of coding order for CBFs: Y, Cb, Cr
Two probability models for Cb-Cbf
Probability model used is determined by value of Y-Cbf
  ctxIdCb = coded_block_flag[ Y ]

## Slide 3: Simulation Results (VTM configuration)

## Slide 4: Simulation Results (BMS configuration)

## Slide 5: Summary
Context Modelling for Chroma Coded Block Flags
Use Cb-CBF for determining context for Cr-CBF
  for all blocks
Use Y-CBF for determining context for Cb-CBF
  only for intra-coded blocks
  modified coding order: Y, Cb, Cr
Average results relative to VTM:
  AI: −0.25%, RA: −0.15%