## Slide 1: CE1-2.0.11: Picture Boundary Handling
Han Gao
Semih Esenlik, Zhijie Zhao, Anand Meher Kotra, Jianle Chen

## Slide 2: Motivation
Why the picture boundary partition is necessary?
State-of-the-art in VVC, inherited from HEVC  Forced QT
Incomplete CTU on boundary
No non transform unit

## Slide 3: Picture Boundary Handling (CE1-2.0.11)
Using exactly same partition syntax of the normal block (non-boundary) (for instance, VTM-1.0 like Fig. 1) for boundary located block, the syntax need to be unchanged.
If the no split mode is parsed for the boundary CU, used forced boundary partition (FBP) to match the picture boundary.
After forced boundary partition (non-singling boundary partition), no further partition.
0
0
0
0
0
1
1
1
1
1
QT
No split/FBP
Horizontal
Vertical
HTT
HBT
VTT
VBT

## Slide 4: Picture Boundary Handling (CE1-2.0.11)
The FBP could use any kind of forced partition (forced QT, forced BT …)
In CE1-2.0.11 proposal we used forced QTBT as FBP method with following rules
  If isBoundary && BlockSize > MaxBtSize  forced QT
  Else if, isBottomBoundary  forced HBT
  Else if, isRightBoundary  forced VBT
  Else if isCornerCase  forced QT
BottomBoundary
RightBoundary
CornerCase

## Slide 5: Picture Boundary Handling (CE1-2.0.11)
In the alternative solution of JVET-K0287, only forced BT is used for FBP with following rules
  If, isBottomBoundary  forced HBT
  Else if, isRightBoundary  forced VBT
BottomBoundary
RightBoundary

## Slide 6: Experiment results
Anchor: BMS 1.0
Anchor: VTM 1.0

## Slide 7: Supplementary results
Anchor: BMS 1.0
Anchor: VTM 1.0

## Slide 8: Conclusion
The picture boundary handling without syntax change is proposed.
Proposed to included in VVC