## Slide 1: CE4-related: ranking based spatial merge candidate list for inter prediction (JVET-K0304)
G. Li, X. Xu, X. Li, S. Liu
2018/07

## Slide 2: Introduction
A ranking based method is proposed to replace the spatial merge candidate ordering in the candidate list
The positions of merge candidates are extended
Keeping maximum number of merge candidates unchanged
BD-rate improvement observed against VTM

## Slide 3: Spatial Candidates in VTM
Currently 5 Positions of spatial merge candidates
  A0: Left-bottom candidate
  A1: Left candidate
  B0: Above-right candidate
  B1: Above candidate
  B2: Above-left candidate
The order of spatial positions in the list
  {A1, B1, B0, A0, B2}

## Slide 4: Range of Spatial Neighbors
All spatial neighbors are checked in a defined range
  M sub-blocks on the left side, M = 2 * Block_Height / 4;
  N sub-blocks on the above side, N = 2 * Block_Width / 4;
  Top-Left neighbor included

## Slide 5: Merge List Construction
Scan all spatial neighbors in range
Collect counts of each available motion information
Build a sorted list of motion info. based on counts
Fill candidate list from top of sorted list
  Highest occurrence first
If candidate list is not full, use non-spatial candidates to fill in original order
  TMVP, Combined Bi-Dir, Zero MVs

## Slide 6: Simulation results
 | Random Access Main 10 |  |  |  | 
 | Over VTM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.25% | -0.17% | -0.26% | 96% | 106%
Class A2 | -0.12% | -0.13% | -0.08% | 96% | 107%
Class B | -0.26% | -0.19% | -0.15% | 97% | 105%
Class C | -0.26% | -0.33% | -0.22% | 97% | 105%
Class E |  |  |  |  | 
Overall | -0.23% | -0.21% | -0.18% | 97% | 106%
Class D | -0.13% | 0.04% | -0.02% | 97% | 104%
Class F (optional) | -0.03% | -0.01% | -0.02% | 97% | 104%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.27% | -0.16% | -0.06% | 98% | 112%
Class C | -0.16% | -0.18% | -0.08% | 97% | 101%
Class E | -0.85% | -0.81% | -0.84% | 97% | 105%
Overall | -0.38% | -0.33% | -0.26% | 98% | 106%
Class D | -0.15% | 0.00% | -0.18% | 97% | 109%
Class F (optional) | -0.22% | -0.13% | -0.10% | 96% | 102%
Low delay P Main10 |  |  |  | 
Over VTM-1.0 |  |  |  | 
Y | U | V | EncT | DecT
-0.39% | -0.17% | -0.26% | 100% | 111%
-0.34% | -0.37% | -0.51% | 96% | 107%
-0.95% | -1.05% | -0.53% | 91% | 106%
-0.51% | -0.46% | -0.41% | 97% | 108%
-0.37% | -0.53% | -0.06% | 94% | 101%
-0.19% | -0.24% | 0.32% | 97% | 107%

## Slide 7: Conclusion
A ranking based merge candidate list ordering is proposed
With proposed method in VTM, there are 0.23%, 0.38%, and 0.51% BD-rate improvement for Random Access, Low Delay B, and Low Delay P, respectively.
It is proposed to include it into a core experiment for further evaluation.