## Slide 1: JVET-K0312: AHG13: Reporting of adjusted decoder runtimes in tool on/off tests
Jill Boyce, Dmitry Gurulev, Vasily Aristarkhov (Intel)
Alexis Tourapis (Apple)

## Slide 2: Introduction
Propose additional reporting in future “tool on” / “tool off” tests in AHG13
  Count how often a tool is used, per block size
    Used to calculate % of directly impacted pixels
  Calculate and report adjusted decoder runtime ratio (in addition to DecT)
BMS-1 software decoder patch provided for two example tools: Affine and NSST
  Simple instrumentation in decoder to count how often tool is used, by block size
  Similar software changes would be needed for each tested tool
Reporting template provided, with example data for Affine tool

## Slide 3: Background and Motivation
In current tool reporting templates, encoder and decoder runtimes are reported as
  Absolute times
  Ratios between “Reference” and “Tested” times
Decoder software runtimes are easy to measure and report, but are an incomplete representation of decoder complexity
If a tool is only very rarely used in a bitstream, “tool on” experiment runtimes are not representative of the worst case complexity that could be required if the tool was maximally used
  For example, if DecT is 110% but a tool is only used 5% of the time, worst case decoder runtime would be considerably worse

## Slide 4: Calculations
% of impacted pixels (PercentageOfImpactedPixels) calculated by counting the CUs or TUs for which a tool is enabled, and multiplying by the number of luma samples in the CU or TU, and accumulating for the entire sequence.
The adjusted decoder runtime ratio, AdjDecT, calculated using original decoder runtime ratio (DecT) and PercentageOfImpactedPixels:
AdjDecT = (DecT - 1) / PercentageOfImpactedPixels + 1
The adjusted decoder runtime ratio is not claimed to be an accurate representation of the increase in decoder complexity given the introduction of a particular tool, but may provide some useful additional information

## Slide 5: Example reporting: Affine, NSST for Affine “tool on” test
M_FRAME: 500 pixels:49920000
M_AFFINE: 16454
M_AFFINE_128x128: 34 pixels: 557056
M_AFFINE_128x16 : 6 pixels: 12288
M_AFFINE_128x32 : 8 pixels: 32768
M_AFFINE_128x4 : 1 pixels: 512
M_AFFINE_128x64 : 8 pixels: 65536
M_AFFINE_128x8 : 3 pixels: 3072
M_AFFINE_16x128 : 10 pixels: 20480
M_AFFINE_16x16 : 4877 pixels: 1248512
M_AFFINE_16x32 : 1606 pixels: 822272
M_AFFINE_16x4 : 296 pixels: 18944
M_AFFINE_16x64 : 335 pixels: 343040
M_AFFINE_16x8 : 555 pixels: 71040
M_AFFINE_32x128 : 23 pixels: 94208
M_AFFINE_32x16 : 823 pixels: 421376
M_AFFINE_32x32 : 2726 pixels: 2791424
M_AFFINE_32x4 : 84 pixels: 10752
M_AFFINE_32x64 : 362 pixels: 741376
M_AFFINE_32x8 : 249 pixels: 63744
M_AFFINE_4x128 : 2 pixels: 1024
M_AFFINE_4x16 : 629 pixels: 40256
M_AFFINE_4x32 : 337 pixels: 43136
M_AFFINE_4x64 : 72 pixels: 18432
M_AFFINE_64x128 : 19 pixels: 155648
M_AFFINE_64x16 : 109 pixels: 111616
M_AFFINE_64x32 : 182 pixels: 372736
M_AFFINE_64x4 : 11 pixels: 2816
M_AFFINE_64x64 : 455 pixels: 1863680
M_AFFINE_64x8 : 27 pixels: 13824
M_AFFINE_8x128 : 2 pixels: 2048
M_AFFINE_8x16 : 981 pixels: 125568
M_AFFINE_8x32 : 798 pixels: 204288
M_AFFINE_8x64 : 98 pixels: 50176
M_AFFINE_8x8 : 726 pixels: 46464
Total impacted pixels % impacted pixels
10370112 20.77%
M_NSST: 0
Total impacted pixels % impacted pixels
0 0.00%

## Slide 6: Example: Affine tool for BMS-1 from AHG13 bitstreams
 | Random Access Main 10 |  |  |  |  |  | Random Access Main10 | 
 | Over VTM |  |  |  |  |  | Over VTM | 
 | Y | U | V | EncT | DecT |  | Impacted Pixels | Adj DecT
Class A1 | -1.97% | -1.58% | -1.65% | 134% | 107% |  | 6% | 189%
Class A2 | -5.87% | -4.74% | -4.46% | 138% | 119% |  | 18% | 199%
Class B | -3.26% | -2.16% | -2.34% | 139% | 112% |  | 9% | 195%
Class C | -1.27% | -0.76% | -0.80% | 137% | 111% |  | 8% | 226%
Class E |  |  |  |  |  |  |  | 
Overall | -2.99% | -2.19% | -2.21% | 137% | 112% |  | 9% | 202%
Class D | -1.79% | -1.02% | -1.21% | 137% | 111% |  | 8% | 210%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! |  | #NUM! | #DIV/0!
 | Low delay B Main10 |  |  |  |  |  | Low delay B Main10 | 
 | Over VTM |  |  |  |  |  | Over VTM | 
 | Y | U | V | EncT | DecT |  | Impacted Pixels | Adj DecT
Class A1 |  |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  |  | 
Class B | -2.49% | -1.48% | -1.77% | 164% | 109% |  | 12% | 151%
Class C | -1.44% | -0.77% | -0.60% | 148% | 106% |  | 11% | 134%
Class E | -2.18% | -1.84% | -2.32% | 204% | 108% |  | 14% | 151%
Overall | -2.06% | -1.33% | -1.52% | 168% | 108% |  | 10% | 154%
Class D | -2.94% | -1.97% | -2.28% | 141% | 110% |  | 14% | 151%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! |  | #NUM! | #DIV/0!

## Slide 7: Recommendation
Add counting instrumentation to VTM, BMS
Ask proponents to include counting functionality in software when tools are adopted to VTM or BMS
In AHG13 Tests:
  Report % of Impacted Pixels and Adjusted DecT in future AHG13 tests
  Provide log files with breakdown of counts per block size

## Slide 8: Future Improvements
Add support for counting the basic prediction types included in the VTM by CU size as well as reporting the collected information per picture
Reformat the output log reporting