## Slide 1: CE2: Tests on long deblocking (CE2.2.1.4)
D. Rusanovskyy, J. Dong, M. Karczewicz
JVET-K0334

## Slide 2: Tested method:
Deblocking Filter Characteristics:
  Long deblocking (LDB) for large block boundaries (>16)
  Strong HEVC deblocking for block boundaries (<16)
  Filtered: 4 samples on each side
  LDB is 11 tap filter:
  Filter support area for long filtering of P and Q blocks :
P
QL
Qs
Number of taps per line: 70
Coefficient, power of 2: 28
Line buffers: 6
Smallest sizes: 8x16, 16x8
 |  | Input P |  |  |  |  |  |  |  |  | Input Q |  |  |  |  |  |  |  | 
output |  | p8 | p7 | p6 | p5 | p4 | p3 | p2 | p1 | p0 | q0 | q1 | q2 | q3 | q4 | q5 | q6 | q7 | q8
output Q | q3 |  |  |  |  |  |  |  | -3 | 16 | -3 | 1 | 5 | 16 | 18 | 14 | 0 | 0 | 0
 | q2 |  |  |  |  |  |  | -1 | 4 | 12 | -3 | 6 | 14 | 14 | 16 | 2 | 0 | 0 | 
 | q3 |  |  |  |  |  | -1 | 6 | 7 | 8 | -2 | 13 | 15 | 10 | 8 | 0 | 0 |  | 
 | q0 |  |  |  |  | 0 | 2 | 9 | 12 | 1 | 3 | 13 | 16 | 5 | 3 | 0 |  |  | 
OutputP | p0 |  |  |  | 0 | 3 | 5 | 16 | 13 | 3 | 1 | 12 | 9 | 2 | 0 |  |  |  | 
 | p1 |  |  | 0 | 0 | 8 | 10 | 15 | 13 | -2 | 8 | 7 | 6 | -1 |  |  |  |  | 
 | p2 |  | 0 | 0 | 2 | 16 | 14 | 14 | 6 | -3 | 12 | 4 | -1 |  |  |  |  |  | 
 | p3 | 0 | 0 | 0 | 14 | 18 | 16 | 5 | 1 | -3 | 16 | -3 |  |  |  |  |  |  | 
LDB
SDB

## Slide 3: Tested method:
Characteristics of decision making:
  HEVC identifies boundary for strong filtering
  Additional LDB smoothness estimate is derived for P and Q
    Laplacian kernel to estimate local activity:
    Smooth criteria is estimated by aggregating local activities
  LDB is applied if following criteria met:
  LDB is applied if above criteria met and block is >16
P
QL
Qs
Decision frequency : 4 line
Smoothness criteria: 45 taps
Properties: Independent for P and Q

## Slide 4: Simulation results: VTM configuration
Initial software made available on 1st of June, final release on June 19th 2018
Comparative performance of CE2.2.1.4 vs. CTC VTM Anchor
Execution time estimates (Decoder estimates produced on stand along PC ):

## Slide 5: Simulation results: BMS configuration
Initial software made available on 1st of June, final release on June 19th 2018
Comparative performance of CE2.2.1.4 vs. CTC BMS Anchor
Execution time estimates (Estimates produced on heterogenous cluster **):
 | All Intra |  |  | Random Access |  |  | Low Delay B |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A1 | 0.07% | 0.16% | 0.04% | -0.14% | -0.68% | -1.21% |  |  | 
Class A2 | 0.06% | 0.04% | 0.03% | 0.02% | -0.30% | -0.43% |  |  | 
Class B | 0.05% | 0.00% | 0.00% | 0.00% | -0.31% | -0.42% | -0.01% | -0.99% | -0.43%
Class C | 0.02% | 0.00% | 0.00% | 0.02% | -0.18% | -0.17% | -0.04% | -0.32% | -0.20%
Class E | -0.02% | -0.01% | -0.03% |  |  |  | -0.19% | -0.99% | -1.41%
Overall | 0.04% | 0.03% | 0.01% | -0.02% | -0.34% | -0.51% | -0.07% | -0.76% | -0.60%
Class D | 0.02% | -0.01% | 0.00% | 0.06% | -0.13% | -0.03% | -0.05% | -0.07% | -0.57%
 | EncT | DecT | EncT | DecT | EncT | DecT
Class A1 | 104% | 97% | 102% | 94% |  | 
Class A2 | 102% | 94% | 102% | 94% |  | 
Class B | 103% | 96% | 103% | 97% | 102% | 94%
Class C | 125% | 118% | 127% | 120% | 128% | 122%
Class E | 125% | 116% |  |  | 130% | 127%
Overall | 111% | 103% | 109% | 101% | 117% | 111%
Class D | 125% | 120% | 127% | 120% | 128% | 126%

## Slide 6: Simulation results: Discussion
All Intra results:
  QP seems to be low for sever blocking artifacts
Random Access (VTM):
  Sufficiently high QP for deblocking take effect
  UHD sequences show largest gain, up-to 0.56% for FM4
VTM | delta BD rate, % |  | 
RA | Y | U | B
Tango2 | -0.36 | -1.69 | -2.19
FoodMarket4 | -0.56 | -1.10 | -1.32
Campfire | -0.11 | -0.01 | -0.44
CatRobot1 | -0.07 | -0.68 | -0.59
DaylightRoad2 | -0.18 | -0.38 | -0.38
ParkRunning3 | 0.08 | -0.05 | -0.08
MarketPlace | 0.07 | -0.10 | -0.36
RitualDance | -0.08 | -0.49 | -0.36
Cactus | -0.01 | -0.29 | -0.11
BasketballDrive | -0.05 | -0.56 | -0.53
BQTerrace | 0.01 | 0.06 | 0.20
BasketballDrill | -0.03 | -0.27 | -0.13
BQMall | -0.01 | 0.00 | -0.23
PartyScene | -0.01 | -0.13 | 0.02
RaceHorses | -0.08 | -0.13 | -0.15
BasketballPass | -0.02 | 0.11 | -0.07
BQSquare | 0.01 | -0.16 | 0.00
BlowingBubbles | -0.01 | 0.17 | -0.10
RaceHorses | -0.02 | 0.07 | -0.34

## Slide 7: Summary and Conclusion
Long deblocking test in CE2.2.1.4
  Strong HEVC deblocking is replaced by long deblocking for blocks >16
  HEVC deblocking is applied to the rest
  Proposed deblocking filter
    6 lines buffer
    70 taps per filtered line (worst case)
    Smallest affected sizes: 8x16 and 16x8
  Proposed decision making:
    Independent for P and Q
    Frequency: every 4 lines
    Smoothness criteria: 45 taps
Results:
  VTM delta bdRate Y: 0.01%/-0.09%/0.02% for AI/RA/LB
    -0.34% for UHD1, RA
  BMS delta bdRate Y: 0.04%/-0.02%/-0.07% for AI/RA/LB
    -0.14% for UHD1, RA
  VTM decoding time estimate : ~104%-106%
  Visual improvement

## Slide 8: Summary and Conclusion
Proposals and suggestions:
  Continue CE on long deblocking filtering
  Sub-CEs on deblocking and decision making processes
Technical proposals and suggestions:
  Consider increase QPs for study
  Visual improvement assessment
  Include HDR sequences in study/viewing
  Decoding time complexity to be assessed on single PC as average of several decoding passes