## Slide 1: CE3: Intra mode signaling with priority based MPM and non-MPM list construction (Test 3.2.2)
Anand Meher Kotra, Zhijie Zhao, Jianle Chen

## Slide 2: Prior art: Intra mode signaling in BMS 1.0
Fig. 1 Neighbor Intra Modes used in MPM list construction
Current Coding Unit
67 Intra modes are coded as one of the following:
  MPM list (Size: 6)
    Five Spatial Neighbors Intra modes used
    Order of insertion is
      Left (L), Above (A), Planar Mode, DC mode, Below Left (BL), Above Right (AR), Above Left (AL),
    Derived Angular modes
    Default Modes
  Selected Modes (Size: 16)
    Fixed subsampling of remaining 61 Intra modes
  Remaining 45 Intra modes are coded as Non Selected Modes

## Slide 3: Prior art: Signaling of Intra mode in BMS-1.0
Intra prediction modes | MPM flag | Selected flag | Bin string
MPM modes (6) | 1 |  | 0
 |  |  | 10
 |  |  | 110
 |  |  | 1110
 |  |  | 11110
 |  |  | 11111
Selected modes (16) | 0 | 1 | 4 bits fixed length code
Non-selected modes (45) | 0 | 0 | Truncated binary code

## Slide 4: Main changes proposed for MPM list
MPM list changes
  Second Tier neighbors (non adjacent) neighbors intra modes are also included in the MPM list
    To not increase line buffer, only second tier neighbors which belong to the same CTU as current coding unit are considered
  DC mode is included after including Second Tier Neighbors
  For the default list which is used to complete the MPM list,
    DIA (diagonal) mode is replaced using VDIA (vertical diagonal) mode
Current Coding Unit
L
BL
AL
AR
A
L
A
L
A
A
Second Tier Neighbors
L
Second Tier
Neighbors
L

## Slide 5: Main changes proposed for non-MPM list
Selected Modes
  Are filled using offsets to the first two angular modes from the MPM list
Non-Selected Modes
  Since truncated binarization is used for signaling:
    First 19 modes use 5 bits for signaling
    Rest use 6 bits for signaling
  First 19 modes in Non-Selected Modes category are derived as follows:
    First 14 modes are filled using offsets to the first two angular modes from the MPM list
    Remaining 5 modes are filled from a default list which is ordered based on the intra mode probability occurrence

## Slide 6: Experimental Results
Simulations results w.r.t. to anchors VTM and BMS
(*For VTM simulations, Intra65Ang is set to 1)

## Slide 7: Supplementary Results
Result of inserting Second Tier Neighbors before DC mode
 | All Intra Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.88% | -0.72% | -0.70% | 111% | 104% | -0.11% | 0.07% | 0.02% | 101% | 102%
Class A2 | -1.20% | -1.19% | -1.22% | 111% | 103% | -0.09% | -0.02% | -0.11% | 101% | 102%
Class B | -1.48% | -1.36% | -1.33% | 111% | 103% | -0.09% | 0.06% | 0.09% | 101% | 102%
Class C | -1.10% | -0.84% | -0.89% | 112% | 107% | -0.09% | 0.10% | 0.19% | 101% | 102%
Class E | -1.89% | -2.07% | -1.78% | 111% | 105% | -0.12% | 0.11% | 0.11% | 101% | 101%
Overall | -1.32% | -1.23% | -1.19% | 111% | 104% | -0.10% | 0.07% | 0.07% | 101% | 102%
Class D | -0.39% | -0.19% | -0.18% | 112% | 106% | -0.03% | 0.16% | 0.08% | 101% | 101%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.51% | -0.35% | -0.35% | 102% | 101% | -0.03% | 0.03% | 0.10% | 99% | 101%
Class A2 | -0.73% | -0.43% | -0.46% | 101% | 101% | -0.02% | 0.00% | -0.03% | 100% | 101%
Class B | -0.72% | -0.38% | -0.31% | 102% | 100% | -0.05% | 0.10% | 0.14% | 100% | 101%
Class C | -0.46% | -0.19% | -0.33% | 102% | 102% | 0.00% | 0.22% | -0.05% | 100% | 100%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | -0.61% | -0.33% | -0.36% | 102% | 101% | -0.03% | 0.10% | 0.04% | 100% | 101%
Class D | -0.20% | -0.06% | -0.18% | 102% | 101% | 0.01% | 0.15% | -0.08% | 100% | 100%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!

## Slide 8: Supplementary Results
Result of only moving DC mode after “Bottom Left (BL)”
 | All Intra Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.82% | -0.81% | -0.72% | 109% | 102% | -0.04% | 0.00% | -0.04% | 99% | 101%
Class A2 | -1.14% | -1.19% | -1.19% | 109% | 101% | -0.03% | 0.05% | -0.06% | 99% | 101%
Class B | -1.43% | -1.34% | -1.36% | 109% | 102% | -0.04% | 0.07% | 0.01% | 100% | 101%
Class C | -1.05% | -0.83% | -1.02% | 110% | 105% | -0.04% | 0.05% | 0.06% | 100% | 100%
Class E | -1.87% | -2.06% | -1.87% | 109% | 103% | -0.07% | 0.03% | -0.05% | 99% | 100%
Overall | -1.27% | -1.23% | -1.23% | 109% | 103% | -0.04% | 0.04% | -0.01% | 100% | 101%
Class D | -0.37% | -0.23% | -0.39% | 110% | 106% | -0.01% | 0.18% | 0.10% | 100% | 100%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.47% | -0.45% | -0.33% | 101% | 101% | 0.01% | 0.06% | -0.04% | 99% | 101%
Class A2 | -0.71% | -0.59% | -0.47% | 101% | 100% | 0.01% | 0.17% | 0.09% | 99% | 101%
Class B | -0.67% | -0.34% | -0.56% | 101% | 100% | -0.02% | 0.04% | -0.06% | 99% | 100%
Class C | -0.44% | -0.28% | -0.37% | 102% | 101% | 0.03% | 0.15% | -0.33% | 99% | 100%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | -0.58% | -0.40% | -0.44% | 101% | 101% | 0.01% | 0.10% | -0.10% | 99% | 100%
Class D | -0.14% | 0.05% | 0.05% | 101% | 100% | 0.01% | 0.09% | -0.12% | 100% | 100%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!

## Slide 9: Supplementary Results
Results for only Selected and Non-selected modes derivation on top of BMS-1.0
 | All Intra Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | -0.18% | -0.05% | -0.05% | 101% | 101%
Class A2 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | -0.10% | -0.05% | -0.09% | 101% | 101%
Class B | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | -0.12% | 0.05% | 0.10% | 101% | 101%
Class C | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | -0.18% | -0.03% | 0.02% | 101% | 101%
Class E | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | -0.31% | -0.20% | -0.17% | 101% | 100%
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | -0.17% | -0.04% | -0.02% | 101% | 101%
Class D | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | -0.15% | 0.09% | -0.02% | 102% | 101%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | -0.08% | 0.09% | 0.03% | 99% | 101%
Class A2 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | -0.05% | 0.00% | 0.07% | 99% | 100%
Class B | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | -0.07% | 0.05% | -0.01% | 99% | 100%
Class C | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | -0.07% | 0.08% | -0.23% | 99% | 100%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | -0.07% | 0.05% | -0.05% | 99% | 100%
Class D | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | -0.03% | -0.28% | -0.22% | 100% | 101%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!

## Slide 10: Supplementary Results
Anchor : VTM + Intra65Ang:1
Test : Anchor + Intra mode coding changes
 | All Intra Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.27% | -0.01% | -0.07% | 99% | 103% | -0.28% | -0.05% | -0.13% | 102% | 102%
Class A2 | -0.19% | -0.07% | -0.07% | 98% | 103% | -0.20% | -0.10% | -0.16% | 102% | 102%
Class B | -0.20% | 0.02% | 0.09% | 99% | 102% | -0.21% | 0.01% | 0.04% | 103% | 102%
Class C | -0.20% | 0.00% | 0.05% | 98% | 100% | -0.23% | 0.00% | 0.07% | 102% | 101%
Class E | -0.35% | -0.11% | 0.01% | 98% | 101% | -0.38% | -0.01% | -0.03% | 102% | 101%
Overall | -0.23% | -0.03% | 0.01% | 98% | 102% | -0.25% | -0.03% | -0.03% | 102% | 102%
Class D | -0.18% | 0.06% | 0.05% | 99% | 101% | -0.19% | 0.16% | 0.19% | 103% | 100%
Class F (optional) | -0.28% | -0.14% | -0.21% | 98% | 100% | -0.25% | -0.12% | -0.23% | 102% | 101%
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.14% | 0.06% | 0.04% | 100% | 101% | -0.11% | 0.07% | 0.07% | 101% | 101%
Class A2 | -0.09% | 0.03% | -0.01% | 100% | 101% | -0.08% | 0.07% | 0.10% | 101% | 101%
Class B | -0.09% | 0.06% | 0.24% | 99% | 100% | -0.14% | 0.17% | 0.08% | 100% | 100%
Class C | -0.11% | 0.12% | 0.09% | 99% | 99% | -0.10% | 0.20% | -0.10% | 100% | 99%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | -0.11% | 0.07% | 0.11% | 99% | 100% | -0.11% | 0.14% | 0.04% | 100% | 100%
Class D | -0.06% | 0.17% | 0.02% | 99% | 100% | -0.04% | 0.15% | -0.09% | 101% | 98%
Class F (optional) | -0.22% | -0.08% | -0.23% | 99% | 99% | -0.15% | -0.14% | 0.08% | 100% | 99%

## Slide 11: Summary & Conclusion
Two changes are proposed for Intra mode signaling
  MPM list changes
    Second Tier Neighbors are inserted after “Bottom Left” mode.
    DC mode is inserted after Second Tier Neighbors
    DIA mode is replaced with VDIA in the default list of MPM list construction.
  Non-MPM list changes
    Selected and Non selected modes are derived by adding offsets to the first two angular modes from MPM list.
We suggest to adopt the proposed changes for Intra mode signaling

## Slide 12
Thank You
www.huawei.com