## Slide 1: CE2-related: Longer tap Deblocking Filter JVET-K0369
Anand Meher Kotra, Biao Wang, Semih Esenlik, Zhijie Zhao, Jianle Chen

## Slide 2: Blocking artifacts in VTM/BMS 1.0
POC 3 of FoodMarket QP 37
POC 10 of FoodMarket QP 37

## Slide 3: Several longer tap filters being studied in CE2
Test# | Description | Document#
2.2.1.1.a | Long deblocking filters and fixes (only luma) | JVET-K0307
2.2.1.1.b | Long deblocking filters and fixes (only fixes for luma) | JVET-K0307
2.2.1.2 | Extended Deblocking Filter (only luma) | JVET-K0393
2.2.1.3 | Long deblocking filters (only luma) | JVET-K0232
2.2.1.4 | Tests on long deblocking (only long for luma also filtering chroma when long filters are used for luma) | JVET-K0334
2.2.1.5 | Long-tap deblocking filter (only luma) | JVET-K0112
2.2.1.6.a | Long-tap deblocking filter for luma | JVET-K0152
2.2.1.6.b | Long-tap deblocking filter for chroma | JVET-K0152
2.2.1.6.c | Long-tap deblocking filter for luma and chroma | JVET-K0152
2.2.1.7 | Deblocking Improvements for Large CUs both luma and chroma | JVET-K0315

## Slide 4: Aspects of our proposal
Filtering of implicit TU boundaries
  Problem in VTM/BMS deblocking
    Largest transform size is greater than CU size
    VTM/BMS only filters CU boundaries but not TU boundaries
  Fix: Also filter implicit TU boundaries
    Same solution as in JVET-K0307
  Several other CE and CE-related proposals addressed same problem
Parallel deblocking for different CUs
  Avoid overlaps
  Same solution as in JVET-K0307
Longer tap deblocking filter

## Slide 5: Longer tap Deblocking Filter (luma only)
New filter conditions considering:
  Block sizes
  Spatial activity across edges
On top of HEVC filter, longer tap uses:
  8 samples for filter decision on each side of the edge
  7 samples are modified on each side of the edge
Line buffer reduction for “longer tap filters” is also studied
  For horizontal edges overlapping with Hor. CTU boundaries:
    For the top block, the number of samples used in filter decision and filter modification are kept the same as in HEVC
    Modified filter condition and filter coefficients are proposed

## Slide 6: New filter conditions:
For both the first and fourth lines of a deblocking segment:

## Slide 7: New filter coefficients:
Output pixel | Filter coefficients {p7, p6, p5, p4, p3, p2, p1, p0, q0, q1, q2, q3, q4, q5, q6, q7} | Input pixels
p6 | {6, 3, 1, 1, 1, 1, 1, 1, 1, 0, 0, 0, 0, 0, 0, 0} | p7 ~ q0
p5 | {5, 1, 3, 1, 1, 1, 1, 1, 1, 1, 0, 0, 0, 0, 0, 0} | p7 ~ q1
p4 | {4, 1, 1, 3, 1, 1, 1, 1, 1, 1, 1, 0, 0, 0, 0, 0} | p7 ~ q2
p3 | {3, 1, 1, 1, 3, 1, 1, 1, 1, 1, 1, 1, 0, 0, 0, 0} | p7 ~ q3
p2 | {2, 1, 1, 1, 1, 3, 1, 1, 1, 1, 1, 1, 1, 0, 0, 0} | p7 ~ q4
p1 | {1, 1, 1, 1, 1, 1, 3, 1, 1, 1, 1, 1, 1, 1, 0, 0} | p7 ~ q5
p0 | {1, 1, 1, 1, 1, 1, 1, 2, 1, 1, 1, 1, 1, 1, 1, 0} | p7 ~ q6
q0 | {0, 1, 1, 1, 1, 1, 1, 1, 2, 1, 1, 1, 1, 1, 1, 1} | p6 ~ q7
q1 | {0, 0, 1, 1, 1, 1, 1, 1, 1, 3, 1, 1, 1, 1, 1, 1} | p5 ~ q7
q2 | {0, 0, 0, 1, 1, 1, 1, 1, 1, 1, 3, 1, 1, 1, 1, 2} | p4 ~ q7
q3 | {0, 0, 0, 0, 1, 1, 1, 1, 1, 1, 1, 3, 1, 1, 1, 3} | p3 ~ q7
q4 | {0, 0, 0, 0, 0, 1, 1, 1, 1, 1, 1, 1, 3, 1, 1, 4} | p2 ~ q7
q5 | {0, 0, 0, 0, 0, 0, 1, 1, 1, 1, 1, 1, 1, 3, 1, 5} | p1 ~ q7
q6 | {0, 0, 0, 0, 0, 0, 0, 1, 1, 1, 1, 1, 1, 1, 3, 6} | p0 ~ q7

## Slide 8: Filter for horizontal edges overlapping with CTU boundaries
Problem:
  Using a longer tap filter at CTU boundaries will require a increase in line buffer when compared to HEVC DBF.
Current Proposal:
  At CTU boundaries for the top blocks, only use
      “4” samples for filter decision
      “3” samples for filter modification
      Same as in HEVC
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
…
…
…
…
…
…
…
…
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
Block Height =16
Block Height =16
…
…
…
…
…
…
…
…
Horizontal edge overlapping with CTU boundary
x
Sample used in filter decision
x
Sample modified by filter

## Slide 9: Filter for horizontal edges overlapping with CTU boundaries
Output pixel | Filter coefficients {p7, p6, p5, p4, p3, p2, p1, p0, q0, q1, q2, q3, q4, q5, q6, q7} | Input pixels
p2 | {0, 0, 0, 0, 6, 3, 1, 1, 1, 1, 1, 1, 1, 0, 0, 0} | p3 ~ q4
p1 | {0, 0, 0, 0, 5, 1, 3, 1, 1, 1, 1, 1, 1, 1, 0, 0} | p3 ~ q5
p0 | {0, 0, 0, 0, 5, 1, 1, 2, 1, 1, 1, 1, 1, 1, 1, 0} | p3 ~ q6
q0 | {0, 0, 0, 0, 4, 1, 1, 1, 2, 1, 1, 1, 1, 1, 1, 1} | p3 ~ q7
q1 | {0, 0, 0, 0, 3, 1, 1, 1, 1, 3, 1, 1, 1, 1, 1, 1} | p3 ~ q7
q2 | {0, 0, 0, 0, 2, 1, 1, 1, 1, 1, 3, 1, 1, 1, 1, 2} | p3 ~ q7
q3 | {0, 0, 0, 0, 1, 1, 1, 1, 1, 1, 1, 3, 1, 1, 1, 3} | p3 ~ q7
q4 | {0, 0, 0, 0, 0, 1, 1, 1, 1, 1, 1, 1, 3, 1, 1, 4} | p2 ~ q7
q5 | {0, 0, 0, 0, 0, 0, 1, 1, 1, 1, 1, 1, 1, 3, 1, 5} | p1 ~ q7
q6 | {0, 0, 0, 0, 0, 0, 0, 1, 1, 1, 1, 1, 1, 1, 3, 6} | p0 ~ q7

## Slide 10: Characteristics of Filter conditions and coefficients as suggested to report by JVET-K0022 (CE2 report)
Color component | Additional sets of number of samples to filter on respective side | Maximum number of taps to filter one line | Max filter accuracy (>>N) | Line buffers
Luma | 7+7/3+7 *(3+7) used at horizontal CTU boundary | 168 (out of which 144 are power of 2 operations) | 4 | 4 (same as HEVC)
Switching frequency in number of lines | Total number of taps for smooth decisions per line(strong and long filters) | Deblock implicit split TUs | Deblock without overlap between CUs | Deblock sub-block boundaries
4 | 6 (for HEVCstrong/weak decision) + 16 (For New longer tap filter) | Yes | Yes | No

## Slide 11: Subjective results (I):
BMS 1.0
Proposed approach

## Slide 12: Subjective results (II):
BMS 1.0
Proposed approach

## Slide 13: Objective results:

## Slide 14: Summary && Conclusions:
Summary of our Longer Tap Filter:
  New filter conditions and filter coefficients
  Line buffer reduction
  Implicit TU boundaries are also filtered.
Conclusions:
  Significant improved subjective results.
  Objective results:
    VTM: -0.12%, -0.13%, -0.02% for AI, RA, LDB, respectively
    BMS: -0.08%, -0.01%, 0.04% for AI, RA, LDB, respectively
We request to study the proposal in a core experiment (CE)
Thanks to Canon for the cross check (JVET-K0492)

## Slide 15
Thank You
www.huawei.com

## Slide 16: An intermediate bug fix version
Codebase is BMS
Implicit TU boundaries are also filtered:
  Largest TU is 64x64
  Largest CU is 128x128
  Implicit TU boundaries occurs when a CU is 128x128 samples large
Parallel deblocking filter can be applied in parallel
  Restrict the number of filter samples:
    for vertical edges: no filter than half of the width of P and Q block
    for horizontal edges: no filter than half of the height of P and Q block
The proposal is above feature, plus:
  New filter condition and filter coefficients
  Line buffer restrictions

## Slide 17
Objective results over bugfix version

## Slide 18
Backup slides
Intermediate Bug Fix
Proposed approach

## Slide 19: Subjective results (II):
Intermediate Bug Fix
Proposed approach

## Slide 20
Backup slides