## Slide 1
              CE2.4.1.4: Reduced filter shape size for ALF
            JVET-K0371, JVET-K0372

## Slide 2: ALF shapes
BMS
CE2-4.1.4 (JVET-K0371)
JVET-K0372
luma
chroma
luma
chroma
luma/chroma
luma/chroma

## Slide 3: Signalled ALF shapes
BMS
  Classification 2x2
  Number of fixed filters is 400
  Luma: 5x5, 7x7, or 9x9, filtering is 9x9
  Chroma: 5x5, filtering is 5x5
CE2-4.1.4 (JVET-K0371)
  Classification 2x2 or 4x4
  Number of fixed filters is 128
  Max filter size is 9x9
    Luma: 5x5, 7x7 or 9x9, filtering is 9x9
    Chroma: 5x5, filtering 5x5; or 7x7, filtering 7x7
  Max filter size is 7x7
    Luma: 5x5 or 7x7, filtering is 7x7
    Chroma: 5x5, filtering 5x5; or 7x7, filtering 7x7
JVET-K0372
  Classification 2x2 or 4x4
  Number of fixed filters is 128
  Max filter size is 9x9
    Luma/chroma: 5x5, 7x7 or 9x9, filtering 9x9
  Max filter size is 7x7
    Luma/chroma: 5x5 or 7x7, filtering 7x7

## Slide 4: Results for VTM configuration
CE2-4.1.4 tests | AI (Y, U, V) |  |  | RA (Y, U, V) |  |  | LB (Y, U, V) |  |  | RA Enc | RA Dec
1. luma 7x7, classifier 2x2, chroma 5x5 | 3.10 | 3.56 | 4.07 | 5.10 | 2.29 | 1.69 | 4.32 | 1.79 | 1.77 | 105% | 135%
2. luma 7x7, classifier 2x2, chroma 7x7 | 3.09 | 4.20 | 4.73 | 5.11 | 3.16 | 2.66 | 4.31 | 2.63 | 2.72 | 104% | 134%
3. luma 7x7, classifier 4x4, chroma 5x5 | 2.99 | 3.56 | 4.07 | 4.99 | 2.24 | 1.66 | 4.19 | 1.64 | 1.85 | 104% | 122%
4. luma 7x7, classifier 4x4, chroma 7x7 | 2.98 | 4.20 | 4.73 | 4.98 | 3.14 | 2.66 | 4.23 | 2.44 | 2.57 | 104% | 122%
5. luma 9x9, classifier 2x2, chroma 5x5 | 3.28 | 3.54 | 4.05 | 5.33 | 2.21 | 1.63 | 4.56 | 1.81 | 2.01 | 108% | 143%
6. luma 9x9, classifier 2x2, chroma 7x7 | 3.27 | 4.19 | 4.71 | 5.35 | 3.11 | 2.57 | 4.63 | 2.61 | 2.88 | 107% | 142%
7. luma 9x9, classifier 4x4, chroma 5x5 | 3.17 | 3.54 | 4.05 | 5.21 | 2.20 | 1.66 | 4.46 | 1.83 | 2.01 | 107% | 129%
8. luma 9x9, classifier 4x4, chroma 7x7 | 3.16 | 4.19 | 4.71 | 5.23 | 3.15 | 2.63 | 4.49 | 2.59 | 2.72 | 108% | 129%
Reducing max filter shape from 9x9 to 7x7
  from 0.1 to 0.3 luma loss (test 1 vs test 5, test 2 vs test 6)
Changing classification block size from 2x2 to 4x4
  ~0.1 luma loss (test 1 vs test 3, test 2 vs test 4, test 5 vs test 7, test 6 vs test 8)

## Slide 5: Results for BMS configuration
CE2-4.1.4 tests | AI (Y, U, V) |  |  | RA (Y, U, V) |  |  | LB (Y, U, V) |  |  | RA Enc | RA Dec
2. luma 7x7, classifier 2x2, chroma 7x7 | 2.55 | 4.11 | 4.25 | 4.83 | 3.22 | 2.43 | 4.04 | 2.39 | 2.31 | 101% | 122%
4. luma 7x7, classifier 4x4, chroma 7x7 | 2.47 | 4.11 | 4.25 | 4.71 | 3.22 | 2.42 | 3.98 | 2.31 | 2.55 | 101% | 114%
6. luma 9x9, classifier 2x2, chroma 7x7 | 2.71 | 4.09 | 4.24 | 5.05 | 3.17 | 2.39 | 4.35 | 2.48 | 2.53 | 101% | 127%
8. luma 9x9, classifier 4x4, chroma 7x7 | 2.63 | 4.09 | 4.23 | 4.96 | 3.16 | 2.42 | 4.30 | 2.48 | 2.62 | 102% | 119%
CE2-4.1.4 tests | AI (Y, U, V) |  |  | RA (Y, U, V) |  |  | LB (Y, U, V) |  |  | RA Enc | RA Dec
2. luma 7x7, classifier 2x2, chroma 7x7 | -0.20 | 0.72 | 0.72 | -0.26 | 1.04 | 1.12 | -0.21 | 0.79 | 0.69 | 100% | 72%
4. luma 7x7, classifier 4x4, chroma 7x7 | -0.29 | 0.71 | 0.72 | -0.38 | 1.05 | 1.10 | -0.28 | 0.73 | 0.93 | 100% | 67%
6. luma 9x9, classifier 2x2, chroma 7x7 | -0.03 | 0.70 | 0.71 | -0.01 | 0.99 | 1.08 | 0.12 | 0.89 | 0.92 | 100% | 75%
8. luma 9x9, classifier 4x4, chroma 7x7 | -0.11 | 0.70 | 0.70 | -0.11 | 0.99 | 1.11 | 0.06 | 0.88 | 1.00 | 101% | 70%
Anchor is BMS with ALF disabled
Anchor is BMS

## Slide 6: Results of unified luma and chroma filter shapes
Anchor is VTM-1.0
JVET-K0372 tests | AI (Y, U, V) |  |  | RA (Y, U, V) |  |  | LB (Y, U, V) |  |  | RA Enc | RA Dec
1. Max filter 7x7, classifier 2x2 | 3.09 | 4.20 | 4.73 | 5.11 | 3.15 | 2.65 | 4.34 | 2.74 | 2.67 | 105% | 135%
2. Max filter 7x7, classifier 4x4 | 2.98 | 4.20 | 4.73 | 4.99 | 3.15 | 2.65 | 4.22 | 2.55 | 2.65 | 104% | 122%
3. Max filter 9x9, classifier 2x2 | 3.26 | 4.49 | 5.01 | 5.34 | 3.60 | 3.09 | 4.63 | 3.60 | 3.47 | 107% | 144%
4. Max filter 9x9, classifier 4x4 | 3.15 | 4.49 | 5.01 | 5.23 | 3.61 | 3.11 | 4.53 | 3.50 | 3.61 | 107% | 130%
CE2-4.1.4 tests | AI (Y, U, V) |  |  | RA (Y, U, V) |  |  | LB (Y, U, V) |  |  | RA Enc | RA Dec
1. luma 7x7, classifier 2x2, chroma 5x5 | 3.10 | 3.56 | 4.07 | 5.10 | 2.29 | 1.69 | 4.32 | 1.79 | 1.77 | 105% | 135%
3. luma 7x7, classifier 4x4, chroma 5x5 | 2.99 | 3.56 | 4.07 | 4.99 | 2.24 | 1.66 | 4.19 | 1.64 | 1.85 | 104% | 122%
5. luma 9x9, classifier 2x2, chroma 5x5 | 3.28 | 3.54 | 4.05 | 5.33 | 2.21 | 1.63 | 4.56 | 1.81 | 2.01 | 108% | 143%
7. luma 9x9, classifier 4x4, chroma 5x5 | 3.17 | 3.54 | 4.05 | 5.21 | 2.20 | 1.66 | 4.46 | 1.83 | 2.01 | 107% | 129%
~1% chroma gain is achieved with unified filter shapes

## Slide 7: TC offset
TC was used in JEM CTC
Encoder change in config file
  -6 for AI
  -2 for other configurations
 | All Intra Main10 |  |  |  | 
 | Over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.87% | -0.72% | 0.69% | 100% | 100%
Class A2 | -1.11% | -0.20% | -0.47% | 100% | 101%
Class B | -0.99% | -0.64% | 0.00% | 100% | 99%
Class C | -0.72% | -1.22% | -1.14% | 101% | 101%
Class E | -0.67% | 0.18% | 0.73% | 100% | 100%
Overall | -0.87% | -0.57% | -0.10% | 100% | 100%
Class D | -0.67% | -0.79% | -0.77% | 100% | 100%
 | Random Access Main 10 |  |  |  | 
 | Over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.04% | -0.53% | -0.18% | 100% | 99%
Class A2 | -0.23% | -0.31% | -0.40% | 100% | 100%
Class B | -0.26% | -0.58% | -0.56% | 100% | 101%
Class C | -0.18% | -0.70% | -0.73% | 100% | 99%
Class E |  |  |  |  | 
Overall | -0.19% | -0.55% | -0.50% | 100% | 100%
Class D | -0.22% | -0.73% | -0.70% | 100% | 101%
 | Low delay B Main10 |  |  |  | 
 | Over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.35% | -0.43% | -0.01% | 100% | 98%
Class C | -0.30% | -0.16% | -0.36% | 100% | 100%
Class E | -0.76% | -0.38% | 0.11% | 100% | 98%
Overall | -0.44% | -0.33% | -0.09% | 100% | 99%
Class D | -0.35% | 0.23% | -0.78% | 99% | 97%

## Slide 8: TC offset for CE test with ALF 7x7 and classification 4x4
 | All Intra Main10 |  |  |  | 
 | Over VTM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -3.05% | -3.21% | -2.71% | 103% | 121%
Class A2 | -3.82% | -3.89% | -4.16% | 102% | 118%
Class B | -3.43% | -3.03% | -3.02% | 102% | 114%
Class C | -3.38% | -3.84% | -4.74% | 101% | 105%
Class E | -5.12% | -8.27% | -8.25% | 101% | 114%
Overall | -3.70% | -4.26% | -4.41% | 102% | 113%
Class D | -2.58% | -3.51% | -4.12% | 102% | 105%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -4.43% | -3.61% | -2.11% | 105% | 130%
Class A2 | -6.37% | -2.41% | -1.82% | 106% | 129%
Class B | -5.52% | -4.80% | -3.28% | 104% | 121%
Class C | -4.25% | -2.51% | -3.76% | 103% | 111%
Class E |  |  |  |  | 
Overall | -5.13% | -3.47% | -2.88% | 104% | 122%
Class D | -5.00% | -3.04% | -3.63% | 105% | 108%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -4.38% | -3.49% | -2.43% | 105% | 116%
Class C | -4.10% | -2.93% | -3.43% | 103% | 115%
Class E | -5.33% | -1.93% | -2.76% | 113% | 109%
Overall | -4.52% | -2.91% | -2.85% | 106% | 114%
Class D | -4.16% | -3.82% | -3.90% | 101% | 101%
 | All Intra Main10 |  |  |  | 
 | Over VTM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -2.30% | -3.56% | -3.77% | 102% | 122%
Class A2 | -2.82% | -4.06% | -4.09% | 102% | 112%
Class B | -2.58% | -2.79% | -3.37% | 102% | 115%
Class C | -2.84% | -3.33% | -4.42% | 102% | 110%
Class E | -4.65% | -8.51% | -9.00% | 102% | 115%
Overall | -2.98% | -4.20% | -4.73% | 102% | 114%
Class D | -2.09% | -3.20% | -3.88% | 101% | 108%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -4.41% | -3.22% | -2.06% | 103% | 129%
Class A2 | -6.16% | -2.28% | -1.62% | 104% | 127%
Class B | -5.32% | -4.47% | -3.08% | 106% | 123%
Class C | -4.12% | -2.08% | -3.36% | 103% | 111%
Class E |  |  |  |  | 
Overall | -4.98% | -3.14% | -2.66% | 104% | 122%
Class D | -4.84% | -2.70% | -3.24% | 105% | 108%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -4.09% | -3.09% | -2.41% | 104% | 117%
Class C | -3.89% | -2.84% | -3.09% | 104% | 116%
Class E | -4.93% | -0.81% | -2.16% | 114% | 112%
Overall | -4.23% | -2.44% | -2.57% | 107% | 116%
Class D | -3.85% | -3.56% | -3.68% | 105% | 110%
TC offset is 0 (CE test)
TC offset is applied

## Slide 9: TC offset for CE test with ALF 9x9 and classification 2x2
 | All Intra Main10 |  |  |  | 
 | Over VTM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -3.26% | -3.19% | -2.69% | 102% | 139%
Class A2 | -4.15% | -3.87% | -4.15% | 102% | 133%
Class B | -3.67% | -3.00% | -2.99% | 101% | 129%
Class C | -3.91% | -3.82% | -4.72% | 99% | 114%
Class E | -5.62% | -8.27% | -8.25% | 101% | 130%
Overall | -4.06% | -4.24% | -4.40% | 101% | 128%
Class D | -3.16% | -3.51% | -4.12% | 100% | 114%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -4.59% | -3.57% | -2.00% | 106% | 155%
Class A2 | -6.69% | -2.34% | -1.68% | 108% | 153%
Class B | -6.01% | -4.73% | -3.32% | 107% | 141%
Class C | -4.65% | -2.55% | -3.67% | 106% | 127%
Class E |  |  |  |  | 
Overall | -5.50% | -3.44% | -2.82% | 107% | 142%
Class D | -5.56% | -3.11% | -3.64% | 110% | 124%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -4.86% | -3.29% | -2.56% | 108% | 135%
Class C | -4.49% | -3.01% | -3.52% | 105% | 123%
Class E | -5.70% | -1.47% | -2.35% | 121% | 118%
Overall | -4.95% | -2.74% | -2.83% | 110% | 127%
Class D | -4.76% | -3.85% | -3.91% | 105% | 112%
 | All Intra Main10 |  |  |  | 
 | Over VTM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -2.45% | -3.54% | -3.75% | 103% | 137%
Class A2 | -3.05% | -4.04% | -4.07% | 102% | 126%
Class B | -2.79% | -2.76% | -3.34% | 102% | 129%
Class C | -3.29% | -3.32% | -4.41% | 102% | 121%
Class E | -5.08% | -8.51% | -9.00% | 103% | 134%
Overall | -3.27% | -4.19% | -4.71% | 102% | 129%
Class D | -2.59% | -3.20% | -3.88% | 102% | 119%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -4.56% | -3.25% | -1.97% | 106% | 155%
Class A2 | -6.49% | -2.18% | -1.55% | 107% | 154%
Class B | -5.79% | -4.44% | -3.01% | 108% | 143%
Class C | -4.52% | -2.04% | -3.21% | 106% | 125%
Class E |  |  |  |  | 
Overall | -5.35% | -3.11% | -2.57% | 107% | 142%
Class D | -5.37% | -2.62% | -3.21% | 112% | 127%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -4.58% | -3.36% | -2.79% | 107% | 134%
Class C | -4.24% | -2.81% | -3.26% | 107% | 125%
Class E | -5.25% | -1.10% | -2.53% | 122% | 122%
Overall | -4.63% | -2.61% | -2.88% | 111% | 128%
Class D | -4.44% | -3.59% | -3.35% | 109% | 121%
TC offset is 0 (CE test)
TC offset is applied

## Slide 10: Recommendation
Use ALF classification 4x4
Align ALF filter shapes for luma and chroma
Reduce number of fixed filters
Add TC offset -6 for AI and -2 for other configurations in the next CTC