## Slide 1: JVET-K0389 Proposed software management for VTM
E. Thomas, A. Gabriel (TNO)
Joint Video Exploration Team (JVET)
of ITU-T SG 16 WP 3 and ISO/IEC JTC 1/SC 29/WG 11
11th Meeting: Ljubljana, SI, 10–18 Jul. 2018

## Slide 2: 1. Proposed VTM project organisation
Migration to Git
Migration to a Git-based hosting service (Gitlab)
Both already underway
Status?

## Slide 3: 1. Proposed VTM project organisation
A main repository containing the latest update agreed code base. This repository remains always clean with a working software.
For each CE or EE, one secondary repository is forked from the main repository.
Each JVET contributor may create individual repository to exchange and collaborate with other participants.

## Slide 4: 1. Proposed VTM project organisation
Type of repository | Main | Secondary (CE or EE) | Individual
Owned by | VTM coordinator | VTM coordinator | Contributor
Push permission | VTM coordinator | CE/EE participants | Contributor

## Slide 5: 2. Tooling for the VTM project / Unit tests
Pel IntraPrediction::xGetPredValDc( const CPelBuf &pSrc, const Size &dstSize ) {
CHECK( dstSize.width == 0 || dstSize.height == 0, "Empty area provided" );
Int iInd, iSum = 0;
Pel pDcVal;
const int width = dstSize.width;
const int height = dstSize.height;
for( iInd = 0; iInd < width; iInd++ ) {
iSum += pSrc.at( 1 + iInd, 0 );
}
for( iInd = 0; iInd < height; iInd++ ) {
iSum += pSrc.at( 0, 1 + iInd );
}
pDcVal = ( iSum + ( ( width + height ) >> 1 ) ) / ( width + height );
return pDcVal;
}

## Slide 6: 2. Tooling for the VTM project / Unit tests
CPelBuf pSrc = … (hardcoded);
Size dstSize = … (hardcoded);
Pel expected = … (hardcoded);
Pel tested = xGetPredValDc(pSrc, dstSize);
TEST_EQ(tested, expected) // Error if not equal

## Slide 7: 2. Tooling for the VTM project / Unit tests
Recommendation
Write unit tests at least for sensitive functions, metric calculation, transform, prediction, etc… There are several options for the framework to use: Google Test, Boost.Test, etc…

## Slide 8: 2. Tooling for the VTM project / Functional testing
expected = “expected.bin”
./Encoder [options] -o result.bin
TEST_EQ(expected.bin, result.bin)
expected = “expected.yuv”
./Decoder [options] -i test.bin -o result,yuv
TEST_EQ(“expected.yuv”, “result,yuv”)

## Slide 9: 2. Tooling for the VTM project / Functional testing
Recommendation
Write functional tests where expected bitstreams are compared to generated bitstreams for at least one test sequence over at least one GoP for each encoding configuration (intra, random access, etc…)

## Slide 10: 2. Tooling for the VTM project / Continuous integration
At every push, merge, tag, GitLab can trigger automatic build executed on a CI runner.
Runner executes tests and build in Docker (preferred)
Tests are defined in the current repository in a .gitlab-ci.yml

## Slide 11: 2. Tooling for the VTM project / Continuous integration

## Slide 12: 2. Tooling for the VTM project / Continuous integration
Practice | Test / Action | Tool
Unit testing | Are all the tests OK ? How much of the source code they cover ? | Google Test or Boost.Test (or similar)
Functional testing | Are all the tests OK ? (No crash, same bitstream produced if no new feature, etc…) | Custom script (e.g. Python)
Style guide | Is the code complying with the style guide ? | Cpplint, clang-format
Documentation | Regeneration document based on source code | doxygen