## Slide 1
JVET-K0390: Rate Control for VVC
Yiming Li, Zhenzhong Chen (Wuhan University)
Xiang Li, Shan Liu (Tencent)

## Slide 2: Introduction
Fixed a bug in VTM1.1/BMS1.1
Proposed an improved rate control method based on the current R-lambda model
Compared with HM rate control in VTM1.1(with bug fixed), it has 9.03%(Y), 2.94%(Y) performance improvement in RA and LB configuration
In LB configuration, it has 1.34%/3.81%/4.03% performance improvement when compared with fixQP method

## Slide 3
cs.fracBits >> SCALE_BITS is not the actual bits of the current CTU. The value will be accumulated.
#if !ENABLE_WPP_PARALLELISM
Int actualBits = int(cs.fracBits >> SCALE_BITS);
#endif
if ( pCfg->getUseRateCtrl() )
{
…
pRateCtrl->getRCPic()->updateAfterCTU( pRateCtrl->getRCPic()->getLCUCoded(), actualBits, actualQP, actualLambda, pcSlice->getSliceType() == I_SLICE ? 0 : pCfg->getLCULevelRC() );
…
}
In the function of void EncSlice::encodeCtus()
1. Bug fix
Proposed Method

## Slide 4
#if !ENABLE_WPP_PARALLELISM
Int actualBits = int(cs.fracBits >> SCALE_BITS);
#endif
#if WHU_BUG_FIX
actualBits -= (Int)m_uiPicTotalBits;
#endif
if ( pCfg->getUseRateCtrl() )
{
…
pRateCtrl->getRCPic()->updateAfterCTU( pRateCtrl->getRCPic()->getLCUCoded(), actualBits, actualQP, actualLambda, pcSlice->getSliceType() == I_SLICE ? 0 : pCfg->getLCULevelRC() );
…
}
Proposed Method
Proposed method:
1. Bug fix

## Slide 5
In HD sequences, most of the blocks are skipped, and the target bpp are very small in inter frames
  Causing the frame level R-D curve very flat
The CTU level lambda and QP will be clipped by the frame level parameters for avoiding fluctuation
R
D
Frame
avg.
Non-skip CTU
Proposed Method
2. Split the coding data of skip, non-skip blocks

## Slide 6
Proposed method:
Only calculate the average bits, distortion, and lambda for non-skip CTU.
Using these coding data of non-skip CTU to update the frame level R-D model
R
D
Frame
avg.
Non-skip CTU
Proposed Method
2. Split the coding data of skip, non-skip blocks

## Slide 7
Motivation:
The default updating strategy of R-D parameters is based on least square method.
Proposed Method
3. Updating strategy of the rate-distortion parameters

## Slide 8
Using the adjacent one or two frames to update the RD parameters in the same level.
can be obtained after encoding
Proposed Method
Proposed method:
3. Updating strategy of the rate-distortion parameters

## Slide 9
4. Extend rate control to support GOP 16
Current implementation if GOP size not equals to 4 or 8:
for ( Int i=0; i<GOPSize; i++ )
{
bitsRatio[i] = 10;
if ( !GOPList[i].m_refPic )
{
bitsRatio[i] = 2;
}
}
The performance may decrease in current random access configuration (GOP size=16).
Proposed Method

## Slide 10
Proposed method:
The target bits ratio is designed following W0062/X0038
QPlevelx = + QPOffset + QPOffestModelScale * QPOffest + QPoffsetModelOff
If is known, we can acquire the ratio of each layer
Proposed Method
If is unknown in the first two GOPs. Some fixed bit ratio tables are used.

## Slide 11
Simulation Results
LB configuration: HM RC in VTM 1.1 vs. FixQP

## Slide 12
Simulation Results
LB configuration: HM RC in VTM 1.1(with bug fix) vs. FixQP

## Slide 13
Simulation Results
LB configuration: Proposed without splitting skip CTU vs. FixQP

## Slide 14
Simulation Results
LB configuration: Proposed full strategy vs. FixQP

## Slide 15
Simulation Results
LB configuration: Proposed full strategy vs. HM RC in VTM (with bug fix)

## Slide 16
Simulation Results
Anchor Bit Error
(RC with Bug Fix)
Test Bit Error
Delta PSNRY
Delta PSNRU
Delta PSNRV
Avg. 0.39%
MAX. 3.62%
0.31%
2.19%
0.06
0.01
0.00
LB configuration: Proposed full strategy vs. HM RC in VTM (with bug fix)

## Slide 17
Simulation Results
RA configuration: HM RC in VTM 1.1 vs. FixQP

## Slide 18
Simulation Results
RA configuration: HM RC in VTM 1.1(with bug fix) vs. FixQP

## Slide 19
Simulation Results
RA configuration: Proposed with only GOP size Extend+Bug fix vs. FixQP

## Slide 20
Simulation Results
RA configuration: Proposed full strategy vs. FixQP
(Splitting skip CTU strategy is closed in RA configuration, currently)

## Slide 21
Simulation Results
RA configuration: Proposed full strategy vs. HM RC in VTM (with bug fix)

## Slide 22
Simulation Results
RA configuration: Proposed full strategy vs. Proposed with only GOP size Extend+Bug fix

## Slide 23
Simulation Results
Anchor Bit Error
(RC with Bug Fix)
Test Bit Error
Delta PSNRY
Delta PSNRU
Delta PSNRV
Avg. 0.43%
MAX. 3.91%
0.26%
2.60%
0.26
0.17
0.19
RA configuration: Proposed full strategy vs. HM RC in VTM (with bug fix)

## Slide 24
Simulation Results

## Slide 25
Simulation Results

## Slide 26
Simulation Results

## Slide 27
THANKS!