## Slide 1: Dense Residual Convolutional Neural Network (DRN) based In-Loop Filter for VVC
Yingbin Wang, Zhenzhong Chen, Yiming Li
Wuhan University
Liang Zhao, Shan Liu, Xiang Li
Tencent

## Slide 2
Outline
Introduction
Proposed Method
Experimental Results
Conclusion
1
2
3
4

## Slide 3: Introduction
In-Loop Filter in VTM1.1
Trans./ Quant.
Entropy
Coder
SAO
DBF
Input
frame
Recon.
frame
Bitstreams
Inter
Predictor
Intra
Predictor
Inv. Trans.
& Quant.
Split into
CTUs
+
-
+
+
In-loop filters
Predictor
Trans. / Quant. Coeff.
Prediction Data
Filter Ctrl. Data

## Slide 4: Introduction
Trans./ Quant.
Entropy
Coder
DRN
SAO
DBF
Input
frame
Recon.
frame
Bitstreams
Inter
Predictor
Intra
Predictor
Inv. Trans.
& Quant.
+
-
+
+
In-loop filters
Predictor
Trans. / Quant. Coeff.
Prediction Data
Filter Ctrl. Data
Split into
CTUs
Proposed Dense Residual Convolutional Neural Network (DRN) based In-Loop Filter

## Slide 5
Proposed Scheme
Pre-Processing
Post-Processing
Color Space Conversion
DRN
Up-
sampling
Color Space Conversion
Down-
sampling
Reconstructed
YUV420
Filtered
YUV420
YUV444
RGB
YUV444
RGB
Proposed Method

## Slide 6
The architecture of DRN.
CONV 3×3×M
CONV 3×3×M
CONV 3×3×M
CONV 3×3×M
···
N×DRU
N: the number of DRU
M: the number of the feature maps generated by the convolutional layer
Proposed Method

## Slide 7
Dense Residual Unit (DRU)
Proposed Method
CONV 3×3×M
ReLU
CONV 3×3×M
CONV 1×1×M

## Slide 8
Training details
Proposed Method
N=8 and M=64
Trained and validated on DIV2K dataset [1].
The high-quality images are compressed using different QPs (22, 27, 32 and 37) with All Intra (AI) configuration.
Mean square error (MSE) loss function:
[1] E. Agustsson and R. Timofte, “NTIRE 2017 challenge on single image super-resolution: dataset and study,” in Proc. IEEE Int. Conf. Computer Vision and Pattern Recognition Workshops (CVPRW), July 2017.

## Slide 9
Block-level on/off control
DRN
RDO
DF
SAO
Reconstruction
Filtered
Reconstruction
Proposed Method
Divided into
blocks
Divided into
blocks
Block-level on/off flags
Entropy
Coder
Bitstreams

## Slide 10
BD-rate results for the proposed scheme
Experimental Results
 | All Intra Main10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -3.50% | -20.59% | -18.79% | 112% | 1958%
Class A2 | -4.61% | -20.32% | -14.02% | 100% | 1656%
Class B | -4.38% | -16.77% | -20.27% | 91% | 2002%
Class C | -6.98% | -21.61% | -25.01% | 107% | 1145%
Class E | -9.77% | -7.70% | -12.49% | 108% | 1883%
Overall | -5.75% | -17.56% | -18.74% | 102% | 1689%
Class D | -6.92% | -21.98% | -24.85% | 116% | 1420%
Results for AI Main10 VS VTM1.1

## Slide 11
 | Random Access Main 10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -4.69% | -15.60% | -14.56% | 112% | 4080%
Class A2 | -8.02% | -19.74% | -10.37% | 117% | 5585%
Class B | -6.09% | -14.85% | -16.56% | 124% | 3539%
Class C | -5.77% | -14.36% | -14.43% | 116% | 3067%
Class E |  |  |  |  | 
Overall | -6.11% | -15.85% | -14.36% | 118% | 3840%
Class D | -5.57% | -15.98% | -18.49% | 125% | 2197%
BD-rate results for the proposed scheme
Experimental Results
Results for RA Main10 VS VTM1.1

## Slide 12
 | Low delay B Main10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -4.65% | -11.70% | -13.07% | 108% | 3409%
Class C | -5.70% | -15.09% | -13.30% | 112% | 3114%
Class E | -8.85% | -6.49% | -9.68% | 110% | 5227%
Overall | -6.05% | -11.53% | -12.30% | 110% | 3680%
Class D | -5.54% | -13.43% | -15.52% | 113% | 2711%
BD-rate results for the proposed scheme
Experimental Results
Results for LDB Main10 VS VTM1.1

## Slide 13
 | Low delay P Main10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -6.77% | -12.32% | -13.23% | 102% | 3091%
Class C | -5.81% | -15.48% | -14.13% | 130% | 3143%
Class E | -9.55% | -7.46% | -9.99% | 117% | 4783%
Overall | -7.14% | -12.16% | -12.72% | 115% | 3467%
Class D | -6.23% | -14.12% | -16.40% | 113% | 2427%
BD-rate results for the proposed scheme
Experimental Results
Results for LDP Main10 VS VTM1.1

## Slide 14
Experimental Results
Chart: The Number of DRU
| 2 | 8 | 16
Class B | 0.020819 | 0.033219 | 0.044
Class C | 0.034186 | 0.054613 | 0.064578
Class D | 0.036652 | 0.055845 | 0.064784
Class E | 0.047917 | 0.076203 | 0.09021
Performance of DRNLF with different number of DRUs (AI)

## Slide 15
Propose an additional CNN based in-loop filter based in-loop filter for VTM.
  Dense residual convolutional neural network;
  Taking advantage of the correlation of luma and both chroma;
  Block-level on/off control;
  Increasing performance as the number of DRU increases
Conclusion

## Slide 16
Simulation results report BD-rate savings for luma, and both chroma components compared with VTM1.1
  -5.75%, -17.56%, -18.74% for AI configuration,;
  -6.11%, -15.85%, -14.36% for RA configuration;
  -6.05%, -11.53%, -12.30% for LDB configuration;
  -7.14%, -12.16%, -12.72% for LDP configuration.
Conclusion

## Slide 17
Thank You!