## Slide 1: AHG8: Selective In-loop filtering for 360 Video Compression
10 July 2018
Samsung Electronics Co. Ltd

## Slide 2: Issue and Solution
In case of frame packing 2D projected spherical content, spherical non-neighbors may be placed as neighbors on 2D plane
Performing in-loop filtering on such content may introduce undesired artifacts as shown in below figure
If in-loop filters are applied in the above region (marked with red), color bleeding may happen across the boundary
Simple solution is to not to perform in-loop filtering across such boundaries which does not require major change in current codec and also does not require extra memory for padding (in case of spherical padding)
Spherical non-neighbors
Color Bleeding

## Slide 3: Bleeding artifacts with de-blocking filter
Without deblocking filter
With deblocking filter
Comparison of boundary artifact in Harbor sequence in RSP format (No Blending used)

## Slide 4: Effect of Deblocking and ALF

## Slide 5: Selectively disabling deblocking (OFF at seam boundary)
If the seam boundary is in the span of deblocking filter then deblocking filtering shall be disabled
Filtering area
Current CU
Boundary is on inside filtering area
Boundary is on outside filtering area
Filter off
Filter on
Seem boundary

## Slide 6: Contd…
RSP seam boundary
3x2 CMP seam boundary

## Slide 7: Objective Quality with Deblocking Filter ON/OFF
 | Deblocking ON |  |  | Deblocking Off |  | 
 | Y | U | V | Y | U | V
SkateboardInLot | -19.03% | -20.17% | -19.94% | -19.11% | -20.31% | -20.21%
ChairLift | -25.81% | -19.39% | -20.18% | -25.84% | -19.39% | -20.19%
KiteFlite | -9.57% | -2.43% | -4.48% | -9.58% | -2.45% | -4.53%
Harbor | -12.43% | -7.36% | -8.34% | -12.48% | -7.47% | -8.43%
Trolley | -9.46% | 0.12% | -4.91% | -9.47% | 0.02% | -4.96%
GasLamp | -7.71% | -3.80% | -2.75% | -7.73% | -3.83% | -2.81%
Balboa | -9.87% | -6.98% | -8.41% | -9.91% | -7.26% | -8.44%
Broadway | -8.64% | -7.45% | -6.96% | -8.67% | -7.36% | -6.96%
Landing2 | -2.60% | -2.62% | -4.77% | -2.59% | -2.74% | -4.95%
BranCastle2 | -11.49% | -9.33% | -9.19% | -11.50% | -9.36% | -9.27%
Class S1 | -14.00% | -8.84% | -10.10% | -14.04% | -8.91% | -10.19%
Class S2 | -8.15% | -6.60% | -7.33% | -8.17% | -6.68% | -7.41%
Overall | -11.66% | -7.94% | -8.99% | -11.69% | -8.02% | -9.08%
Objective quality improvement for RSP format with VTM software (CTC)

## Slide 8: Conclusion
Turning off in-loop filtering at the seam location of 360 projection formats (RSP,CMP,ISP,..) shows considerable improvement in subjective quality
Simply turning off in-loop filtering may not add complexity and require extra memory
If projection format and packings are fixed then the seam boundary can be uniquely identified
Using tiling to avoid in-loop filtering may not always work as the seam boundary may not be aligned with CTU. To make them aligned extra padding may be required which may increase the overall frame size
Using appropriate spherical neighbors for in-loop filtering is a good idea but it requires considerable changes in codec and additional memory as well
Our suggestion is to have a CE on this aspect for further investigation

## Slide 9
Thank you