## Slide 1: JVET-K0430: CE5-related: State-based probability estimator
Extension of the state-based VTM-1.0 (AVC, HEVC) probability estimator
Transition table size of VTM-1.0 is reduced from 64 bit to 32 elements
Two state variables S0 and S1 are used per context model (S0: 8 bit, S1: 12 bit) Note: Counter-based estimator of C5 requires at least 10 + 14 bit
Luma BD-rate reductions: VTM configuration: AI = -0.67%, RA = -0.45%, LB = -0.41% BMS configuration: AI = -0.71%, RA = -0.46%, LB = ???

## Slide 2: Memory comparison
 | VTM-1.0 | JVET-K0430 | Counter-based (CE5) | 
RAM per context model (ctx) | 7 bit | 8 + 12 bit | 15 + 15 bit | 10 + 14 bit
Transition table size (ROM) | 64 x 6 bit | 32 x 8 bit | 0 bit | 0 bit
BMS-1.0 total ctx RAM (359 context models) | 2,513 bit | 7,180 bit | 10,770 bit | 8,616 bit

## Slide 3: Similar update equations as in CE5
JVET-K0430:
if( bin == 1 ) { S0 += Next[16+(S0>>3)] >> 1 S1 += Next[16+(S1>>7)] } else { S0 -= Next[16+(-S0>>3)] >> 1 S1 -= Next[16+(-S1>>7)] }
Counter-based (CE5):
if( bin == 1 ) { S0 += ( 32768 - S0 ) >> 4 S1 += ( 32768 - S1 ) >> 7 } else { S0 -= S0 >> 4 S1 -= S1 >> 7 }
One small lookup table for updating both states:
Next[32]={ 171, 151, 132, 114, 98, 82, 68, 56, 45, 35, 28, 21, 16, 11, 8, 5, 4, 4, 4, 4, 4, 4, 4, 4, 4, 4, 4, 4, 4, 4, 4, 0 }

## Slide 4: Coding interval subdivision similar to VTM-1.0
VTM-1.0 (rangeTabLPS table size 64x4):
R_lps = rangeTabLps[ state ][(range >> 6) & 3]
JVET-K0439 (rangeTabLPS table size 32x16):
R_lps = rangeTabLps[ abs((S0<<4)+S1) >> 7][(range >> 4) & 15]
Further sizes are currently being tested.

## Slide 5: Experimental results

## Slide 6: Comparison of rangeTabLPS sizes (without cross-check) Reference: 32x16 (VTM), Test: 32x8 (VTM)

## Slide 7: Comparison to CE5 Test: 32x8 (VTM), Ref.: CE5, 10+14 bit, 32x8, noCW (VTM)