## Slide 1: JVET-K0469: CE3-related: Chroma intra prediction simplification
Chang-Hao Yau, Po-Han Lin, Ching-Chieh Lin, Sheng-Po Wang and Chun-Lung Lin
Ljubljana, SI
July 2018

## Slide 2: Outline
Observations
Proposed method
Results
Conclusions

## Slide 3: Observations
For Chroma Intra coding, there are 5 coding modes
  DM, Planar, DC, Vertical and Horizontal.
Neighboring chroma intra coding modes are not used in the current VTM design
5 RDOs are applied to select the best mode in the current VTM design
As single LM mode was adopted in VTM, then an additional RDO is applied
  Total 6 RDOs for chroma intra coding
Notes: To reduce the number of elements in the RDO list

## Slide 4: One possible solution
To use the neighboring coding mode by enabling MDMS in VTM
  Enbale MDMS to replace LM-Angular
Five candidates are used for signaling
The same number of RDO compared to the current VTM
Notes: To reduce the number of elements in the RDO list

## Slide 5: Results of VTM+MDMS
0.07% luma gain
0.41% and 0.46% chroma gain
Notes: To reduce the number of elements in the RDO list

## Slide 6: Proposed simplified method
Enable MDMS and only signal the first three candidates
RDO reduction: from 5 to 3
Notes: To reduce the number of elements in the RDO list

## Slide 7: Proposed method with enabling LM only + CCLM Cb-to-Cr (CE3 test 4.1.9)
Enabling CE3 test 4.1.9
  LM only + CCLM Cb-to-Cr
Keep only three RDOs
  LM only + CCLM Cb-to-Cr
  The first candidate from MDMS
  The second candidate from MDMS

## Slide 8: Results of VTM+CE3.4.1.9+Proposed method
Compare to VTM
  1.51%, 10.11%, 10.70% luma and chroma gain
  No encoding time change
Compare to VTM+CE3.4.1.9
  0.36%, 0.26% chroma gain
  14% encoding time saving
Notes: To reduce the number of elements in the RDO list

## Slide 9: Results over BMS
Compare to VTM
  0.01%, 0.22%, 0.25% luma and chroma gain
  9% encoding time saving
Notes: To reduce the number of elements in the RDO list

## Slide 10: Additional results with the adoption of single LM
Test: Single LM(4.1.8) + MDMS with 2 candidates

## Slide 11: Conclusions
Enabling MDMS and only signal the first two candidates when LM is on.
Compare to VTM+CE3.4.1.9
  0.36%, 0.26% chroma gain and 14% encoding time saving
It is suggested to further study in a CE.

## Slide 12: Thank you!

## Slide 13: Results of VTM+CE3.4.1.8+MDMS
Notes: To reduce the number of elements in the RDO list