## Slide 1: JVET-K0235 Complexity in CE2.4.2.2.e
Presenter: Ching-Yeh Chen
Authors: Ching-Yeh Chen, Yu-Chi Su, Yu-Wen Huang, Shaw-Min Lei

## Slide 2: BMS-GALF in BMS-1.0
Geometric block-based filter adaptation (GeometricBA) is supported
Up to 25 luma filters and 1 chroma filter in one filter set
  20 coef. in one 9x9 diamond filter * (25)* 9bits + 6 coeff * 9bits = 4554 bits
  12 coef. in one 7x7 diamond filter * (25)* 9bits + 6 coeff * 9bits = 2754 bits
16x25 predefined filters can be used
  20 coef. in one 9x9 diamond filter * 400 * 9bits + 6 coeff * 9bits = 72054 bits
  12 coef. in one 7x7 diamond filter * 128 * 9bits + 6 coeff * 9bits = 13878 bits
Signal all ALF parameters including filter parameters and on/off control flags before the first CTU by using CABAC
  The minimum size of on/off control unit is 8x8.
  For 3840 x2160 videos, the max number of on/off control flags is 129,600.
  If on/off flags are moved to CTU level, then 256 flags are required only.

## Slide 3: Proposed Method: CTB-based ALF with Slice Filter Sets
4 modes are supported for each CTB and coded with CU data interleaved
  Off: disable ALF
  NewFilterMode: signal one new filter
  MergeFilterMode: inherit one filter from one selected neighboring CTB
  SliceFilterMode: use the slice filter set, where could be multiple filters for luma
Slice filter set is signaled at slice header.
  Simplified to single filter for each color component in CE2.4.2.2.e

## Slide 4: Filter Footprints
One filter shape
  9x9 Cross + 3x3 Square
Two symmetry types
  Half symmetry: 10 signaled coefficients
  Full symmetry: 4 signaled coefficients
  Center coefficient is derived for filter gain equal to 1
  No offset
Coefficients
  8 bits representation and 7 bits are the fractional part
  80 bits per filter
0
1
2
3
5
7
8
5
4
2
1
8
3
7
6
4
9
9
6
0
0
1
2
3
3
1
2
3
3
2
1
2
3
1
0
3
3
3
0
0
10 additions to sum two pixels first 11 multiplications for filter coefficients 10 additions to sum 11 multiplication results
1 shift with 1 addition for normalization
1 comp for clipping => 21 additions, 11 multiplications, 1 shift, 1 comp.

## Slide 5: NewFilter & MergeFilter Modes
NewFilter mode
  Signal one new filter
  Apply it to every sample in the current CTB
  Deriving predictors by averaging 4 merge candidates takes 33 additions and 11 shifts per CTB
MergeFilter mode
  Inherit one filter among four merge candidates
  Apply the inherited filter to every sample in the current CTB
  Generate four merge candidates from one priority list
    12 comparisons * 10 coefficients per CTB
  Storage of filters
    80 bits per filter * (NumCTUsInRows +2) * 3 + 3 filters from slice filter set
C
2
1
3
5
4
6

## Slide 6: SliceFilter Mode in CE2.4.2.2.e
The filter in slice filter set is used
Apply the filter to each sample
Notes: Directional difference?

## Slide 7
Thank You