## Slide 1: 67 Intra mode coding with 3MPM
July,14, 2018
Narae Choi, Yinji Piao
JVET-K0529
(CE3.3-related)

## Slide 2: Intra mode coding
VTM Intra prediction
  35 Intra modes
  3MPM
  32 remaining modes: 5-bit FLC
3-MPM solution for 67 modes
  3MPM
  64 reaming mode: 6-bit FLC
6-MPM solution for 67 modes
  6MPM
  61 remaining modes: 3 modes: 5-bit FLC, 58 mode 6-bit FLC

## Slide 3: Complexity analysis
 | 3MPM | 6MPM
Number of Full RD check | numFull+ max.2MPM | numFull + max.3MPM
Number of condition check in MPM generation | 12 | 84
Number of condition check in parsing MPM | 1 | 5
Number of context model used for MPM coding | 0 | 3
Number of condition check in parsing remaining mode | 0 | 1
Number of bit for remaining mode | 6-bit FLC | 5/6-bit FLC

## Slide 4: Experimental result
BMS s/w
  VTM/BMS configuration
  67 Intra modes + 3MPM + 6-bit FLC
 | All Intra Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.13% | -0.45% | -0.39% | 102% | 102% | 0.76% | 0.27% | 0.39% | 95% | 97%
Class A2 | -0.51% | -0.84% | -0.62% | 102% | 105% | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class B | -0.76% | -1.02% | -1.17% | 101% | 99% | 0.74% | 0.40% | 0.30% | 95% | 99%
Class C | -0.45% | -0.48% | -0.61% | 101% | 96% | 0.72% | 0.46% | 0.50% | 93% | 98%
Class E | -1.16% | -1.73% | -1.53% | 102% | 95% | 0.74% | 0.52% | 0.24% | 94% | 100%
Overall | -0.61% | -0.89% | -0.88% | 102% | 99% | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class D | 0.01% | -0.21% | -0.09% | 102% | 99% | 0.46% | 0.18% | 0.37% | 94% | 98%
Class F (optional) | 0.25% | 0.16% | 0.23% | 101% | 99% | 1.28% | 1.13% | 0.75% | 94% | 99%
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.20% | -0.33% | -0.27% | 101% | 101% | 0.35% | 0.25% | 0.39% | 95% | 100%
Class A2 | -0.42% | -0.70% | -0.45% | 101% | 103% | 0.33% | -0.08% | 0.22% | 95% | 100%
Class B | -0.36% | -0.45% | -0.65% | 102% | 105% | 0.32% | 0.16% | -0.15% | 95% | 101%
Class C | -0.18% | -0.01% | -0.24% | 102% | 100% | 0.33% | 0.26% | -0.07% | 94% | 100%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | -0.29% | -0.36% | -0.43% | 102% | 102% | 0.33% | 0.16% | 0.05% | 95% | 100%
Class D | 0.03% | -0.05% | -0.12% | 104% | 98% | 0.21% | 0.04% | -0.20% | 106% | 99%
Class F (optional) | 0.16% | 0.22% | 0.27% | 112% | 106% | 0.81% | 0.53% | 0.70% | 112% | 106%

## Slide 5: Experimental result
BMS s/w
  VTM/BMS configuration
  67 Intra modes + 3MPM + 6-bit FLC
  NumFullRD+1+max2MPM
 | All Intra Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.30% | -0.43% | -0.41% | 105% | 100% |  |  |  |  | 
Class A2 | -0.65% | -0.92% | -0.68% | 105% | 104% |  |  |  |  | 
Class B | -0.88% | -1.05% | -1.24% | 107% | 97% |  |  |  |  | 
Class C | -0.58% | -0.56% | -0.67% | 109% | 102% | 0.49% | 0.30% | 0.30% | 100% | 98%
Class E | -1.34% | -1.70% | -1.55% | 106% | 99% | 0.53% | 0.46% | 0.22% | 98% | 101%
Overall | -0.76% | -0.92% | -0.93% | 107% | 100% |  |  |  |  | 
Class D | -0.22% | -0.14% | -0.05% | 111% | 101% | 0.20% | 0.11% | 0.30% | 100% | 97%
Class F (optional) |  |  |  |  |  |  |  |  |  | 
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.27% | -0.38% | -0.33% | 99% | 105% |  |  |  |  | 
Class A2 | -0.48% | -0.73% | -0.43% | 97% | 106% |  |  |  |  | 
Class B | -0.43% | -0.46% | -0.67% | 99% | 106% | 0.23% | -0.07% | -0.17% | 98% | 101%
Class C | -0.29% | -0.20% | -0.27% | 103% | 106% | 0.22% | 0.10% | -0.23% | 99% | 100%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | -0.37% | -0.43% | -0.45% | 100% | 106% |  |  |  |  | 
Class D | -0.07% | 0.21% | -0.04% | 108% | 108% | 0.08% | -0.18% | -0.32% | 103% | 106%
Class F (optional) |  |  |  |  |  |  |  |  |  | 

## Slide 6: Experimental result (by 6mpm proponent)
 | All Intra Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.80% | -0.85% | -0.74% | 115% | 101% |  |  |  |  | 
Class A2 | -1.10% | -1.14% | -1.09% | 115% | 100% |  |  |  |  | 
Class B | -1.40% | -1.38% | -1.44% | 115% | 101% |  |  |  |  | 
Class C | -1.06% | -0.91% | -1.03% | 115% | 104% | -0.04% | 0.00% | -0.06% | 100% | 99%
Class E | -1.85% | -2.13% | -1.94% | 115% | 102% | -0.04% | 0.00% | -0.07% | 100% | 99%
Overall | -1.25% | -1.27% | -1.26% | 115% | 102% |  |  |  |  | 
Class D | -0.38% | -0.31% | -0.40% | 115% | 104% | -0.04% | 0.10% | 0.14% | 100% | 99%
Class F (optional) |  |  |  |  |  |  |  |  |  | 
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.48% | -0.42% | -0.30% | 102% | 100% |  |  |  |  | 
Class A2 | -0.69% | -0.67% | -0.49% | 101% | 99% |  |  |  |  | 
Class B | -0.65% | -0.47% | -0.61% | 102% | 100% | -0.02% | -0.10% | 0.01% | 99% | 99%
Class C | -0.45% | -0.27% | -0.34% | 103% | 101% | 0.02% | 0.13% | -0.22% | 99% | 100%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | -0.57% | -0.45% | -0.45% | 102% | 100% |  |  |  |  | 
Class D | -0.17% | 0.23% | -0.12% | 103% | 101% | -0.01% | -0.17% | -0.01% | 100% | 100%
Class F (optional) |  |  |  |  |  |  |  |  |  | 
6MPM + 5/6bit-FLC

## Slide 7: Experimental result (by 6mpm proponent)
 | All Intra Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 |  |  |  |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  |  |  |  | 
Class B |  |  |  |  |  |  |  |  |  | 
Class C | -1.06% | -0.91% | -1.03% | 109% | 106% |  |  |  |  | 
Class E |  |  |  |  |  |  |  |  |  | 
Overall |  |  |  |  |  |  |  |  |  | 
Class D | -0.38% | -0.31% | -0.40% | 109% | 105% |  |  |  |  | 
Class F (optional) |  |  |  |  |  |  |  |  |  | 
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-1.0 |  |  |  |  | Over BMS-1.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 |  |  |  |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  |  |  |  | 
Class B |  |  |  |  |  |  |  |  |  | 
Class C |  |  |  |  |  |  |  |  |  | 
Class E |  |  |  |  |  |  |  |  |  | 
Overall |  |  |  |  |  |  |  |  |  | 
Class D |  |  |  |  |  |  |  |  |  | 
Class F (optional) |  |  |  |  |  |  |  |  |  | 
6MPM + 5/6bit-FLC + encFastOpt

## Slide 8: Conclusion
Suggest simple intra mode coding in VTM s/w
Less condition check for MPM generation
Encoder optimization method for 6MPM also can be applied to 3MPM solution