## Slide 1: Spatial-temporal merge mode (non subblock STMVP)
(JVET-K0161/K0532)
TianYang Zhou
Tomohiro Ikai

## Slide 2: Outline
Proposal
Simulation results
  VTM results
  BMS results
Conclusion

## Slide 3: Proposal
A spatial-temporal merge candidate
  No subblock operation
  Average of motion vectors of above, left and temporal block is calculated
  Above and Left block, up to two position are checked.
0.80 % gain in VTM RA
  better gain than subblock based STMVP in BMS software (0.76 %)
  similar gain of subblok based ATMVP in BMS (0.87 %)

## Slide 4: Proposal: Referencing position
Spatially two position (above and left)
  Afar: (nPbW * 5 / 2, -1), Amid (nPbW / 2, -1)
  Lfar: (-1, nPbH * 5 / 2), Lmid (-1, nPbH/2)
Temporally one position
  collocated position as HEVC
Amid
Afar
Lmid
Lfar
(nPbW/2, -1)
(nPbW*5/2, -1)
(-1, nPbH/2)
(-1, nPbH*5/2)

## Slide 5: Proposal: Motion averaging
2 spatial MV (above and left) and 1 temporal vector is averaged
  mvLX[0] = ((mvLX_A[0] + mvLX_L[0] + mvLX_C[0]) * 43) / 128
  mvLX[1] = ((mvLX_A[1] + mvLX_L[1] + mvLX_C[1]) * 43) / 128
  Note: 1 multiply with 1 shift for each component. in bi-prediction, both L0 and L1 vector is computed in the same way.
  Note: if only two vectors are available, just averaging is used.

## Slide 6: Simulation results (VTM, RA)
Note: the number of merge candidates (MaxNumMergeCand) is 6 in test and 5 in anchor.
 |  | Random Access Main 10 |  |  |  | 
 |  | Over BMS-1.0 ( VTM configuration ) |  |  |  | 
 |  | Y | U | V | EncT | DecT
proposed | Class A1 | -0.83% | -0.85% | -0.81% | 102% | 100%
 | Class A2 | -1.12% | -1.12% | -1.12% | 102% | 101%
 | Class B | -0.80% | -0.71% | -0.64% | 103% | 103%
 | Class C | -0.53% | -0.56% | -0.65% | 103% | 102%
 | Overall | -0.80% | -0.78% | -0.78% | 102% | 102%
 | Class D | -0.64% | -0.45% | -0.58% | 103% | 102%
STMVP technique (jn BMS, JEM) | Class A1 | -0.75% | -0.93% | -0.89% | 106% | 126%
 | Class A2 | -1.13% | -1.29% | -1.15% | 106% | 132%
 | Class B | -0.68% | -0.96% | -0.80% | 107% | 123%
 | Class C | -0.61% | -0.92% | -1.02% | 106% | 123%
 | Overall | -0.76% | -1.01% | -0.95% | 106% | 126%
 | Class D | -0.77% | -0.79% | -0.86% | 106% | 123%
STMVP technique (128x128 subblock = no subblock) | Class A1 | -0.64% | -0.67% | -0.66% | 102% | 102%
 | Class A2 | -0.90% | -0.91% | -0.96% | 102% | 103%
 | Class B | -0.66% | -0.53% | -0.49% | 102% | 101%
 | Class C | -0.45% | -0.48% | -0.40% | 102% | 101%
 | Overall | -0.65% | -0.62% | -0.59% | 102% | 102%
 | Class D | -0.63% | -0.44% | -0.66% | 102% | 101%
just for comparison
(not proposal)
Proposal

## Slide 7: Simulation results (VTM, LB)
 |  | Low delay B Main10 |  |  |  | 
 |  | Over BMS-1.0 ( VTM configuration ) |  |  |  | 
 |  | Y | U | V | EncT | DecT
proposed | Class B | -0.42% | -0.08% | -0.53% | 109% | 116%
 | Class C | -0.32% | -0.03% | -0.05% | 107% | 115%
 | Class E | -0.02% | -0.13% | -0.39% | 107% | 105%
 | Overall | -0.28% | -0.06% | -0.14% | 108% | 113%
 | Class D | -0.40% | -0.17% | -0.08% | 107% | 109%
Note: the number of merge candidates (MaxNumMergeCand) is 6 in test and 5 in anchor.

## Slide 8: Simulation results (BMS, RA)
 |  | Random Access Main 10 |  |  |  | 
 |  | Over BMS-1.0 |  |  |  | 
 |  | Y | U | V | EncT | DecT
Proposed | Class A1 | -0.33% | -0.30% | -0.29% | 102% | 105%
 | Class A2 | -0.39% | -0.25% | -0.42% | 103% | 103%
 | Class B | -0.41% | -0.26% | -0.32% | 103% | 106%
 | Class C | -0.26% | -0.18% | -0.24% | 102% | 102%
 | Overall | -0.35% | -0.24% | -0.31% | 102% | 104%
 | Class D | -0.46% | -0.38% | -0.36% | 103% | 100%
Note: the number of merge candidates (MaxNumMergeCand) is 7 in test and 6 in anchor.

## Slide 9: Conclusion
This contribution proposes a spatial-temporal merge mode (no subblock STMVP) as an efficient method.
It is reported that the bd-rate gain shows 0.80 % and 0.28 % in RA and LB condition respectively.