## Slide 1: JVET-L0068 CE4-related : DC prediction based LIC
Kwangwoon University, ETRI

## Slide 2: Introduction
LIC in BMS 2.0.1 employs a linear model by using the neighboring reconstructed samples of the current CU and reference CU
Figure 1. Current block for local illumination compensation and its reconstructed reference samples

## Slide 3: Introduction
To compute the linear model parameter, all the previous neighboring CUs have been reconstructed, thus, the prediction for the current CU cannot start
To solve this, K0118 saves the scale and offset parameter of the LIC after CU reconstruction
Figure 2. Parameter computation process of K0118

## Slide 4: Introduction
However, this method still has a problem that it cannot proceed before the processing of the neighboring CU is all finished
Figure 3 shows a case of LIC pipeline issue for adjacent CUs
  The #2 CU cannot start to decode before computation and decoding of #1 CU

## Slide 5: Introduction
Additionally, there is a problem that an additional memory is required for store scale and offset parameter
Therefore, this contribution proposed an DC-based LIC method to alleviates LIC pipeline issue by calculate and save LIC parameter before previous CU processes is completed
In addition, the proposed method uses only offset parameter without using the scale parameter, it reduces memory size to save LIC parameter and computes the offset parameter with lower complexity

## Slide 6: DC prediction based LIC
In this contribution, only offset parameter is used to compensate illumination change
The offset parameter can be computed from residual data not reconstructed sample values
The offset parameter β is represented by
  Where R(n) is neighboring reconstructed sample of reference CU and C(n) is neighboring reconstructed sample of current CU

## Slide 7: DC prediction based LIC
In the merge case, R(n) is the predictor signal of C(n) and C(n) is the reconstructed signal
Since α is assumed to be 1 and the difference between and is residual, the numerator of offset parameter can be denoted by
Figure 4. Relation of neighboring reconstructed sample between merged CU and its reference CU

## Slide 8: DC prediction based LIC
2D IDCT is implemented by row-column decomposition method
The DC of bottom boundary pixels for a 2D residual signal is the DC coefficient of the vertical inverse transform for the bottom boundary coefficient
  Thus, the DC of the bottom boundary pixels can be derived in between 2D IDCT
(2)
Figure 5. Derivation of the offset parameter during 2D inverse transform

## Slide 9: DC prediction based LIC
After the CU process is finished, the offset parameter computed at given CU is stored
If the given CU is applied LIC, the value of the stored offset parameter plus the value of the offset parameter which used for the LIC is stored
Figure 6. Example of storing offset parameter

## Slide 10: DC prediction based LIC
With this method, it is possible to alleviate the pipeline issue of the LIC of BMS 2.0.1
  In BMS 2.0.1 and K0018 method, LIC application can start after reconstructed of reference CU
  But in proposed method, LIC application can start before reconstruction of reference CU

## Slide 11: DC prediction based LIC
Figure 6. Pipeline stages of the LIC in BMS 2.0.1 and the proposed LIC

## Slide 12: DC prediction based LIC
In BMS 2.0.1, LIC flag can be signaled or not, depending on the size of the CU, type of prediction modes and merge on/off mode
  When the LIC flag is signaled, the flag indicate whether LIC is applied to a given CU or not
In the proposed design, any LIC flag is not signaled
  If the current CU is coded by the merge mode and its motion vector is the same to that of the left side CU, LIC is applied to the current CU
In the current design, the flag is not used
  However RD optimization with a flag can be used for the proposed method
  Further study should be required to improve RD performance with the LIC on/off flag

## Slide 13: Experiment result
The proposed DC prediction based LIC is implemented within VTM 2.0.1
  VTM 2.0.1 vs proposed LIC
 |  | BD-rate (piecewise cubic) |  |  | BD-rate (cubic) |  | 
 |  | Y | U | V | Y | U | V
Class B | MarketPlace | 0.09% | 0.37% | 0.05% | 0.09% | 0.36% | 0.04%
 | RitualDance | -0.11% | -0.07% | 0.01% | -0.11% | -0.04% | 0.00%
 | Cactus | -0.01% | 0.01% | 0.04% | -0.01% | 0.01% | 0.05%
 | BasketballDrive | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
 | BQTerrace | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Class C | BasketballDrill | -0.14% | -0.14% | -0.21% | -0.14% | -0.13% | -0.20%
 | BQMall | -0.02% | 0.21% | -0.23% | -0.02% | 0.23% | -0.24%
 | PartyScene | -0.03% | 0.10% | -0.07% | -0.03% | 0.08% | -0.07%
 | RaceHorses | 0.05% | 0.23% | 0.35% | 0.05% | 0.27% | 0.35%
Class D | BasketballPass | 0.04% | 0.03% | 0.17% | 0.05% | 0.01% | 0.26%
 | BQSquare | 0.05% | -0.07% | 0.03% | 0.04% | -0.13% | 0.02%
 | BlowingBubbles | -0.10% | 0.12% | 0.01% | -0.10% | 0.09% | -0.01%
 | RaceHorses | 0.05% | 0.19% | 0.00% | 0.04% | 0.19% | 0.03%
 | Class B | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
 | Class C | -0.03% | 0.10% | -0.04% | -0.04% | 0.11% | -0.04%
 | Class D | 0.01% | 0.07% | 0.05% | 0.01% | 0.04% | 0.08%
 | All | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!

## Slide 14: THANK YOU
Q&A