## Slide 1
Most Frequent Mode (MFM) for Intra Mode Coding
JVET-L0155
The 12th JVET Meeting
Oct. 2018
Yong-Uk Yoon, Do-Hyeon Park, Jae-Gon Kim
Jinho Lee, Jungwon Kang

## Slide 2: Most Frequent Mode
Background
  The MPM efficiently represents the intra mode of the current block with the neighbor modes as candidates
    Assuming that the current block is highly correlated with the neighboring blocks in terms of prediction mode
  The MPM is signaled with MPM_FLAG (1-bin) and MPM_IDX (1~2-bins)
  Since the number of intra mode is increased to 67,
    The MPM candidates derived from two locations may not be enough to accommodate diverse modes
  Observations
    One or two modes are likely to be dominant in the selected mode distribution
    The more the same mode exists in the neighboring blocks,
      The more the intra mode of current block is the same mode with the neighboring mode

## Slide 3: Most Frequent Mode
Most Frequent Mode (MFM)
  Derive one intra mode from the five neighboring blocks which are the same positions for MERGE derivation
    The MFM is the most frequent mode at the derivation positions
  To select among the same frequent modes and avoid redundancy in the MPM derivation
    The search order is defined
      L → A → LB → AR → AL
  The MPM candidates list order
    L → A → Planar → DC → LB → AR → AL
  The selected MFM is signaled by MFM_FLAG
    If MFM_FLAG is false, parse MPM_FLAG
      The remaining modes (63) are coded by TB

## Slide 4: Most Frequent Mode
Examples of MFM derivation
  If there are multiple modes with the same occurrence
    A priority is given in the order of the search order
      L → A → LB → AR → AL

## Slide 5: Experiment Results
Experiment results
  VTM configuration over BMS 2.0.1
  In VTM 2.0.1, the number of MPM RD-check is determined according to the neighboring modes condition below:
    (Above == Left) ? 1 : 2
  Three tests include the MFM in default in the RD-check list and adjust the number of RD-checks for the MPM
    Test 1: MFM & (Above == Left) ? 0 : 1 for MPM
      The same with the current number of RD-check in VTM 2.0.1
    Test 2: MFM & (Above == Left) ? 1 : 1 for MPM
      MPM 0 are included in default in RD-check list
    Test 3: MFM & (Above == Left) ? 1 : 2 for MPM
      Add 1 or 2 MPMs in RD-check list

## Slide 6: Experiment Results
  Test 1: (Above == Left) ? 0 : 1
  Test 2: (Above == Left) ? 1 : 1
 | Over BMS-2.0.1 (VTM cfg) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.24% | -0.30% | -0.24% | 100% | 104%
Class A2 | -0.24% | -0.25% | -0.32% | 100% | 100%
Class B | -0.26% | -0.31% | -0.32% | 100% | 100%
Class C | -0.32% | -0.39% | -0.19% | 100% | 99%
Class E | -0.35% | -0.34% | -0.39% | 101% | 97%
Overall | -0.28% | -0.32% | -0.29% | 100% | 100%
Class D | -0.15% | -0.02% | -0.26% | 101% | 94%
Class F (optional) | -0.37% | -0.45% | -0.39% | 102% | #NUM!
 | Over BMS-2.0.1 (VTM cfg) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.33% | -0.36% | -0.32% | 104% | 104%
Class A2 | -0.31% | -0.33% | -0.33% | 103% | 100%
Class B | -0.34% | -0.32% | -0.32% | 104% | 100%
Class C | -0.36% | -0.40% | -0.25% | 103% | 99%
Class E | -0.41% | -0.42% | -0.37% | 103% | 98%
Overall | -0.35% | -0.36% | -0.32% | 103% | 100%
Class D | -0.22% | -0.08% | -0.36% | 103% | 96%
Class F (optional) | -0.46% | -0.61% | -0.55% | 104% | #NUM!

## Slide 7: Experiment Results
  Test 3: (Above == Left) ? 1 : 2
 | Over BMS-2.0.1 (VTM cfg) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.52% | -0.42% | -0.39% | 110% | 105%
Class A2 | -0.40% | -0.34% | -0.41% | 110% | 100%
Class B | -0.45% | -0.39% | -0.38% | 111% | 101%
Class C | -0.47% | -0.45% | -0.29% | 111% | 101%
Class E | -0.58% | -0.45% | -0.52% | 111% | 99%
Overall | -0.48% | -0.41% | -0.39% | 111% | 101%
Class D | -0.33% | -0.09% | -0.37% | 113% | 101%
Class F (optional) | -0.61% | -0.68% | -0.54% | 113% | #NUM!

## Slide 8: Conclusions
Proposed MFM
  The MFM is derived from neighbors
    Signaled with MFM_FLAG (1 bin)
Coding gain in BD-rate for AI
  Three tests include the MFM in default in the RD-check list and adjust the number of RD-checks for the MPM
    Test 1: including MFM & (Above == Left) ? 0 : 1 for MPM
      0.28% gains, 100%/100% encoding/decoding time
    Test 2: including MFM & (Above == Left) ? 1 : 1 for MPM
      0.35% gains, 103%/100% encoding/decoding time
    Test 3: including MFM & (Above == Left) ? 1 : 2 for MPM
      0.48% gains, 111%/101% encoding/decoding time
Suggest to study this contribution in the intra mode coding CE
  Meaningful coding gain without decoding run time increase