## Slide 1: JVET-K0156 – CE4.2.4 Adding constructed temporal affine to affine merge mode
October 2018
F.Galpin - Technicolor

## Slide 2: Constructed temporal affine
Add temporal constructed affine candidates
  Full list of candidates for 6 parameters model:
  Add a test to detect spurious affine candidate, similar to pure translational model detection in common base
Final number of candidates | Max Number of inherited candidates | Max Number of constructed candidates (4 prms) | Max Number of constructed candidates (6 prms)
8 | 5 | 12 | 16
Candidate number | Type | Corner number | Corner name
1 | spatial | { 0, 1, 2 } | LT, RT, LB
2 | temporal | { 0, 1, 2 } | LT, RT, LB
3 | spatial | { 0, 1 } | LT, RT
4 | temporal | { 0, 1, 3 } | LT, RT, RB
5 | spatial | { 0, 2 } | LT, LB
6 | temporal | { 0, 2, 3 } | LT, LB, RB
7 | spatial | { 1, 2 } | RT, LB
8 | temporal | { 1, 2, 3 } | RT, LB, RB
9 | spatial | { 0, 1, 3 } | LT, RT, RB
10 | temporal | { 0, 1 } | LT, RT
11 | spatial | { 0, 2, 3 } | LT, LB, RB
12 | temporal | { 0, 2 } | LT, LB
13 | spatial | { 1, 2, 3 } | RT, LB, RB
14 | temporal | { 1, 2 } | RT, LB
15 | spatial | { 0, 3 } | LT, RB
16 | temporal | { 0, 3 } | LT, RB

## Slide 3: Results
 | Random Access Main 10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -1.02% | -0.68% | -1.01% | 110% | 111%
Class A2 | -1.15% | -1.15% | -1.25% | 112% | 113%
Class B | -0.75% | -0.59% | -0.75% | 111% | 109%
Class C | -0.61% | -0.47% | -0.48% | 110% | 109%
Overall | -0.85% | -0.69% | -0.83% | 111% | 110%
Class D | -0.90% | -0.74% | -0.81% | 111% | 118%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class B | -0.42% | -0.49% | -0.53% | 117% | 116%
Class C | -0.40% | -0.61% | -0.32% | 110% | 109%
Class E | -0.76% | -0.35% | -0.39% | 111% | 113%
Overall | -0.50% | -0.50% | -0.42% | 113% | 113%
Class D | -0.62% | 0.48% | -0.43% | 109% | 108%

## Slide 4: Complexity
  Filtering has the a complexity of 34 (compared to 14 for the common base), thanks to the reuse of previous comparisons results for temporal candidates (see stroken pairs in the table below)
Complexity analysis of list construction |  |  |  |  |  | 
 | Max number of |  |  |  |  | 
M Merge list size | P Potential candidates | candidate comparison (M-2)*(M-1)/2 + (M-1) * (P-M+1) | MV scaling | temporal candidates | Max number of memory access | Others
8 | 21 | 119 | 32 | 8 | 21 | 34 CPMV comparisons
Candidate number | Type | CPMV number | CPMV pair comparison
2 | temporal | { 0, 1, 2 } | (0,1) (0,2)
4 | temporal | { 0, 1, 3 } | (0,1) (0,3)
6 | temporal | { 0, 2, 3 } | (0,3) (0,2)
8 | temporal | { 1, 2, 3 } | (1,2) (1,3)
10 | temporal | { 0, 1 } | (0,1)
12 | temporal | { 0, 2 } | (0,2)
14 | temporal | { 1, 2 } | (1,2)
16 | temporal | { 0, 3 } | (0,3)

## Slide 5
Thanks to H. Huang for cross-checking (contribution L0580)

## Slide 6: CPMV comparisons reduction
Max list size | Type | CPMV number | CPMV comparisons
6 | temporal | { 0, 1, 2 } | {0}: 6, {1}:6, {2}:6
7 | temporal | { 0, 1, 3 } | {0}:1, {1}:1, {2’}:7
7 | temporal | { 0, 2, 3 } | {0’}:7, {1’}:1, {2}:1
7 | temporal | { 1, 2, 3 } | {0’}:7, {1}:1, {2’}:7
7 | temporal | { 0, 1 } | {2’}:7
7 | temporal | { 0, 2 } | {1’}:7
7 | temporal | { 1, 2 } | {0’}:7
7 | temporal | { 0, 3 } | {1’}:7 {2’}:7
Further optimization can also be performed for candidate comparisons. If result of the comparison with each CPMV with the candidates list is kept, it can reduced the number of comparisons to perform. In the table, numbers with an apostrophe refer to CPMV recomputed from other CPMVs. In the last column, we show the number of comparison N to perform for a CPMV C as {C}:N.
The total number of CPMV comparison is down 6*3+7*3*7=273 from to 86.