## Slide 1: JVET-L0160 AHG14: Intra Refresh Test conditions and Anchors generation Proposal
Jean-Marc Thiesse
Didier Nicholson
David Gommelet

## Slide 2: Background
Intra Refresh is a classical technology addressing:
  Low-latency by removing of sizeable I picture while keeping random accessibility of stream
  And/or error resilience.
Usually implemented by encoder-only modifications leading to significant efficiency losses.
JVET-K0212 proposed a normative approach to handle Intra Refresh => AhG 14 was established at Ljubljana.
JVET-L0160

## Slide 3: Summary
This contribution addresses AhG14 first mandates:
  Proposition of test conditions for studying Intra Refresh.
  Proposition of an encoder-only Intra Refresh.
  Characterization of the solution.
JVET-L0160

## Slide 4: Encoder-only Intra Refresh proposal
The software modifications to support Intra Refresh tool at the encoder-level in VTM software include:
  Intra prediction mode forced on column basis.
  Constrained Intra Prediction enabled.
  Motion vectors constrained (6 pixels due to filters).
  Removing of former reference pictures at re-looping.
  Disabling of ALF of CTU including Intra refresh pixels.
JVET-L0160

## Slide 5: Software modifications
The additional parameters added to the configuration file are as follows:
  IntraRefreshType : 1 # Intra Refresh type flag 0: disable, 1: enc-only, 2: normative
  IntraRefreshStart : 0 # Position of the first column of Intra refresh (in pixels)
  IntraRefreshDirection : 0 # Direction of Intra Refresh 0: left to right, 1: right to left
  IntraRefreshPeriod : 32 # Period of the Intra Refresh
JVET-L0160

## Slide 6: Test condition for Intra Refresh
Basis: Low-Delay B Main10 configuration
Without pyramidal B structure
QP offset = +1
Intra Refresh period of 32 (as Random Access)
Reference for losses characterization:
Same with an Intra period of 32 (I picture)
JVET-L0160

## Slide 7: Results: Intra Refresh without constraints
=>Losses already comes by forcing Intra CUs (motion dependencies break and less efficient Intra)
JVET-L0160
 | Low delay B Intra Refresh Main10 |  |  |  | 
 | Over Non-hierarchical Low delay B Main 10 with Intra period = 32 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B |  |  |  |  | 
Class C | 5,98% | 6,92% | 7,37% | 133% | 
Class E | 16,46% | 15,95% | 20,39% | 143% | 
Overall |  |  |  |  | 
Class D | 5,92% | 11,44% | 12,52% | 130% | 
Class F (optional) | 11,85% | 12,24% | 12,60% | 148% | 

## Slide 8: Results: Intra Refresh with constraints
Significant losses, especially for low motion sequences.
Thank you very much to Fujitsu for crosschecking (JVET-L0637) and feedbacks => random accessibility OK.
JVET-L0160
 | Low delay B Intra Refresh Main10 |  |  |  | 
 | Over Non-hierarchical Low delay B Main 10 with Intra period = 32 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B |  |  |  |  | 
Class C | 22,14% | 32,03% | 34,76% | 130% | 
Class E | 71,91% | 98,70% | 108,36% | 159% | 
Overall |  |  |  |  | 
Class D | 24,57% | 41,63% | 46,01% | 140% | 
Class F (optional) | 53,14% | 58,97% | 61,11% | 164% | 

## Slide 9: Conclusion
An implementation of encoder-only Intra Refresh and associated testing conditions have been proposed.
Performance have been characterized:
  Significant losses of 20% in average on classical sequences and 60% for Class E and F.
  One quarter of the loss comes from forcing Intra CU itself.
A solution is desirable to bring this low-latency functionnality with reduced loss on VVC.
Recommendation:
  To add the proposed test conditions to CTC.
  To integrate encoder-only modfications within VTM software.
  To further improve the propsed implementation (assessment of Intra mode restrictions instead of CIP)
JVET-L0160

## Slide 10: Thank you
The research leading to this work has been supported by the FUI23 EFIGI project, BPIFrance and Region Ile de France.

## Slide 11: Update : Test condition for Intra Refresh
Basis: Low-Delay B configuration
Without pyramidal B structure
Intra Refresh period of 32 (as Random Access)
To deal with first Intra picture:
  PSNR and bitrates computed after first refresh (Pic 33)
  Or 1st picture repeated 33 times and then PSNR computed starting from Pic 33 (for same amount of pictures as others tests)
JVET-L0160