## Slide 1: JVET-L0207 CE 4 related: simplified non-sub-block STMVP
July 2018
F. Le Léannec - Technicolor

## Slide 2: Non-sub-block STMVP introduced in JVET-K0532
  JVET-K0532:
  Test CE4.4.1:
  STMVP candidate = Average of the 1, 2 or 3 found available MV

## Slide 3: Observations on non-sub-block STMVP
  Most of the coding gain comes from using the averaged spatial MV predictor.
  The temporal MV predictor brings about 0.1% gain. Can be improved through slight modification of TMVP derivation.
  STMVP gain not sensitive to the position of the spatial MVPs. The spatial positions that give most gain are the left-middle (Lmid) and above-middle (Amid)
  Considering several spatial positions on the left and above is almost useless. Gain very slightly affected by removing “Afar” and “Lfar” from the process.

## Slide 4: Proposed method
  Goal:
    Reduce the number of candidate positions to construct STMVP candidate
  Proposal:
    One single position above and on the left of current PU: Amid and Lmid
    Slightly modify the position of the temporal candidate:
    STMVP computed if at least 2 spatial-temporal candidate found
    ATMVP and STMVP moved to 3rd position in the merge list

## Slide 5: Results over VTM-2.0.1
Merge list size=6
Merge list size=8

## Slide 6: Results over VTM-2.0.1
Merge list size=8 with 2 STMVP candidates
H
Amid
Lmid
(nPbW/2, -1)
(-1, nPbH/2)
STMVP candidate 1
STMVP candidate 2

## Slide 7: Further simplification (2nd method)
(nPbW-1, -1)
B1
A1
(-1, nPbH-1)
Goal: share candidates with usual merge modes
  The spatial MV predictor positions A1 and B1 are used instead of Amid and Lmid.
  The modified TMVP predictor derivation, described in section 2.1, is also applied in the usual TMVP merge mode.
    This reduces the number of temporal predictors from 2 to 1 in the worst-case scenario of the decoding process.

## Slide 8: Results over VTM-2.0.1 (2nd method)
Merge list size=6
Merge list size=8

## Slide 9: Results over VTM-2.0.1 (2nd method)
Merge list size=8 with 2 STMVP candidates
H
B1
A1
STMVP candidate 1
STMVP candidate 2

## Slide 10: Combination with HMVP (CE4.4.7+STMVP)
Merge list size=6, HMVP only in merge mode
Merge list size=6, HMVP applied in AMVP and merge

## Slide 11: Combination with Long-distance Merge and HMVP (CE4.4.2+CE4.4.7+STMVP)
Merge list size=10, HMVP applied in merge only
Merge list size= 10, HMVP applied in AMVP and merge

## Slide 12: Combination with Long-distance Merge and HMVP (CE4.4.2+CE4.4.7+STMVP)
Merge list size=10, HMVP applied in merge only, 2 STMVP candidates
Merge list size= 10, HMVP applied in AMVP and merge, 2 STMVP candidates

## Slide 13: Conclusion
  2 modified STMVP methods are proposed
  Proposal is 2nd proposed method with 2 STMVP candidates (coding efficiency/changes to VTM)