## Slide 1
JVET-L0242 AHG9:Dense Residual Convolutional Neural Network (DRN) based In-Loop Filter
Yingbin Wang, Zhenzhong Chen, Yiming Li (Wuhan University)
Liang Zhao, Shan Liu, Xiang Li (Tencent)

## Slide 2: Summary
A simplified network architecture for CNNIF is proposed.
The proposed method has less than 3% number of parameters compared with the proposal JVET-K0391
2.34%/1.61%/2.14% BD-rate savings for Y/Cb/Cr when compared with VTM 2.0.1 under AI configuration.

## Slide 3: Introduction
Encoder framework of VTM 2.0.1
Trans./ Quant.
Entropy
Coder
SAO
DBF
Input
frame
Recon.
frame
Bitstreams
Inter
Predictor
Intra
Predictor
Inv. Trans.
& Quant.
Split into
CTUs
+
-
+
+
In-loop filters
Predictor
Quant. Trans. Coeff.
Prediction Data
Filter Ctrl. Data
DRN
ALF

## Slide 4
Network structure of DRN (in JVET-K0391)
N: the number of DRU
M: the number of the feature maps generated by the convolutional layer
Proposed Method
CONV 3×3×M
···
CONV 1X1XM
CONV 1X1XM
CONV 1X1XM
CONV 3X3XM
ReLU
CONV 3X3XM
CONV 3X3XM
ReLU
CONV 3X3XM
CONV 3X3XM
ReLU
CONV 3X3XM
CONV 3X3XM
ReLU
CONV 3X3XM
N×DRU
CONV 3×3×M
CONV 3×3×M
CONV 3×3×M

## Slide 5
Network structure of DRN (in this contribution)
N: the number of DRU
M: the number of the feature maps generated by the convolutional layer
Proposed Method

## Slide 6
Main changes:
Proposed Method
the 3x3 convolutional layers outside the global identity skip connection are removed
normalized QP map is concatenated with the rec.
the number of DRU is reduced from 8 to 4 and CNN kernel is reduced from 64 to 32

## Slide 7
Dense Residual Unit (DRU)
Proposed Method
DSC 3×3×M
ReLU
DSC 3×3×M
CONV 1×1×M

## Slide 8
Main changes:
Proposed Method
3x3 conventional convolutional layer is replaced by 3x3 depth-wise separable convolutional (DSC) layer in each DRU.
After the above modifications, the total number of the model parameters in this contribution is 22K compared to 810K in K0391.

## Slide 9
Training details
Proposed Method
Trained and validated on DIV2K dataset [1].
The images in DIV2K dataset are converted from RGB color space to YUV color space before compression.
The high-quality images are compressed by VTM2.0.1 using different QPs (22, 27, 32 and 37) under All Intra (AI) configuration.
[1] E. Agustsson and R. Timofte, “NTIRE 2017 challenge on single image super-resolution: dataset and study,” in Proc. IEEE Int. Conf. Computer Vision and Pattern Recognition Workshops (CVPRW), July 2017.

## Slide 10
Block-level on/off control
Proposed Method
DRN
RDO
DF
SAO
Reconstruction
Filtered Reconstruction
Block-level on/off flags
Entropy
Coder
Bitstreams
Divided into Blocks
Divided into Blocks

## Slide 11
BD-rate results of the proposed scheme (N=4, M=32, DSC)
Experimental Results
Results for AI Main10 VS VTM2.0.1
 | Over VTM-2.0.1 All Intra Main 10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -1.56% | -2.21% | -4.20% | 102% | 755%
Class A2 | -1.89% | -1.24% | -0.83% | 102% | 594%
Class B | -1.45% | -1.71% | -2.47% | 102% | 811%
Class C | -3.08% | -1.92% | -1.75% | 102% | 755%
Class E | -4.06% | -0.81% | -1.39% | 102% | 922%
Overall | -2.34% | -1.61% | -2.14% | 102% | 765%
Class D | -3.74% | -2.13% | -2.41% | 102% | 1100%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
Notes: This is the performance in GPU platform

## Slide 12
BD-rate results of the proposed scheme (N=4, M=32, DSC)
Experimental Results
Results for AI Main10 VS VTM2.0.1(CPU only)
 | Over VTM-2.0.1 All Intra Main 10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -1.56% | -2.21% | -4.20% | 124% | 6611%
Class A2 | -1.89% | -1.24% | -0.83% | 110% | 3818%
Class B | -1.45% | -1.71% | -2.47% | 108% | 5120%
Class C | -3.08% | -1.92% | -1.75% | 107% | 6914%
Class E | -4.06% | -0.81% | -1.39% | 117% | 11210%
Overall | -2.34% | -1.61% | -2.14% | 112% | 6198%
Class D | -3.74% | -2.13% | -2.41% | 105% | 6635%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!

## Slide 13
BD-rate results with LD, RA configuration
Experimental Results
 | Low delay B Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class C | -2.08% | -5.05% | -3.88% | 101% | 1350%
Class E | -3.91% | -1.59% | -2.60% | 103% | 1371%
Class D | -2.64% | -2.89% | -3.17% | 102% | 1207%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class C | -2.41% | -2.74% | -2.26% | 101% | 1418%
Class E |  |  |  |  | 
Class D | -3.03% | -2.52% | -2.51% | 101% | 1251%

## Slide 14
1. Compared with the last proposal
 | N | M | C | W | S | DSC
Test 1 | 8 | 64 | RGB | 1:1:1 | F | F
Test 2 | 8 | 64 | YUV | 10:1:1 | T | F
Test 6 | 4 | 32 | YUV | 10:1:1 | T | F
Test 9 | 4 | 32 | YUV | 10:1:1 | T | T
Further Experiments
*Test 1: The network in [1]
*Test 9: Proposal
N, M: the number of DRU, convolution kernel;
C, W: the color space of the training materials, and the weights of components;
S: different structure from JVET-K0391;
DSC: 3x3 depth-wise separable convolution.

## Slide 15
1. Compared with the last proposal
Test 1: N=8, M=64, DSC=False, C=RGB, W=1:1:1, S=False (812K Param.)
 | All Intra Main10 |  | 
 | Over VTM-2.0.1 |  | 
 | Y | U | V
Class A1 | -1.68% | -9.90% | -9.89%
Class A2 | -2.18% | -12.90% | -9.91%
Class B | -2.07% | -11.85% | -13.54%
Class C | -4.23% | -13.59% | -16.59%
Class E | -5.40% | -11.84% | -14.94%
Overall | -3.06% | -12.09% | -13.24%
Class D | -4.82% | -13.71% | -17.87%
 | All Intra Main10 |  | 
 | Over VTM-2.0.1 |  | 
 | Y | U | V
Class A1 | -3.10% | -6.99% | -8.76%
Class A2 | -3.56% | -11.77% | -8.96%
Class B | -3.14% | -9.63% | -10.81%
Class C | -5.58% | -11.58% | -13.70%
Class E | -5.97% | -11.00% | -14.66%
Overall | -4.42% | -9.90% | -10.98%
Class D | -5.97% | -11.00% | -14.66%
Test 2: N=8, M=64, DSC=False, C=YUV, W=10:1:1, S=True (739K Param.)
Further Experiments

## Slide 16
2. BD-rate result of Test6
 | All Intra Main10 |  | 
 | Over VTM-2.0.1 |  | 
 | Y | U | V
Class A1 | -1.97% | -3.10% | -3.39%
Class A2 | -2.18% | -4.55% | -2.52%
Class B | -1.83% | -4.08% | -4.36%
Class C | -3.76% | -4.70% | -5.65%
Class E | -4.81% | -3.07% | -4.09%
Overall | -2.84% | -3.97% | -4.13%
Class D | -4.34% | -5.00% | -6.57%
Further Experiments
Test 6: N=4, M=32, DSC=False, C=YUV, W=10:1:1, S=True (85K Param.)

## Slide 17
3. BD-rate result of Test 9
 | All Intra Main10 |  | 
 | Over VTM-2.0.1 |  | 
 | Y | U | V
Class A1 | -1.56% | -2.21% | -4.20%
Class A2 | -1.89% | -1.24% | -0.83%
Class B | -1.45% | -1.71% | -2.47%
Class C | -3.08% | -1.92% | -1.75%
Class E | -4.06% | -0.81% | -1.39%
Overall | -2.34% | -1.61% | -2.14%
Class D | -3.74% | -2.13% | -2.41%
Further Experiments
Test 3: N=4, M=32, DSC=True, C=YUV, W=10:1:1, S=True (22K Params)

## Slide 18
  Influence of the performance when parameters decrease
Experimental Results
Chart: The ratio of parameters
| 1.0991939140851839
n8m64ORG | 0.030592
n8m32 | 0.036808
n4m64 | 0.033034
n4m32 | 0.028381
n4m32DW | 0.023394
n8m64 | 0.04419

## Slide 19
Proposed a new network architeceture for CNNIF. The proposed method has less than 3% number of parameters when compared with the proposal in last meeting (K0391)
2.34%/1.61%/2.14% BD-rate savings for Y/Cb/Cr when compared with VTM 2.0.1 under AI configuration. The decoding time is much faster than the proposal in last meeting.
It is suggest to further study.
Thank Hikvision for cross-check
Conclusion

## Slide 20
Thank You!