## Slide 1: JVET-L0256 CE9-related: Complexity reduction and bit-width control for bi-directional optical flow (BIO)
Xiaoyu Xiu, Yuwen He, Yan Ye
InterDigital Communications, Inc.
October, 2018

## Slide 2: Introduction
The BIO design in the BMS-2.1
  Enhancing both the granularity and the accuracy of the motion vectors (MVs) at motion compensation (MC)
Complexity issues of the current BIO:
  The implementation requires large multiplier and high bit-widths for intermediate parameters
  The interpolation of extended samples significantly increase the worst-case complexity, e.g., multiplications and additions
  Proposal
  BIO bit-width control: 15-bit multiplier and intermediate value are within 32-bit
  BIO complexity reduction: making the BIO worst-case complexity at the same level as that of regular bi-prediction

## Slide 3: BIO bit-width analysis
The extreme bit-width
  It happens at the calculation of the vertical motion refinement
42-bit
9-bit
33-bit
  The BMS2.1 BIO needs 33-bit multiplier and maximal bit-width of 43-bit for intermediates

## Slide 4: BIO complexity analysis
The BIO worst-case complexity
  The peak complexity increase comes from 4x4 bi-pred
  The number of multiplication is 353% of that of 4x4 bi-prediction.

## Slide 5: BIO complexity analysis
The BIO worst-case complexity
  The peak complexity increase come from 4x4 bi-pred
  The number of multiplication is 429% of that of 8x8 bi-prediction.

## Slide 6: Proposed bit-width control
Introduce additional right shifts to some BIO parameters for reducing overall internal bit-width
Remove internal bit-width increase in the original BIO in BMS-2.1
Modify the derivation of the motion refinement

## Slide 7: Proposed bit-width control
4-bit
15-bit
12-bit
  15-bit multiplier is guaranteed
  The internal bit-width of the whole BIO process does not exceed 32-bit
4-bit
The extreme bit-width
  It happens at the calculation of the vertical motion refinement

## Slide 8: Proposed BIO complexity reduction
Reduce the number of extended samples to one single row/column on each CU boundary
Use bilinear filters to replace 8-tap filters for generating extended samples
  Pad the sample values and gradients of CU boundary positions to extended positions

## Slide 9: Complexity analysis
  The peak complexity increase comes from 8x8 bi-pred
  The number of multiplication is 103% of that of 4x4 bi-prediction.

## Slide 10: Complexity analysis
  The peak complexity increase comes from 8x8 bi-pred
  The number of multiplication is 134% of that of 8x8 bi-prediction.

## Slide 11: Simulation results
11
© 2018 InterDigital, Inc. All Rights Reserved.
Anchor: BMS-2.1 with VTM configuration
Test | Y | U | V | Enc | Dec
BMS-2.1 BIO | -1.41% | -0.58% | -0.40% | 103% | 119%
Bit-width control | -1.38% | -0.52% | -0.37% | 103% | 109%
Complexity reduction | -1.31% | -0.53% | -0.40% | 103% | 113%
Bit-width control & Complexity reduction | -1.28% | -0.52% | -0.37% | 102% | 102%