## Slide 1: CE6-related: Unification of Transform Skip mode and MTS (JVET-L0289)
X. Zhao, X. Li, S. Liu ( Tencent )
2018/10

## Slide 2: Problem statement
Separate syntax for Transform Skip mode and MTS, but both coding tools are designed for transform selection
Separate quantization schemes are used for MTS and Transform Skip mode
For 4x2 and 2x4 blocks, Transform Skip may need multiplication and shift, which is lossy

## Slide 3: Proposed method
Replace 4-pt DST-7/DCT-b by 4-pt IDTR
TS and MTS signaling is unified in a way that TS mode becomes one MTS candidate
{DST-7, DST-7}, {DST-7, IDTR}, {IDTR, DST-7}, {IDTR, IDTR}
{ 512 0 0 0 }
{ 0 512 0 0 }
{ 0 0 512 0 }
{ 0 0 0 512 }

## Slide 4: Results
CTC
CTC, w/ inter MTS

## Slide 5: Conclusion
4-pt MTS is simplified by replacing 4-pt DCT-8 with shifting
TS and MTS is unified, the quantization process is unified
Draft text is simplified
It is proposed to adopt this proposal