## Slide 1
Reduced context models for transform coefficients coding (JVET-L0316)
Min Gao, Xiang Li, Shan Liu

## Slide 2
Syntax elements:
  sig_coeff_flag, par_level_flag, rem_abs_gt1_flag, rem_abs_gt2_flag
  abs_remainder
Separate scan pass coding:
  The first pass:
    sig_coeff_flag, par_level_flag, rem_abs_gt1_flag
  The second pass:
    rem_abs_gt2_flag
  The third pass:
    abs_remainder
Context Model:
The Current Transform Coefficient Coding
d = x + y
sumAbs = sum of absolute values in local neighbourhood (template)
sumAbs1 = sum of partially reconstructed absolute levels after first pass
numSig = number of transform coefficients with sig_coeff_flag == 1

## Slide 3
Context Model:
  sig_coeff_flag:
  par_level_flag, rem_abs_gt1_flag, rem_abs_gt2_flag:
The Current Transform Coefficient Coding
ctxIdSig = 18 * max(0, state−1) + min( sumAbs1, 5 ) + ( d < 2 ? 12 : ( d < 5 ? 6 : 0 ) )
ctxIdSig = 12 * max(0, state−1) + min( sumAbs1, 5 ) + ( d < 2 ? 6 : 0 ) ) (Chroma)
ctxIdPar = 1 + min( sumAbs1 – numSig, 4 ) +
( d == 0 ? 15 : ( d < 3 ? 10 : ( d < 10 ? 5 : 0 ) ) )
ctxIdPar = 1 + min( sumAbs1 – numSig, 4 ) + ( d == 0 ? 5 : 0 ) (Chroma)
ctxIdGt1 = ctxIdPar ctxIdGt2 = ctxIdPar

## Slide 4
Reduced context model for transform coefficients:
  Share the context models among some coefficients:
    Luma (par_level_flag, rem_abs_gt1_flag, rem_abs_gt2_flag):
    Chroma (par_level_flag, rem_abs_gt1_flag, rem_abs_gt2_flag):
The Proposed Method
Diagonal position | Context model index
d=0 | 16, 17, 18, 19, 20
d<3 | 11, 12, 13, 14, 15
d<10 | 6, 7, 8, 9, 10
d>=10 | 1, 2, 3, 4, 5
Last non-zero coefficient | 0
Diagonal position | Context model index
d=0 | 6, 7, 8, 9, 10
d>0 | 1, 2, 3, 4, 5
Last non-zero coefficient | 0

## Slide 5
Anchor VTM-2.0.1
Experimental Results:

## Slide 6
Share the context models among the transform coefficients to reduce the context models.
The proposed method can save 12 context models in total, at the cost of minor coding loss.
  The BD rate loss is 0.02%, 0.02%, 0.02% for AI, RA and LD configurations, respectively.
Conclusions:

## Slide 7
Thanks to MTK for cross-check!