## Slide 1: CE4-related: affine merge mode with prediction offsets JVET-L0320
G. Li, X. Xu, X. Li, S. Liu
2018/10

## Slide 2: Introduction
Merge Candidates in VTM-2.0.1 Affine Merge Common Base includes
  Inherited Model-based merge candidates
  Constructed control-point based candidates
  Zero motion vectors padding
There’s room for further improvement on top of the current affine merge
Affine merge with prediction offset is proposed

## Slide 3: Proposed Method
Based on VTM-2.0.1 Affine Merge Common Base
First affine merge candidate used as Base Predictor
Base Predictor’s Inter prediction direction is used
Currently use 4-parameter model for all candidates
  Only 2 Control Points used from Base Predictor
  Offset applied to each control point separately
  A zero_MVD flag to indicate offset to be applied

## Slide 4: Proposed Method
Distance IDX | 0 | 1 | 2 | 3 | 4
Distance-offset | 1/2-pel | 1-pel | 2-pel | 4-pel | 8-pel
Offset Direction IDX | 00 | 01 | 10 | 11
x-dir-factor | +1 | –1 | 0 | 0
y-dir-factor | 0 | 0 | +1 | –1
Offset Direction: only on X or Y direction
Distance Offset: 5 magnitude values
Uni-prediction Affine Case
  Signaled Distance Offset applied on signaled direction
Bi-prediction Affine Case
  L0: Signaled Distance Offset applied on signaled direction
  L1: Signaled Distance Offset applied on opposite direction

## Slide 5: Simulation results
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-2.0.1 Affine Merge Common Base |  |  |  |  | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.41% | -0.37% | -0.32% | 134% | 104% | -1.37% | -0.95% | -1.21% | 139% | 111%
Class A2 | -0.47% | -0.46% | -0.52% | 144% | 104% | -1.47% | -1.44% | -1.65% | 152% | 111%
Class B | -0.33% | -0.21% | -0.27% | 140% | 103% | -1.00% | -0.77% | -0.97% | 153% | 112%
Class C | -0.12% | -0.12% | -0.16% | 138% | 101% | -0.60% | -0.57% | -0.70% | 157% | 123%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | -0.32% | -0.27% | -0.30% | 139% | 103% | -1.06% | -0.89% | -1.08% | 151% | 114%
Class D | -0.07% | 0.03% | 0.09% | 143% | 104% | -0.75% | -0.64% | -0.69% | 162% | 135%
Class F (optional) | -0.08% | -0.04% | -0.14% | 129% | 101% | -0.22% | -0.22% | -0.28% | 142% | 114%
 | Low delay B Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-2.0.1 Affine Merge Common Base |  |  |  |  | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 |  |  |  |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  |  |  |  | 
Class B | -0.11% | -0.19% | 0.16% | 145% | 100% | -0.11% | -0.19% | 0.16% | 145% | 100%
Class C | -0.03% | 0.02% | -0.24% | 142% | 105% | -0.03% | 0.02% | -0.24% | 142% | 105%
Class E | -0.12% | -0.34% | -1.02% | 156% | 102% | -0.12% | -0.34% | -1.02% | 156% | 102%
Overall | -0.09% | -0.16% | -0.27% | 147% | 102% | -0.09% | -0.16% | -0.27% | 147% | 102%
Class D | 0.11% | 0.58% | -0.27% | 140% | 100% | 0.11% | 0.58% | -0.27% | 140% | 100%
Class F (optional) | -0.14% | -0.31% | -0.09% | 133% | 102% | -0.14% | -0.31% | -0.09% | 133% | 102%
Anchor: VTM-2.0.1 with Affine Merge Common Base
2nd Reference: VTM-2.0.1

## Slide 6: Simplification of Proposed Method
To reduce the signaling overhead by signaling the distance offset index and the offset direction index per block.
The same offset will be applied to all control points in the same way.
3 control points for 6-parameter type;
The zero_MVD flag is not used in this method.

## Slide 7: Simplification test results
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-2.0.1 Affine Merge Common Base |  |  |  |  | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.56% | -0.44% | -0.45% | 103% | 96% | -1.52% | -1.03% | -1.33% | 106% | 103%
Class A2 | -0.72% | -0.64% | -0.72% | 105% | 96% | -1.72% | -1.61% | -1.85% | 111% | 103%
Class B | -0.42% | -0.39% | -0.35% | 102% | 89% | -1.09% | -0.95% | -1.04% | 112% | 97%
Class C | -0.12% | -0.03% | -0.11% | 102% | 81% | -0.60% | -0.49% | -0.65% | 116% | 99%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | -0.43% | -0.35% | -0.38% | 103% | 89% | -1.17% | -0.98% | -1.16% | 112% | 100%
Class D | -0.08% | -0.13% | 0.10% | 103% | 79% | -0.76% | -0.80% | -0.67% | 117% | 103%
Class F (optional) | -0.11% | -0.09% | -0.14% | 100% | 83% | -0.25% | -0.27% | -0.28% | 109% | 94%
 | Low delay B Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-2.0.1 Affine Merge Common Base |  |  |  |  | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 |  |  |  |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  |  |  |  | 
Class B | -0.17% | -0.26% | 0.17% | 107% | 93% | -0.56% | -0.54% | -0.47% | 114% | 96%
Class C | -0.07% | -0.04% | -0.17% | 102% | 87% | -0.43% | -0.42% | -0.43% | 112% | 93%
Class E | -0.20% | -0.12% | -0.63% | 105% | 86% | -0.83% | -0.75% | -0.82% | 117% | 95%
Overall | -0.15% | -0.15% | -0.14% | 105% | 89% | -0.58% | -0.56% | -0.54% | 114% | 95%
Class D | 0.09% | 0.61% | -0.09% | 101% | 77% | -0.51% | 0.18% | -0.68% | 115% | 94%
Class F (optional) | -0.13% | -0.35% | 0.13% | 100% | 84% | -0.22% | -0.15% | 0.12% | 109% | 90%
Anchor: VTM-2.0.1 with Affine Merge Common Base
2nd Reference: VTM-2.0.1

## Slide 8: Conclusion
Proposed affine merge mode with prediction offset method provides BD-rate gain on top of Affine Merge Common Base
  0.32% on RA, 0.09% on LDB
There’s potential for further improvement, an improved version has BD-rate gain of
  0.43% on RA, 0.15% on LDB
It is proposed to further study the proposed method in core experiments.