## Slide 1: JVET-L0333 CE9-related: Motion Vector Refinement in Bi-directional Optical Flow
Hongbin Liu, Li Zhang, Kai Zhang, Yue Wang, Pengwei Zhao, Dingkun Hong

## Slide 2: Summary
Motivation
  In bi-directional optical flow (BIO), optical flow are derived to improve prediction of the CU, however, they are not used to refine motion vector of the CU.
  In CE9, partial removal of the latency caused by motion vector refinement is studied and it can bring some coding gain.
Proposed solution
  Refine motion vector of the CU by adding the scaled optical flow to it.
  It can achieve -0.63% BD-rate reduction.
Thanks Samsung for crosschecking

## Slide 3: Proposed Method
Optical flow derived in BIO: (DMVx, DMVy)
Proposed method

## Slide 4: Simulation results
Anchor: BMS-2.1 + VTM configuration
Tested: BMS-2. 1 + VTM configuration + proposed method
 | Random Access Main 10 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.47% | -0.32% | -0.43% | 101% | 100%
Class A2 | -1.03% | -0.92% | -1.02% | 99% | 98%
Class B | -0.57% | -0.42% | -0.46% | 101% | 101%
Class C | -0.52% | -0.34% | -0.46% | 102% | 105%
Class E |  |  |  |  | 
Overall | -0.63% | -0.48% | -0.56% | 101% | 102%
Class D | -0.80% | -0.50% | -0.72% | 101% | 104%

## Slide 5: Conclusion
This contribution uses optical flow to refine motion vector of the CU. It achieves -0.63% BD-rate reduction.
Suggest to study it in CE.

## Slide 6
Thanks！