## Slide 1: JVET-L0341：CE3-related: CCLM coefficients derivation method without down-sampling operation
X. Ma, H. Yang, J. Chen
Huawei Technologies Co., Ltd

## Slide 2: Main points
Linear model coefficients derivation method without down-sampling
  without using 6-taps down-sampling filters to neighboring luma samples
  fetch the samples directly, from 1 line and 1 column.
  implement on simplified CCLM method
    Called MaxMin method, from JVET-K0204, JVET-L0191

## Slide 3: VTM2.0: down-sampling, 2 lines, 3 columns
Luma template samples deriving method in VTM2.0
  6-taps down-sampling filter (bi-linear).
  2 lines, 3 columns, for down-sampling.

## Slide 4: Proposed: no-sampling, 1 line, 1 column
Proposed: Luma template samples deriving method
  no down-sampling filter, fetch directly.
  1 line (the first top line), 1 column(the second left column).

## Slide 5: Experimental results
Implement on MaxMin method.

## Slide 6: Further comparison
Comparisons
Thank ITRI for cross-checking
 | AI |  |  | RA |  | 
 | Y | U | V | Y | U | V
CCLM (tool off, JVET-L0013) | 2.15% | 16.75% | 15.49% | 1.00% | 15.45% | 14.35%
MaxMin (JVET-L0191) | 0.11% | 0.48% | -0.02% | 0.08% | 0.78% | 0.19%
MaxMin+Proposed | 0.26% | 1.81% | 1.18% | 0.15% | 2.01% | 1.29%