## Slide 1: JVET-L0359 AHG12: Flexible Tile Partitioning
Yukinobu Yasugi Tomohiro Ikai
Sharp Corporation
Follow up of JVET-K0155:
AHG12: Flexible Tile Partitioning

## Slide 2: Problem statement
Tile partitioning using CTU unit basis
  In HEVC, tile sizes is restricted to be multiples of CTU except for picture boundary
  Problems:
    Difficulty in load balancing
    Difficulty in fitting regions (e.g. ROI, frame-packing etc.)
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
ctuRsAddr=
Unit of tile (CTU)

## Slide 3: Proposal
Tile partitioning using CTU basis with non-multiple of CTU boundary
  CTU splitting is used as usual
    Allow non-multiple of CTU boundary (i.e. incomplete CTU) for the right and bottom side for each tile
    the same as picture boundary
  Benefits:
    Better load balance
    Better fitting to regions
0
1
2
3
4
5
6
ctuRsAddr=
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
31
Unit of tile

## Slide 4: Proposal
Signal a syntax element in PPS
  tile_unit_size_idc
    0: CtbSizeY
    1: CtbSizeY>>1
    2: CtbSizeY>>2
    …
    …: 8
  TileUnitSize = Max(CtbSizeY >> tile_unit_size_idc, 8)
  Proposed minimum tile unit size: 8x8
    hardware needs multiply to 8 for efficient memory allocation
    good load balancing
derive tile size by column_width_minus1 / row_row_minus1 or uniform splitting with the unit of TileUnitSize
… | 
if ( tile_enabled_flag ) { | 
num_tile_columns_minus1 | ue(v)
num_tile_rows_minus1 | ue(v)
uniform_spacing_flag | u(1)
tile_unit_size_idc | ue(v)
if ( !uniform_spacing_flag ) { | 
for ( i=0; i < num_tile_columns_minus1: i++ ) | 
column_width_minus1[i] | ue(v)
for ( i=0; i < num_tile_rows_minus1: i++ ) | 
row_height_minus1[i] | ue(v)
} | 
loop_filter_across_tiles_enabled_flag | u(1)
} | 
… | 
alternative: 16x16 or minCTUsize

## Slide 5: Proposal
We prepared a tile implementation
  ALF is also supported (which lacks in the current VTM)
    Now All loop filters can be controlled by LFCrossTileBoundaryFlag
      DF, SAO and ALF
    Note: VTM has a basic tile implementation with HEVC_TILES_WPP but several missing parts exist.
  Friendly implementation for (more) flexible tile
  Clean implementation
    valgrind check was done (e.g. for ALF SIMD alignment bug fix)

## Slide 6: Partitioning
An example of partitioning:
RandomAccess-BQMall-QP37, POC8
CU CTU Tile

## Slide 7: Experimental results (without paddings)
Totally, losses with multiple of non-CTU size is small in 16x16 and 32x32 unit, the loss of 8x8 unit is also acceptable level.
Recalculated BD-rates without CABAC-zero-word paddings

## Slide 8: Conclusion
Propose a flexible tile partitioning
  provide finer tile size unit by allowing boundary for each tile
  8x8 basis as minimum
Experiment results
  The average coding performance is similar to HEVC tile
    0.69% loss while HEVC/conventional partitioning shows 0.67%
  No additional loss due to finer partitioning in 32x32 unit.
It is suggested
  to adopt the proposed tile partitioning in the next WD and VTM/reference software
  to continue to study tile structure