## Slide 1: CE10-related: inter prediction sample filtering
Weiwei Xu, Haitao Yang, Yin Zhao and Jianle Chen
Huawei Technolgoies
JVET-L0375

## Slide 2: Proposed method
Test 1: Filter skip/merge prediction with 2 spatial rec. samples
  P(x,y) = ( L(-1,y) + A(x,-1) + 6 *pred(x,y) + 4) >> 3
Test 3: Filter skip/merge prediction with intra Planar predictors (4 samples)
  Simplification on CE10.1.1c in JVET-L0100 in which four intra prediction modes are used, also mode-dependent weighting, size-dependent mode list…
  P(x,y) = ( H(x,y) + V(x,y) + 2 *pred(x,y) + 2) >> 2
  A flag is signaled in skip/merge mode whether inter prediction is combined with Planar prediction
H(x,y) and V(x,y) are horizontal and vertical planar predictors
JVET-L0375

## Slide 3: Simulation results
Test 1:
Test 3:
 | Random Access Main 10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.27% | 0.03% | -0.19% | 105% | 100%
Class A2 | -0.28% | -0.22% | -0.39% | 106% | 100%
Class B | -0.34% | -0.19% | -0.19% | 105% | 100%
Class C | -0.27% | -0.07% | -0.23% | 106% | 100%
Class E |  |  |  |  | 
Overall | -0.30% | -0.12% | -0.24% | 105% | 100%
Class D | -0.12% | -0.19% | -0.37% | 106% | 100%
Class F | -0.32% | -0.25% | -0.27% | 104% | 100%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.50% | -0.02% | -0.30% | 106% | 102%
Class A2 | -0.41% | -0.25% | -0.54% | 107% | 101%
Class B | -0.54% | -0.29% | -0.23% | 107% | 102%
Class C | -0.44% | -0.16% | -0.41% | 107% | 101%
Class E |  |  |  |  | 
Overall | -0.48% | -0.19% | -0.35% | 107% | 102%
Class D | -0.27% | -0.16% | -0.14% | 106% | 101%
Class F | -0.27% | -0.15% | -0.16% | 106% | 101%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.45% | -0.29% | -0.30% | 107% | 102%
Class A2 | -0.44% | -0.46% | -0.65% | 109% | 103%
Class B | -0.57% | -0.49% | -0.46% | 108% | 103%
Class C | -0.53% | -0.37% | -0.60% | 110% | 105%
Class E |  |  |  |  | 
Overall | -0.51% | -0.41% | -0.50% | 108% | 103%
Class D | -0.33% | -0.23% | -0.48% | 110% | 103%
Class F | #VALUE! | #VALUE! | #VALUE! | 100% | 100%
Results of CE10.1.1.c: Multi-hypothesis prediction for intra and inter mode
JVET-L0375

## Slide 4: Conclusion
Filter inter prediction samples with two spatial rec. samples achieves -0.30% gain
Filter inter prediction samples with two intra Planar predictors (4 spatial rec. samples) achieves -0.48% gain
  Compared to using four intra prediction modes, the proposed method almost has no loss (0.03% BD-rate in RA)
It is recommended to study the proposed method in CE10
JVET-L0375