## Slide 1: CE4-related: Affine restriction for the worst-case bandwidth reduction (JEVT-L0396)
Luong Pham Van, Wei-Jung Chien, Han Huang, Vadim Seregin, Marta Karczewicz

## Slide 2: Introduction
Affine motion compensation (MC)
  6 parameter affine model
  4-parameter affine model
() is the motion vector (MV) at the coordinate ()

## Slide 3: Issues and proposed
Issues: worst-case bandwidth
MV difference of control points leads to non-overlapped fetching
 Memory bandwidth is greatly high
Proposal:
  For each affine block, use control points difference to determine the subblock size
  Subblock size is 4x4 only when the control points difference meets the condition.
Fetched block including pixels for interpolation
Current blocks

## Slide 4: Proposed constraint for worst-case bandwidth reduction
General rule:
  Control points satisfies the constraint:
   Sub-lock size is 4x4
  Otherwise, sub-block size = 8x8
  The constraints are different for each bandwidth reduction level
The constraint can be adaptively applied for Uni-prediction and Bi-prediction

## Slide 5: Proposed1: Worst-case achieves INTER_8x4/INTER_4x8
Constraint for worst-case bandwidth to achieve an INTER_8x4 or INTER_4x8:
Where Norm(v1) = v1*128/w, Norm(v2) = v2*128/h
15
11
Example of worst case bandwidth achieving an INTER_4x8 (CU size = 8x8)

## Slide 6: Proposed2: Worst-case achieves INTER_9x9
Restriction for worst-case bandwidth achieve an INTER_9x9
16
16
A = , B = ,
C= , D =
pel = Norm factor * motion precision = 128*16
Proposed restriction:
( -4 *pel < A < pel ) && ( - pel < B < pel ) &&
( -pel < C < pel ) && ( - 4*pel < D < pel ) &&
(-4*pel < (A+C) < pel) && (-4*pel < (B+D) < pel )
Example of worst case bandwidth of an 8x8 CU achieving an INTER_9x9

## Slide 7
Test a: Worse case bandwidth equal to 4x8/8x4 Bi-prediction and Uni-prediction
 | Random Access Main 10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.05% | 0.02% | 102% | 115%
Class A2 | 0.04% | 0.04% | -0.07% | 97% | 100%
Class B | 0.01% | 0.04% | -0.07% | 82% | 93%
Class C | 0.00% | 0.06% | 0.04% | 96% | 98%
Class E |  |  |  |  | 
Overall | 0.01% | 0.05% | -0.02% | 92% | 100%
Class D | 0.00% | -0.04% | 0.03% | 96% | 97%
Class F (optional) | 0.02% | 0.00% | 0.02% | 83% | 94%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.02% | 0.10% | 0.02% | 107% | 122%
Class C | 0.02% | 0.06% | -0.16% | 113% | 103%
Class E | -0.03% | -0.43% | -0.14% | 94% | 96%
Overall | 0.01% | -0.05% | -0.08% | 105% | 109%
Class D | -0.05% | 0.24% | 0.13% | 97% | 98%
Class F (optional) | -0.05% | 0.31% | 0.61% | 83% | 94%

## Slide 8: Test b: Bi-prediction: Worse case bandwidth equal to 9x9, Uni-prediction: sub-block size is 4x4
 | Random Access Main 10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.09% | 0.04% | 100% | 100%
Class A2 | 0.16% | 0.15% | 0.09% | 100% | 100%
Class B | 0.03% | 0.03% | 0.00% | 98% | 99%
Class C | -0.01% | 0.05% | 0.02% | 97% | 96%
Class E |  |  |  |  | 
Overall | 0.04% | 0.07% | 0.03% | 99% | 99%
Class D | 0.02% | -0.02% | 0.00% | 97% | 95%
Class F (optional) | 0.06% | 0.07% | 0.09% | 98% | 96%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.03% | -0.05% | -0.03% | 100% | 101%
Class C | -0.02% | -0.07% | -0.27% | 100% | 101%
Class E | -0.19% | -0.33% | -0.36% | 99% | 102%
Overall | -0.04% | -0.13% | -0.19% | 100% | 101%
Class D | 0.00% | 0.54% | -0.01% | 99% | 97%
Class F (optional) | -0.06% | 0.07% | 0.45% | 98% | 98%

## Slide 9: Test c: Bi-prediction: Worse case bandwidth equal to 9x9, Uni-prediction: Worse case bandwidth equal to 8x4
 | Random Access Main 10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | 0.08% | 0.06% | 101% | 100%
Class A2 | 0.18% | 0.17% | 0.05% | 99% | 99%
Class B | 0.01% | 0.08% | -0.07% | 99% | 100%
Class C | 0.00% | 0.16% | 0.05% | 98% | 98%
Class E |  |  |  |  | 
Overall | 0.03% | 0.12% | 0.01% | 99% | 99%
Class D | 0.02% | -0.05% | 0.02% | 98% | 97%
Class F (optional) | 0.09% | 0.13% | 0.13% | 99% | 97%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.01% | -0.06% | -0.39% | 100% | 102%
Class C | 0.03% | -0.04% | -0.18% | 99% | 101%
Class E | -0.19% | -0.07% | -0.35% | 99% | 99%
Overall | -0.03% | -0.06% | -0.31% | 100% | 101%
Class D | -0.01% | 0.73% | -0.10% | 100% | 98%
Class F (optional) | -0.02% | 0.22% | 0.22% | 99% | 99%

## Slide 10: Test c: Bi-prediction: Worse case bandwidth equal to 9x9 Uni-prediction: Worse case bandwidth equal to 8x4
 | Random Access Main 10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | 0.08% | 0.06% | 101% | 100%
Class A2 | 0.18% | 0.17% | 0.05% | 99% | 99%
Class B | 0.01% | 0.08% | -0.07% | 99% | 100%
Class C | 0.00% | 0.16% | 0.05% | 98% | 98%
Class E |  |  |  |  | 
Overall | 0.03% | 0.12% | 0.01% | 99% | 99%
Class D | 0.02% | -0.05% | 0.02% | 98% | 97%
Class F (optional) | 0.09% | 0.13% | 0.13% | 99% | 97%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.01% | -0.06% | -0.39% | 100% | 102%
Class C | 0.03% | -0.04% | -0.18% | 99% | 101%
Class E | -0.19% | -0.07% | -0.35% | 99% | 99%
Overall | -0.03% | -0.06% | -0.31% | 100% | 101%
Class D | -0.01% | 0.73% | -0.10% | 100% | 98%
Class F (optional) | -0.02% | 0.22% | 0.22% | 99% | 99%