## Slide 1: Angular Merge Prediction
Shunsuke Iwamura, NHK
JVET-L0411
Notes: ご紹介いただいたタイトルで、テレビ方式研究部の岩村が発表いたします。よろしくお願いします。

## Slide 2: Algorithm overview
Additional merge mode where sub-block MVs of current CU are copied from MVs of reconstructed block located in the specific direction.
Similar to intra angular prediction, but number of angular direction is 5 (bottom-left, left, above-left, above, above-right )
granularity :4x4 for small block, 8x8 for large block
Directions of MVs (inter_pred_idc and ref_idx) are also copied from the corresponding reconstructed block

## Slide 3
Additional syntax just after merge_flag
… | 
merge_flag | ae(1)
if (merge_flag) { | 
angular_merge_flag | ae(1)
if (angular_merge_flag) | 
angular_merge_idx | ae(v)
else | 
… | 
} | 
… | 
angular_merge_idx=0
angular_merge_idx=1
angular_merge_idx=2
angular_merge_idx=3
angular_merge_idx=4

## Slide 4: Results
 | RA results over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.20% | -0.08% | -0.22% | 108% | 102%
Class A2 | -0.10% | -0.23% | -0.32% | 111% | 100%
Class B | -0.09% | -0.08% | -0.19% | 111% | 98%
Class C | -0.06% | -0.17% | -0.17% | 112% | 100%
Class E |  |  |  |  | 
Overall | -0.10% | -0.13% | -0.21% | 111% | 100%
Class D | 0.03% | -0.18% | 0.01% | 114% | 102%
 | LD results over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.10% | -0.34% | -0.34% | 117% | 101%
Class C | -0.05% | -0.34% | -0.27% | 112% | 102%
Class E | -0.18% | 0.03% | 0.11% | 115% | 98%
Overall | -0.10% | -0.25% | -0.20% | 115% | 100%
Class D | -0.04% | 0.24% | -0.72% | 116% | 99%
Thanks Sharp for crosschecking
Encoder optimization similar to normal merge mode is curried out.
Separate list construction to the normal/affine merge list.
Num of full RD = 3
Rough mode decision to pick up more probable angular_merge_idx.

## Slide 5: Conclusion
Additional merge mode is introduce:
  Sub-block MVs are copied from MVs of reconstructed block located in the specific direction.
  No additional line buffer for MV storage
Recommend to study combination of other merge mode in CE

## Slide 6: Comparison of fast decision
all 5 candidates RD opt | RA | -0.13% | -0.19% | -0.29% | 123% | 101%
 | LD | -0.15% | -0.34% | -0.41% | 131% | 100%
3 candidates for RD opt | RA | -0.10% | -0.13% | -0.21% | 111% | 100%
 | LD | -0.10% | -0.25% | -0.20% | 115% | 100%