## Slide 1: JVET-L0420: CE3: Chroma intra prediction simplification (Test 2.4.1 and 2.4.2)
Chang-Hao Yau, Po-Han Lin, Ching-Chieh Lin, Bing-Jung Fuhand Chun-Lung Lin
Macao, CN
Oct 2018

## Slide 2: Outline
Observations
Proposed method
Results
Analysis
Conclusions

## Slide 3: Observations
For Chroma Intra coding, there are 6 coding modes
  DM, LM, Planar, DC, Vertical and Horizontal.
DM is the intra mode of the top-left luma block.
The chroma block could correspond to multiple luma blocks with the separate tree method.
Neighboring chroma intra coding modes are not used in the current VTM design
6 RDOs are applied to select the best mode in the current VTM design
Notes: To reduce the number of elements in the RDO list

## Slide 4: CE3-2.4.1: Enable MDMS
To use the multiple DMs and the neighboring coding mode by enabling MDMS
  Enable MDMS to replace Angular mode
5 MDMS candidates are used for signaling
The same number of RDO compared to the current VTM
Notes: To reduce the number of elements in the RDO list

## Slide 5: Results of CE3-2.4.1(over VTM)
0.20% luma gain
1.09% and 1.08% chroma gain
Notes: To reduce the number of elements in the RDO list

## Slide 6: CE3-2.4.2: Simplify the number of RDO checks
The encoder reorders the MDMS candidate list according to the SATD cost.
If the RDO cost is 1.05 times higher than the best RDO cost, the encoder stops calculating RDO cost.
Notes: To reduce the number of elements in the RDO list

## Slide 7: Results of CE3-2.4.2(over VTM)
3% encoder run-time saving
0.20%/0.84%/0.84% (Y/U/V) gain
Notes: To reduce the number of elements in the RDO list

## Slide 8: Results of CE3-2.4.2 (over CE3-2.4.1)
2% encoder run-time saving
0.00%/0.25%/0.23% (Y/U/V) loss
Notes: To reduce the number of elements in the RDO list

## Slide 9: Analysis
The complexity analysis results of the proposed method.
Notes: To reduce the number of elements in the RDO list

## Slide 10: Conclusions
Enabling MDMS and applying the fast encoder search to MDMS.
CE3-2.4.1
  0.20% / 1.09% / 1.08% (Y/U/V) gain
  without encoder run-time change
CE3-2.4.2
  3% encoder run-time saving
  0.20%/0.84%/0.84% (Y/U/V) gain

## Slide 11: Thank you!