## Slide 1: CE-6 related: Transform Simplification JVET-L0489
Christopher Hollmann, Per Wennersten, Jacob Ström, Rickard Sjöberg
Ericsson
VISTA Flow
BTEB ER DRI
2018-04-06

## Slide 2: Background
It has been mentioned several times at this meeting that encoder run time is too high.
Is it possible to reduce encoder run time overhead?
We have looked at Multiple Transform Selection (MTS) which was adopted at the last meeting
Approximate BD rate change:
  -3.3% / -2.0% /-1.3% (AI/RA/LDB)
Approximate run time:
  200% / 160% / 160% (AI/RA/LDB)

## Slide 3: Current encoder approach
For each block smaller than 64 in both dimensions:
  Try DST-7 in horizontal and DST-7 in vertical
  Try DST-7 in horizontal and DCT-8 in vertical
  Try DCT-8 in horizontal and DST-7 in vertical
  Try DCT-8 in horizontal and DCT-8 in vertical
  Try DCT-2 in horizontal and DCT-2 in vertical
Encoder signals whether DCT-2/DCT-2
  if not DCT-2/DCT-2 then:
    one bit for horizontal (DST-7/DCT-8)
    one bit for vertical (DST-7/DCT-8)
3.3%
BDR
100% extra encoder run time
AI compared to turning MTS off:

## Slide 4: Non-normative test: Skip test of DCT-8
For each block smaller than 64 in both dimensions:
  Try DST-7 in horizontal and DST-7 in vertical
  Try DCT-2 in horizontal and DCT-2 in vertical
Encoder signals whether DCT-2/DCT-2
  if not DCT-2/DCT-2 then:
    one bit for horizontal (DST-7/DCT-8) always 0
    one bit for vertical (DST-7/DCT-8) always 0
2.9% BDR gain
26% extra encoder run time
AI compared to turning MTS off:
0.38%

## Slide 5: Normative test: Don’t signal DCT-8.
0.30%
For each block smaller than 64 in both dimensions:
  Try DST-7 in horizontal and DST-7 in vertical
  Try DCT-2 in horizontal and DCT-2 in vertical
Encoder signals whether DCT-2/DCT-2
  if not DCT-2/DCT-2 then:
    assume DST-7/DST-7
3.0% BDR gain
26% extra encoder run time
AI compared to turning MTS off:
0.08%

## Slide 6: Current encoder approach
For each block smaller than 64 in both dimensions:
  Try DST-7 in horizontal and DST-7 in vertical
  Try DST-7 in horizontal and DCT-8 in vertical
  Try DCT-8 in horizontal and DST-7 in vertical
  Try DCT-8 in horizontal and DCT-8 in vertical
  Try DCT-2 in horizontal and DCT-2 in vertical
Encoder signals whether DCT-2/DCT-2
  if not DCT-2/DCT-2 then:
    one bit for horizontal (DST-7/DCT-8)
    one bit for vertical (DST-7/DCT-8)
2.0 % BDR gain
60% extra encoder run time
RA compared to turning MTS off:

## Slide 7: Non-normative test
For each block smaller than 64 in both dimensions:
  Try DST-7 in horizontal and DST-7 in vertical
  Try DCT-2 in horizontal and DCT-2 in vertical
Encoder signals whether DCT-2/DCT-2
  if not DCT-2/DCT-2 then:
    one bit for horizontal (DST-7/DCT-8) always 0
    one bit for vertical (DST-7/DCT-8) always 0
1.8% BDR gain
44 % extra encoder run time
RA compared to turning MTS off:
0.2%

## Slide 8: Normative test
For each block smaller than 64 in both dimensions:
  Try DST-7 in horizontal and DST-7 in vertical
  Try DCT-2 in horizontal and DCT-2 in vertical
Encoder signals whether DCT-2/DCT-2
  if not DCT-2/DCT-2 then:
    assume DST-7/DST-7
RA compared to turning MTS off:
1.9% BDR gain
44 % extra encoder run time
0.13%
0.07%

## Slide 9: Proposals
An encoder that wants to save time can turn off testing DCT-8:
  AI: BDR penalty 0.38%, encoder run time goes from 100% to 62%
    Assuming original gain was -3.3%, this is 88% of the gain preserved
  RA: BDR penalty 0.20%, encoder run time goes from 100% to 90%
    Assuming original gain was -2.0% this is 90% of the gain preserved
First proposal: adopt this non-normative change to the encoder to save run time.

## Slide 10: Proposals
An encoder that turns off DCT-8 testing pays a penalty of having to signal DST-7/DCT-8 = 0 always.
If this is corrected in a normative way, BDR penalty can be further reduced.
  AI: BDR penalty goes down from 0.38% to 0.30%, encoder run time goes from 100% to 62%
    This is 90% of the original gain of 3.3%
  RA: BDR penalty goes down from 0.20% to 0.13%, encoder run time goes from 100% to 90%.
    This is 94% of the original gain of -2.0%
Second proposal: investigate non-normative ways to avoid the penalty