## Slide 1: JVET-M0073: On early termination for BDOF
K. Kondo, M. Ikeda, T. Suzuki (Sony)
Notes: 1

## Slide 2: Summary
Problem statement for hardware complexity
Solutions to solve
Experiments and result
Conclusions

## Slide 3: Early termination in BDOF
SAD
Decoded picture buffer
Large memory size is required to compute SAD in CU level (max 128x128).
It’s not match to the concept of VPDU
Interpolation filter
Memory
128x128
Interpolation filter
Gradient filter
Gradient filter
L0
L1
Early termination decision using the SAD value
Memory
128x128
BIO process
The same problem is expresssed also from two contributions.
JVET-M0249”, Non-CE9: Modifications on Bi-Directional Optical Flow”, (Bytedance)
JVET-M0284, “CE9-related: BDOF Modifications to Enable 64x64 VPDU”, (Huawei)

## Slide 4: Solution-1
EE region
0
64x64
EE region
1
64x64
EE region
2
64x64
EE region
4
64x64
Early exit (EE) region
is decided in PU level
Max 128x128
CTU
BDOF
Max 128x128
Solution-1 64x64
EE0
32x32
EE1
32x32
EE2
32x32
EE3
32x32
EE4
32x32
EE5
32x32
EE6
32x32
EE7
32x32
EE8
32x32
EE9
32x32
EE10
32x32
EE11
32x32
EE12
32x32
EE13
32x32
EE14
32x32
EE15
32x32
Solution-1 32x32
VTM-3.0
Solution-1 16x16
Compute SAD for each early exit (EE) region.
If SAD is smaller than the threshold value, the BDOF process skips for the EE region.
The threshold value in original is divided by number of regions.
Test variation for EE region size

## Slide 5: Solution-2 and solution-3
Solution-2
  When the width or height is larger than 64, BDOF is always enabled.
    No need SAD computation as beyond VPDU.
Solution-3
  When the width or height is larger than 64, BDOF is always disabled.
    No need SAD computation as beyond VPDU.

## Slide 6: Buffer size reduction
SAD
Decoded picture buffer
Interpolation filter
Memory
128x128
Interpolation filter
L0
L1
Memory
128x128
 | VTM-3.0 | Solution-1 64x64 | Solution-1 32x32 | Solution-1 16x16 | Solution-2 | Solution-3
Buffer size in pixel | 128x128 | 64x64 | 32x32 | 16x16 | 64x64 | 64x64
Buffer size % | 100% | 25% | 6% | 2% | 25% | 25%
VTM-3.0

## Slide 7: Solution-1
 |  |  | Random access Main10 |  | 
 |  |  | Over VTM 3.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | 0.05% | 0.01% | 101% | 100%
Class A2 | -0.01% | 0.00% | -0.01% | 102% | 101%
Class B | 0.00% | -0.01% | -0.04% | 101% | 101%
Class C | 0.00% | 0.00% | 0.01% | 100% | 101%
Class E |  |  |  |  | 
Overall | 0.00% | 0.01% | -0.01% | 101% | 101%
Class D | 0.00% | 0.00% | 0.00% | 100% | 100%
Class F | 0.00% | 0.00% | 0.00% | 102% | 106%
 |  |  | Random access Main10 |  | 
 |  |  | Over VTM 3.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.03% | 0.02% | 101% | 102%
Class A2 | -0.01% | -0.01% | 0.05% | 102% | 102%
Class B | 0.00% | 0.01% | -0.03% | 101% | 102%
Class C | 0.00% | 0.02% | -0.02% | 100% | 101%
Class E |  |  |  |  | 
Overall | 0.00% | 0.01% | 0.00% | 101% | 101%
Class D | 0.00% | -0.06% | 0.00% | 100% | 100%
Class F | -0.02% | -0.04% | -0.02% | 102% | 107%
 |  |  | Random access Main10 |  | 
 |  |  | Over VTM 3.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.03% | 0.00% | 101% | 101%
Class A2 | -0.02% | -0.02% | 0.02% | 102% | 102%
Class B | -0.01% | 0.01% | -0.05% | 101% | 102%
Class C | 0.00% | -0.01% | -0.03% | 100% | 101%
Class E |  |  |  |  | 
Overall | -0.01% | 0.00% | -0.02% | 101% | 101%
Class D | 0.01% | -0.06% | -0.02% | 100% | 101%
Class F | -0.01% | -0.03% | -0.02% | 102% | 107%
Solution-1 64x64
Solution-1 32x32
Solution-1 16x16
The BD-rate impact is negligible.
Runtime is almost same as anchor.

## Slide 8: Solution-2 and solution-3
 |  |  | Random access Main10 |  | 
 |  |  | Over VTM 3.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | 0.03% | 0.01% | 101% | 101%
Class A2 | -0.03% | -0.01% | 0.05% | 101% | 101%
Class B | 0.00% | -0.02% | -0.04% | 100% | 101%
Class C | 0.00% | 0.00% | -0.01% | 100% | 100%
Class E |  |  |  |  | 
Overall | 0.00% | 0.00% | -0.01% | 100% | 101%
Class D | 0.00% | 0.00% | 0.00% | 99% | 100%
Class F | -0.01% | -0.01% | -0.01% | 101% | 106%
 |  |  | Random access Main10 |  | 
 |  |  | Over VTM 3.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.23% | 0.19% | 0.14% | 99% | 95%
Class A2 | 0.30% | 0.23% | 0.20% | 100% | 98%
Class B | 0.15% | 0.15% | 0.06% | 99% | 96%
Class C | 0.02% | 0.02% | 0.00% | 99% | 99%
Class E |  |  |  |  | 
Overall | 0.16% | 0.14% | 0.09% | 99% | 97%
Class D | 0.09% | 0.07% | 0.06% | 99% | 99%
Class F | -0.04% | -0.02% | -0.01% | 100% | 96%
Solution-2
Solution-3
Thanks InterDigital for the cross-check!
JVET-M0813
Decoding time slightly decreases, but
0.16% loss for solution-3

## Slide 9: Conclusions
Current BDOF needs large buffer size beyond VPDU
All solutions can reduce the buffer size
For solution-1 and solution-2, almost no change BD-rate.
For solution-3, slight BD loss 0.16% for Y was confirmed.
Recommendation
  Solution-1 or solution-2 is adopted.
 | VTM-3.0 | Solution-1 64x64 | Solution-1 32x32 | Solution-1 16x16 | Solution-2 | Solution-3
Buffer size in pixel | 128x128 | 64x64 | 32x32 | 16x16 | 64x64 | 64x64
Buffer size % | 100% | 25% | 6% | 2% | 25% | 25%