## Slide 1: JVET-M0118 CE10-related: A fix for merge_triangle_flag signaling
Ruoyang Yu
Ericsson
2019-01

## Slide 2: Background
In the last JVET (Macao) meeting, three tools related to merge were adopted:
  MMVD (merge with motion vector difference)
  Combined intra inter prediction (CIIP), also called multi-hypothesis intra inter prediction
  Triangle prediction
The three tools are independent from each other.

## Slide 3: merge_triangle_flag signaling in VTM-3.0
The merge_triangle_flag indicates the usage of triangle prediction for a CU.
When a CU uses MMVD or CIIP, the merge_triangle_flag would always have a value of 0. But in VTM-3.0, the flag is still signaled in those cases.
  Redundant bits are spent.

## Slide 4: Proposed fix for the merge_triangle_flag signaling
It is proposed to avoid signaling the merge_triangle_flag when a CU uses MMVD or CIIP.
The proposed syntax (modification on top of the VVC Draft 3 version 9):
It is noted that in the draft, the merge_triangle_flag is already not signaled when MMVD is enabled for a CU.
… | 
if( sps_triangle_enabled_flag && tile_group_type = = B && cbWidth * cbHeight >= 64 && ciip_flag[ x0 ][ y0 ] = = 0 ) | 
merge_triangle_flag[ x0 ][ y0 ] | ae(v)
… | 

## Slide 5: BD-rate results for the proposed fix
The encoding time and decoding time are not reliable.

## Slide 6: Summary
A fix for the merge_triangle_flag signaling is presented.
It is proposed to adopt the fix to the next VVC draft and VTM.
Thanks to MediaTek for cross-checking.