## Slide 1: CE10-related: Joint optimizations of Triangular prediction unit mode and Multi-Hypothesis prediction mode JVET-M0207
Jan., 2019
Seungsoo Jeong, Min Woo Park, Anish Tamse, Minsoo Park and Kiho Choi (Samsung)
JVET 13th Meeting

## Slide 2: Introduction
  This contribution proposes optimization tests related to Triangular prediction unit mode (Triangle prediction mode) and Multi-Hypothesis (MH) prediction mode
  The first optimization test is the removal of unnecessary flag signalling when MH mode flag is ON.
  The second optimization test is the unification of enable condition between MH mode and Triangular prediction unit mode.
  The third optimization test is the combination of test 1 and test 2.

## Slide 3: Optimiztion test 1
Removal of redundant mode flag
  Currently, when Multi-Hypothesis (MH) prediction mode flag is ON, Triangle partition mode flag is signalled.
  Since MH mode doesn’t use Triangle partition, Triangle partition mode flag does not have to be signalled.
  Optimization 1 is the removal of this redundant Triangle partition mode flag signalling, when MH mode is ON.
Table 1. Proposed merge data syntax
merge_data( x0, y0, cbWidth, cbHeight ) { | Descriptor
if( sps_triangle_enabled_flag && slice_type = = B && mh_intra_flag[ x0 ][ y0 ] == 0 && cbWidth * cbHeight >= 64 ) | 
merge_triangle_flag[ x0 ][ y0 ] | ae(v)
if( merge_triangle_flag[ x0 ][ y0 ] ) | 
merge_triangle_idx[ x0 ][ y0 ] | ae(v)
else if( MaxNumMergeCand > 1 ) | 
merge_idx[ x0 ][ y0 ] | ae(v)
} | 

## Slide 4: Optimization test 2
Unification of enabling condition of MH and Triangle partition mode
  Currently, after skip and merge flag, there are MH mode flag and Triangle prediction mode flag. These two tools’ enable conditions are different with each other. Each tool enables under different conditions.
  The second optimization is the unification of enable condition between MH mode and Triangle prediction mode. After the unification of two tools’ enable conditions, two tools can be conducted with one enable condition without performance loss.
Table 2. Proposed merge data syntax
merge_data( x0, y0, cbWidth, cbHeight ) { | Descriptor
if( sps_mh_intra_enabled_flag && cu_skip_flag[ x0 ][ y0 ] = = 0 && ( cbWidth * cbHeight ) >= 64 && cbWidth < 128 && cbHeight < 128 ) { | 
mh_intra_flag[ x0 ][ y0 ] | ae(v)
if( mh_intra_flag[ x0 ][ y0 ] ) { | 
if ( cbWidth <= 2 * cbHeight ¦ ¦ cbHeight <= 2 * cbWidth ) | 
mh_intra_luma_mpm_flag[ x0 ][ y0 ] | ae(v)
if( mh_intra_luma_mpm_flag[ x0 ][ y0 ] ) | 
mh_intra_luma_mpm_idx[ x0 ][ y0 ] | ae(v)
} | 
} | 
if( sps_triangle_enabled_flag && slice_type = = B && (cbWidth * cbHeight ) >= 64 && cbWidth < 128 && cbHeight < 128) | 
merge_triangle_flag[ x0 ][ y0 ] | ae(v)
if( merge_triangle_flag[ x0 ][ y0 ] ) | 
merge_triangle_idx[ x0 ][ y0 ] | ae(v)
else if( MaxNumMergeCand > 1 ) | 
merge_idx[ x0 ][ y0 ] | ae(v)
} | 

## Slide 5: Optimiztion test 3
The combination of test 1 and test 2
Table 3. Proposed merge data syntax
merge_data( x0, y0, cbWidth, cbHeight ) { | Descriptor
if( sps_mh_intra_enabled_flag && cu_skip_flag[ x0 ][ y0 ] = = 0 && ( cbWidth * cbHeight ) >= 64 && cbWidth < 128 && cbHeight < 128 ) { | 
mh_intra_flag[ x0 ][ y0 ] | ae(v)
if( mh_intra_flag[ x0 ][ y0 ] ) { | 
if ( cbWidth <= 2 * cbHeight ¦ ¦ cbHeight <= 2 * cbWidth ) | 
mh_intra_luma_mpm_flag[ x0 ][ y0 ] | ae(v)
if( mh_intra_luma_mpm_flag[ x0 ][ y0 ] ) | 
mh_intra_luma_mpm_idx[ x0 ][ y0 ] | ae(v)
} | 
} | 
if( sps_triangle_enabled_flag && slice_type = = B && (cbWidth * cbHeight ) >= 64 && mh_intra_flag[ x0 ][ y0 ] == 0 && cbWidth < 128 && cbHeight < 128) | 
merge_triangle_flag[ x0 ][ y0 ] | ae(v)
if( merge_triangle_flag[ x0 ][ y0 ] ) | 
merge_triangle_idx[ x0 ][ y0 ] | ae(v)
else if( MaxNumMergeCand > 1 ) | 
merge_idx[ x0 ][ y0 ] | ae(v)
} | 

## Slide 6: Result
RA | Y | U | V | Enc. | Dec. | LD | Y | U | V | Enc. | Dec.
Test 1 | -0.02% | -0.01% | -0.04% | 100% | 99% | Test 1 | -0.03% | -0.18% | -0.12% | 99% | 98%
Test 2 | -0.01% | 0.00% | -0.01% | 101% | 99% | Test 2 | 0.01% | 0.00% | 0.09% | 98% | 99%
Test 3 | -0.03% | -0.01% | -0.04% | 99% | 99% | Test 3 | -0.04% | -0.04% | -0.04% | 98% | 98%

## Slide 7: Conclusion
This contribution includes two optimization tests. ( Removal of unnecessary flag signalling and Unification of enable condition between MH mode and Triangle prediction mode )
0.03% gain in RA and 0.04% gain in LDB in Test 3.
The adoption of Test 3 on VVC software is requested.
We thank Qualcomm for cross-checking.

## Slide 8
Thank you

## Slide 9: Result
Test 1 : Removal of redundant mode flag

## Slide 10: Result
Test 2 : Unification of enabling condition of MH and Triangle partition mode

## Slide 11: Result
Test 3 : The combination results of Test 1 + Test 2