## Slide 1
JVET-M0314
CE4-related: MMVD improving with signaling distance table
Jingya Li, Ru-Ling Liao Chong Soon Lim

## Slide 2: Introduction
Improving CE4.4.5: MMVD with adaptive distance table
Signaling adaptive distance table at picture level instead of deriving at decoder
Reducing decoder complexity
-0.20% gain in RA when combining with CE4.4.5.c -0.33% gain in RA when combining with CE4.4.4.e
Distance IDX | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Binary Value | 000 | 001 | 010 | 011 | 100 | 101 | 110 | 111

## Slide 3: Simulation results
Random Access | CE4.4.5.c Adaptive distance table for MMVD |  |  |  |  | CE4.4.5.c + signaled distance table (proposed) |  |  |  | 
Main 10 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.46% | -0.64% | -0.72% | 99% | 98% | -0.44% | -0.62% | -0.70% | 99% | 98%
Class A2 | -0.28% | -0.82% | -0.69% | 101% | 97% | -0.28% | -0.81% | -0.69% | 100% | 97%
Class B | -0.17% | -0.23% | -0.40% | 104% | 98% | -0.13% | -0.19% | -0.36% | 103% | 96%
Class C | -0.15% | -0.23% | -0.17% | 107% | 98% | -0.05% | -0.13% | -0.07% | 107% | 99%
Overall | -0.24% | -0.43% | -0.46% | 103% | 98% | -0.20% | -0.38% | -0.42% | 103% | 97%
Class D | -0.19% | -0.44% | -0.38% | 108% | 98% | 0.04% | -0.22% | -0.16% | 108% | 100%
Class F | -0.15% | -0.20% | -0.23% | 108% | 100% | -0.09% | -0.14% | -0.17% | 108% | 98%
Low delay B | CE4.4.5.c Adaptive distance table for MMVD |  |  |  |  | CE4.4.5.c + signaled distance table (proposed) |  |  |  | 
Main 10 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class B | -0.13% | -0.51% | -0.08% | 104% | 100% | -0.09% | -0.48% | -0.04% | 103% | 100%
Class C | -0.17% | 0.15% | -0.02% | 106% | 100% | -0.07% | 0.24% | 0.07% | 106% | 100%
Class E | -0.06% | 0.25% | -0.03% | 104% | 100% | 0.33% | 0.58% | 0.30% | 104% | 100%
Overall | -0.13% | -0.10% | -0.04% | 105% | 100% | 0.02% | 0.02% | 0.08% | 104% | 100%
Class D | -0.17% | -0.60% | -0.18% | 107% | 100% | 0.05% | -0.41% | 0.01% | 107% | 99%
Class F | -0.30% | -0.80% | -0.61% | 105% | 100% | -0.16% | -0.68% | -0.49% | 105% | 100%
Negligible loss in RA

## Slide 4: Simulation results
Random Access | CE4.4.4.e 8 direction + adaptive distance table |  |  |  |  | CE4.4.4.e + signaled distance table (proposed) |  |  |  | 
Main 10 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.57% | -0.62% | -0.75% | 98% | 100% | -0.55% | -0.60% | -0.73% | 99% | 100%
Class A2 | -0.52% | -0.69% | -0.75% | 100% | 100% | -0.51% | -0.68% | -0.74% | 100% | 101%
Class B | -0.29% | -0.18% | -0.32% | 101% | 99% | -0.25% | -0.14% | -0.28% | 101% | 100%
Class C | -0.23% | -0.27% | -0.28% | 104% | 100% | -0.13% | -0.17% | -0.19% | 104% | 100%
Overall | -0.38% | -0.39% | -0.48% | 101% | 100% | -0.33% | -0.35% | -0.44% | 101% | 100%
Class D | -0.36% | -0.28% | -0.22% | 105% | 100% | -0.12% | -0.05% | 0.01% | 105% | 104%
Class F | -0.16% | -0.21% | -0.20% | 107% | 100% | -0.10% | -0.15% | -0.14% | 107% | 101%
Low delay B | CE4.4.4.e 8 direction + adaptive distance table |  |  |  |  | CE4.4.4.e + signaled distance table (proposed) |  |  |  | 
Main 10 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class B | -0.17% | -0.42% | 0.15% | 102% | 100% | -0.13% | -0.38% | 0.18% | 102% | 100%
Class C | -0.19% | 0.01% | -0.15% | 103% | 100% | -0.08% | 0.10% | -0.06% | 104% | 100%
Class E | -0.05% | 0.25% | -0.09% | 102% | 100% | 0.38% | 0.61% | 0.28% | 102% | 100%
Overall | -0.15% | -0.11% | -0.01% | 102% | 100% | 0.01% | 0.03% | 0.13% | 103% | 100%
Class D | -0.26% | -0.63% | -0.08% | 103% | 100% | -0.03% | -0.43% | 0.12% | 104% | 100%
Class F | -0.10% | -0.23% | -0.63% | 103% | 100% | 0.04% | -0.11% | -0.51% | 104% | 100%

## Slide 5: Conclusions
Signaling adaptive distance table for MMVD at picture level
Reducing decoder complexity
-0.20% gain in RA when combining with CE4.4.5.c -0.33% gain in RA when combining with CE4.4.4.e
It is suggested to adopt this proposal to VVC

## Slide 6: Acknowledgments
Thank Sharp for cross-checking

## Slide 7: Adaptive distance table based on resolution
Selecting distance table according to picture resolution
Distance IDX | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Pixel distance | 1/4-pel | 1/2-pel | 1-pel | 2-pel | 4-pel | 8-pel | 16-pel | 32-pel
Distance IDX | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Pixel distance | 1-pel | 2-pel | 4-pel | 8-pel | 16-pel | 32-pel | 64-pel | 128-pel
For picture resolution ≤ 2K
For picture resolution > 2K

## Slide 8: Adaptive distance table based on occurrence
Reordering distance according to occurrence in 1st reference picture of L0
Example
Occurrence in 1st ref. pic. of L0 (from high to low)
2-pel
4-pel
1-pel
8-pel
½-pel
¼-pel
16-pel
32-pel
reordering according to occurrence using weight table
Distance table of 1st reference picture of L0
Distance IDX | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Pixel distance | 1/4-pel | 1/2-pel | 1-pel | 2-pel | 4-pel | 8-pel | 16-pel | 32-pel
Distance IDX | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Pixel distance | 2-pel | 4-pel | 1-pel | 8-pel | 1/2-pel | 1/4-pel | 16-pel | 32-pel
signaling distance table of current picture

## Slide 9: Distance table reordering on encoder side
Order with highest are selected on encoder side and signaled to decoder
distance | position |  |  |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
1/4-pel | 0 | -1 | -2 | -3 | -4 | -5 | -6 | -6
1/2-pel | 2 | 1 | 0 | -1 | -2 | -3 | -4 | -4
1-pel | 4 | 3 | 2 | 1 | 0 | -1 | -2 | -2
2-pel | 6 | 5 | 4 | 3 | 2 | 1 | 0 | 0
4-pel | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 2
8-pel | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 4
16-pel | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 6
32-pel | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 8
How to derive weight table on encoder side
Distance IDX | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Pixel distance | 1/2-pel | 1/4-pel | 1-pel | 2-pel | 4-pel | 8-pel | 16-pel | 32-pel
Weight table | 2 | -1 | 2 | 3 | 4 | 5 | 6 | 8