## Slide 1: Non-CE8: Non-CE8 : MMVD harmonization with CPR (JVET-M0341)
Hyeongmun Jang (hm.jang@lge.com)

## Slide 2: Summary
Harmonize MMVD with CPR
  Proposed method.
    Modified syntax signaling but reuse context model of mmvd for CPR-MMVD
  Additional proposed method
    Re-use conventional mmvd syntax
    Derive mmvd distance to integer-pel based on conventional mmvd distance table.
Experimental result (cross-check by Tencent)
  Proposed method.
    -0.3%, -0.13% BD-rate change for AI and RA respectively. (SCC)
  Additional proposed method
    - 0.03%, 0.02% BD-rate change for AI and RA respectively. (SCC)

## Slide 3: Proposed method
Proposed method
  MMVD and CPR could be enabled together.
  Include CPR candidate during merge candidate construction.
  Syntax signaling
    For P-Slice (which current picture is only one reference picture),
      Modified syntax signaling but re-use conventional context model of mmvd
      1 base motion candidate, modified 4 mmvd distance index, 4 mmvd direction
    For B-Slice
      Conventional mmvd syntax
      2 base motion candidate, 8 mmvd distance index, 4 mmvd direction
  MMVD candidate derivation process
    If base motion is CPR coded based on modified mmvd distance
    Otherwise, conventional mmvd derivation process
mmvd_distance_idx | MmvdDistance(integer)
0 | 1
1 | 2
2 | 4
3 | 6
4 | 8
5 | 12
6 | 16
7 | 32

## Slide 4: Additional proposed method
Re-use conventional mmvd syntax and distance table without any modification.
CPR coded block is included in mmvd base motion candidate.
  If base motion candidate is CPR coded,
    Conventional mmvd merge mode derivation process, except integer-pel mmvd distance derivation process
  Otherwise,
    Conventional mmvd merge mode derivation process
mmvd_distance_idx | MmvdDistance
0 | 1
1 | 2
2 | 4
3 | 8
4 | 16
5 | 32
6 | 64
7 | 128
MmvdOffset[ x0 ][ y0 ][ 0 ] = ( MmvdDistance[ x0 ][ y0 ] << 4 ) * MmvdSign[ x0 ][ y0 ][0]
MmvdOffset[ x0 ][ y0 ][ 1 ] = ( MmvdDistance[ x0 ][ y0 ] << 4 ) * MmvdSign[ x0 ][ y0 ][1]
MmvdOffset[ x0 ][ y0 ][ 0 ] = ( MmvdDistance[ x0 ][ y0 ] << 2 ) * MmvdSign[ x0 ][ y0 ][0]
MmvdOffset[ x0 ][ y0 ][ 1 ] = ( MmvdDistance[ x0 ][ y0 ] << 2 ) * MmvdSign[ x0 ][ y0 ][1]

## Slide 5: Experimental results
 | All Intra Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-3.0-CPR-off |  |  |  |  | Over VTM-3.0-CPR-on |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.08% | -0.08% | 0.00% | 128% | 100% | 0.00% | 0.02% | -0.05% | 101% | 100%
Class A2 | -0.54% | -0.55% | -0.61% | 131% | 100% | -0.07% | -0.05% | -0.06% | 102% | 100%
Class B | -0.32% | -0.46% | -0.39% | 139% | 100% | -0.02% | -0.08% | -0.03% | 102% | 100%
Class C | -0.10% | -0.26% | -0.31% | 144% | 101% | -0.01% | -0.01% | -0.07% | 104% | 100%
Class E | -0.70% | -0.81% | -0.66% | 143% | 100% | -0.06% | -0.01% | -0.07% | 102% | 100%
Overall | -0.30% | -0.43% | -0.39% | 137% | 100% | -0.03% | -0.03% | -0.05% | 102% | 100%
Class D | -0.12% | -0.13% | 0.00% | 140% | 100% | -0.02% | 0.10% | -0.21% | 103% | 100%
Class F (optional) | -12.19% | -12.04% | -11.96% | 161% | 98% | -0.13% | -0.01% | 0.13% | 104% | 100%
Class SCC 1080p | -37.10% | -36.25% | -36.52% | 114% | 83% | -0.30% | -0.22% | -0.26% | 105% | 100%
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-3.0-CPR-off |  |  |  |  | Over VTM-3.0-CPR-on |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.13% | -0.03% | 0.26% | 99% | 100% | -0.01% | 0.01% | 0.04% | 100% | 100%
Class A2 | -0.03% | 0.03% | 0.09% | 97% | 100% | -0.03% | -0.04% | -0.15% | 100% | 100%
Class B | 0.00% | 0.00% | -0.24% | 99% | 100% | -0.02% | 0.01% | -0.03% | 100% | 100%
Class C | 0.19% | -0.07% | 0.26% | 102% | 99% | 0.00% | -0.01% | 0.18% | 100% | 99%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | 0.07% | -0.02% | 0.06% | 99% | 100% | -0.01% | -0.01% | 0.01% | 100% | 100%
Class D | 0.18% | -0.23% | 0.17% | 102% | 99% | 0.03% | 0.05% | 0.02% | 100% | 100%
Class F (optional) | -9.93% | -9.86% | -10.17% | 107% | 99% | -0.07% | 0.05% | -0.25% | 101% | 99%
Class SCC 1080p | -22.13% | -21.74% | -22.28% | 103% | 97% | -0.13% | -0.18% | -0.20% | 100% | 101%
Result of proposed method

## Slide 6
 | All Intra Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-3.0-CPR-off |  |  |  |  | Over VTM-3.0-CPR-on |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.08% | -0.13% | 0.05% | 140% | 99% | 0.00% | -0.03% | -0.01% | 110% | 99%
Class A2 | -0.55% | -0.60% | -0.64% | 139% | 100% | -0.07% | -0.10% | -0.09% | 108% | 100%
Class B | -0.33% | -0.44% | -0.42% | 149% | 99% | -0.04% | -0.06% | -0.06% | 110% | 99%
Class C | -0.13% | -0.23% | -0.27% | 153% | 101% | -0.05% | 0.02% | -0.03% | 110% | 101%
Class E | -0.72% | -0.83% | -0.68% | 153% | 100% | -0.08% | -0.02% | -0.09% | 110% | 99%
Overall | -0.32% | -0.43% | -0.39% | 147% | 100% | -0.05% | -0.04% | -0.05% | 110% | 100%
Class D | -0.16% | 0.00% | 0.12% | 150% | 100% | -0.06% | 0.23% | -0.09% | 110% | 100%
Class F (optional) | -12.11% | -12.16% | -12.09% | 164% | 98% | -0.02% | -0.13% | 0.01% | 106% | 99%
Class SCC 1080p | -36.93% | -36.07% | -36.34% | 114% | 83% | -0.03% | 0.06% | 0.03% | 104% | 99%
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-3.0-CPR-off |  |  |  |  | Over VTM-3.0-CPR-on |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.13% | 0.06% | 0.18% | 99% | 100% | -0.01% | 0.10% | -0.05% | 100% | 100%
Class A2 | -0.04% | -0.03% | 0.21% | 97% | 100% | -0.04% | -0.10% | -0.03% | 100% | 100%
Class B | 0.01% | -0.01% | -0.26% | 99% | 100% | -0.01% | -0.01% | -0.05% | 100% | 100%
Class C | 0.19% | -0.18% | 0.11% | 102% | 99% | 0.00% | -0.12% | 0.03% | 101% | 99%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | 0.07% | -0.05% | 0.02% | 100% | 100% | -0.01% | -0.04% | -0.03% | 100% | 100%
Class D | 0.17% | -0.27% | 0.18% | 103% | 99% | 0.01% | 0.01% | 0.03% | 101% | 100%
Class F (optional) | -9.85% | -9.81% | -9.81% | 108% | 99% | 0.04% | 0.12% | 0.15% | 101% | 100%
Class SCC 1080p | -22.02% | -21.59% | -22.11% | 104% | 97% | 0.02% | -0.01% | -0.01% | 101% | 100%
Result of additional proposed method