## Slide 1: JVET-M0400 - CE2-related: Worst-case memory bandwidth reduction for VVC
Wei-Jung Chien, Luong Pham Van
Han Huang, Vadim Seregin, Marta Karczewicz
@qualcomm
01/2019
AV

## Slide 2: Memory bandwith with luma filter
Luma filter: 8-tap filter  bandwidth = (w + 7) * (h + 7)
In VVC, uni-pred 4x4 and bi-pred 4x4, 8x4/4x8, 16x4/4x16 have higher bandwidth than worst-case of HEVC
Prediction | Block size | # of fetch pixels | # of fetched pixels /1 luma pixel | Over HEVC worst case (%)
bi | 4x4 | 242 | 15.13 | 115
uni | 4x4 | 121 | 7.56 | 8
bi | 4x8/8x4 | 330 | 10.31 | 47
bi | 4x16/16x4 | 506 | 7.91 | 12
bi | 8x8 | 450 | 7.03 | 0
bi | 9x9 | 512 | 8.00 | 14
*bi-pred 9x9 is the worst-case proposed in JVET-M0150 , CE2.4.3(c)

## Slide 3: Memory bandwith with chroma filter
Chroma filter: 4-tap filter  bandwidth = (w + 3) * (h + 3)
Prediction | Block size | # of fetch pixels | # of fetched pixels /1 luma pixel | Over HEVC worst case (%)
Bi | 4x4 | 98 | 6.13 | -13
Uni | 4x4 | 49 | 3.06 | -56
Bi | 4x8/8x4 | 154 | 4.81 | -32
Bi | 4x16/16x4 | 266 | 4.16 | -41

## Slide 4: Proposed worst-case bandwidth reduction Block size restriction
Test1.1: 47% over HEVC: (worst case is 4x8/8x4 bi-prediction)
9x9 affine restriction is tested for affine bi-prediction.
If the restriction is not satisfied  sub-block size = 8x8.
Test 1.2: 14% over HEVC: (worst case is affine 9x9 bi-prediction)
Include Test 1.1 restriction
bi-prediction is excluded from 4x8/8x4.
Test 1.1: 8% over HEVC: (worst case is 4x4 uni-prediction)
Affine bi-prediction is performed using sub-block size of 8x8.
bi-prediction is excluded from 4x8/8x4 and 4x16/16x4.

## Slide 5: Proposed worst-case bandwidth reduction Switch filter
Test1.1: 47% over HEVC: (worst case is 4x8/8x4 bi-prediction)
9x9 affine restriction is tested for affine bi-prediction.
If the restriction is not satisfied  use chroma filter for luma MC.
Test 1.2: 14% over HEVC: (worst case is affine 9x9 bi-prediction)
Include Test 1.1 restriction
Chroma filter is used for bi-pred 4x8/8x4 luma MC.
Test 1.1: 8% over HEVC: (worst case is 4x4 uni-prediction)
Chroma filter is used for bi-pred of 8x4/4x8, 16x4/4x16, and bi-pred affine

## Slide 6: Experimental results over VTM3.0, CTC condition
Good trade-off: 14% bandwidth over worst-case of HEVC
Suggested solution: Switch filter

## Slide 7: Experimental results – Block size restriction
RA |  |  |  | 
Y | U | V | EncT | DecT
0.01% | 0.05% | 0.06% | 100% | 101%
0.20% | 0.33% | 0.44% | 98% | 97%
0.09% | 0.24% | 0.21% | 98% | 98%
0.19% | 0.23% | 0.30% | 101% | 102%
0.12% | 0.22% | 0.25% | 99% | 100%
0.34% | 0.36% | 0.36% | 101% | 101%
0.16% | 0.18% | 0.22% | 99% | 98%
LDB |  |  |  | 
Y | U | V | EncT | DecT
0.12% | -0.04% | 0.30% | 101% | 102%
0.21% | 0.50% | 0.45% | 101% | 101%
0.06% | 0.27% | -0.85% | 99% | 100%
0.13% | 0.22% | 0.06% | 101% | 101%
0.33% | 0.62% | 0.33% | 99% | 95%
0.13% | 0.04% | 0.39% | 99% | 99%
RA |  |  |  | 
Y | U | V | EncT | DecT
0.08% | 0.06% | 0.15% | 98% | 99%
0.71% | 0.73% | 0.83% | 96% | 97%
0.56% | 0.72% | 0.67% | 97% | 96%
0.62% | 0.67% | 0.76% | 100% | 101%
0.51% | 0.58% | 0.62% | 98% | 98%
1.08% | 1.05% | 1.30% | 98% | 100%
0.68% | 0.70% | 0.74% | 98% | 98%
LDB |  |  |  | 
Y | U | V | EncT | DecT
0.55% | 0.36% | 0.96% | 99% | 98%
0.59% | 0.83% | 0.71% | 99% | 101%
0.42% | 0.29% | 0.35% | 96% | 97%
0.53% | 0.50% | 0.72% | 98% | 99%
1.21% | 0.69% | 0.86% | 96% | 94%
0.56% | 0.43% | 0.75% | 97% | 98%
RA |  |  |  | 
Y | U | V | EncT | DecT
0.00% | 0.05% | -0.01% | 99% | 100%
0.14% | 0.16% | 0.17% | 98% | 99%
0.00% | 0.00% | -0.11% | 98% | 98%
0.03% | 0.06% | 0.06% | 102% | 102%
0.03% | 0.06% | 0.01% | 99% | 99%
0.00% | -0.11% | 0.07% | 101% | 102%
0.05% | 0.03% | 0.03% | 98% | 98%
LDB |  |  |  | 
Y | U | V | EncT | DecT
0.01% | -0.28% | -0.10% | 101% | 100%
0.00% | 0.01% | -0.04% | 102% | 102%
-0.05% | 0.11% | -0.05% | 99% | 99%
-0.01% | -0.08% | -0.07% | 101% | 100%
0.03% | -0.11% | -0.10% | 100% | 95%
0.08% | 0.24% | 0.05% | 99% | 98%
Class A1
Class A2
Class B
Class C
Class E
Overall
Class D
Class F
Class A1
Class A2
Class B
Class C
Class E
Overall
Class D
Class F
Test1.1: 47% - CE2.4.3 c
Test1.2: 14%
Test1.3: 8%

## Slide 8: Experimental results – Switch filter
RA |  |  |  | 
Y | U | V | EncT | DecT
0.03% | 0.01% | 0.08% | 100% | 100%
0.01% | -0.03% | -0.05% | 101% | 101%
-0.01% | 0.10% | 0.01% | 100% | 99%
0.06% | 0.08% | 0.05% | 100% | 101%
0.02% | 0.05% | 0.02% | 100% | 100%
0.14% | -0.06% | 0.05% | 100% | 100%
0.02% | -0.04% | 0.01% | 100% | 99%
LDB |  |  |  | 
Y | U | V | EncT | DecT
0.03% | -0.11% | 0.03% | 101% | 102%
0.07% | 0.40% | 0.24% | 102% | 104%
-0.12% | 0.25% | -0.50% | 101% | 101%
0.01% | 0.15% | -0.03% | 101% | 102%
0.17% | 0.71% | 0.51% | 101% | 99%
0.07% | -0.09% | 0.08% | 101% | 103%
RA |  |  |  | 
Y | U | V | EncT | DecT
-0.01% | -0.28% | -0.15% | 107% | 115%
0.17% | 0.01% | 0.06% | 100% | 100%
0.36% | 0.10% | -0.04% | 84% | 96%
0.39% | 0.16% | 0.22% | 83% | 96%
0.26% | 0.01% | 0.02% | 91% | 100%
0.78% | 0.38% | 0.38% | 83% | 93%
0.14% | 0.14% | 0.12% | 83% | 96%
LDB |  |  |  | 
Y | U | V | EncT | DecT
0.32% | 0.09% | 0.34% | 102% | 111%
0.69% | 0.85% | 0.83% | 96% | 99%
0.35% | 0.66% | 0.34% | 83% | 93%
0.45% | 0.49% | 0.50% | 95% | 102%
1.89% | 1.69% | 1.37% | 82% | 89%
0.22% | 0.23% | 0.14% | 82% | 93%
RA |  |  |  | 
Y | U | V | EncT | DecT
0.00% | -0.11% | -0.04% | 100% | 102%
-0.02% | 0.00% | 0.02% | 102% | 101%
-0.02% | 0.09% | 0.05% | 100% | 99%
-0.01% | -0.02% | -0.01% | 101% | 101%
-0.01% | 0.00% | 0.01% | 100% | 101%
0.02% | -0.04% | 0.06% | 100% | 100%
0.01% | -0.03% | -0.06% | 101% | 100%
LDB |  |  |  | 
Y | U | V | EncT | DecT
0.04% | -0.34% | -0.05% | 101% | 102%
-0.01% | 0.05% | -0.05% | 102% | 100%
0.02% | 0.28% | 0.12% | 102% | 104%
0.02% | -0.06% | 0.00% | 102% | 102%
0.02% | 0.31% | -0.02% | 101% | 100%
0.04% | -0.06% | 0.09% | 101% | 103%
Class A1
Class A2
Class B
Class C
Class E
Overall
Class D
Class F
Class A1
Class A2
Class B
Class C
Class E
Overall
Class D
Class F
Test2.1: 47%
Test2.2: 14%
Test2.3: 8%

## Slide 9: Conclusion
Thank Samsung for cross-check
Different worst-case memory bandwidth levels have been proposed
  Block size restriction
  Switch filter
  Good trade-off: 14% bandwidth over worst-case of HEVC
  Suggested solution: Switch filter
  (Y, U, V) BD-rate change: (0.02%, 0.05%, 0.02%) for RA
            (0.01%, 0.15%, -0.03%) for LDB
  Negligible running time change