## Slide 1: JVET-M0437: Non-CE4: Size constraint on MMVD
J. Zhao, S. Kim
LG ELECTRONICS

## Slide 2: Introduction
This proposal proposes to disable MMVD for 4x4 blocks to reduce the MMVD complexity.
.
Result show that the coding impact is 0.01% in RA case, 0.02% in LDB and -0.02% in LDP.

## Slide 3: Background
  In VTM3, MMVD is applied to all block sizes without restriction
  For a CB that uses MMVD, it needs to signal a MMVD flag, starting point, motion magnitude, and motion direction.
  For small block size, the gain may not justify the signalling overhead. It also increases encoder complexities by checking all the MMVD candidates.
  Many other inter tools, such as affine, Multi-Hypothesis Intra-Inter, Triangular prediction etc. have size restrictions based on block width, height or area to reduce their complexities.

## Slide 4: Proposed and Results
Propose to enable MMVD only if block size is larger than 4x4.

## Slide 5: Result
Thanks Tencent for Cross-checking (JVET-M0555)

## Slide 6: CONCLUSIONS
Propose to adopt this simple change to VVC
Thank you!