## Slide 1: JVET-N0131: Offset-based reference samples reduction for CCLM (CE3-1.2.2)
Junyan Huo, Yanzhuo Ma, Shai Wan, Xinwei Li, Jianglin Wang, Xiaoyan Chai, Fuzheng Yang,
Yuanfang Yu, Yang Liu
Mar. 2019

## Slide 2: Current CCLM
Ymax and Ymin are found from the down-sampled neighboring reference samples.

## Slide 3: JVET-N0131 CE3-1.2.2
Using only 4 reference samples for CCLM for any CU size.

## Slide 4: JVET-N0131 CE3-1.2.2
Unified scheme with different CU sizes: 4 reference samples

## Slide 5: JVET-N0131 CE3-1.2.2
Unified scheme with different CU shapes: 4 reference samples

## Slide 6: JVET-N0131 CE3-1.2.2
Unified scheme with different CCLM modes: 4 reference samples
CCLM_LT CCLM_T CCLM_L

## Slide 7: How to find the 4 reference samples in CE3-1.2.2
Along one side, reference samples number:
  original: N
  actually used: N’
Sampling interval ∆
Start offset
CCLM_LT
(N’=2 )
CCLM_T
(N’=4 )
CCLM_L
(N’=4 )

## Slide 8: How to find the 4 reference samples in CE3-1.2.2
e.g. CCLM_LT
  N =8
  N’ =2

## Slide 9: How to find the 4 reference samples in CE3-1.2.2
e.g. CCLM_T
  N =16
  N’ =4

## Slide 10: How to find the 4 reference samples in CE3-1.2.2
e.g. CCLM_L
  N =16
  N’ =4

## Slide 11: How to find the 4 reference samples in CE3-1.2.2
3 modifications over VTM 4.0.

## Slide 12: Complexity analysis of CE3-1.2.2
The number of reference samples
The number of comparison to find Ymax and Ymin
Short length of chroma block | Current CCLM N | CE3-1.2.2 N’
2 | 4 | 4
4 | 8 | 
8 | 16 | 
16 | 32 | 
32 | 64 | 
 | Current CCLM | CE3-1.2.2
Comparisons | 2N | 8

## Slide 13: Experimental results
 |  |  | All Intra |  | 
 |  |  | Over VTM-4.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.08% | -0.23% | -0.47% | 100% | 100%
Class A2 | -0.01% | 0.05% | -0.03% | 100% | 100%
Class B | -0.02% | -0.42% | -0.48% | 100% | 99%
Class C | -0.03% | -0.32% | -0.35% | 99% | 99%
Class E | -0.03% | -0.11% | -0.13% | 100% | 99%
Overall | -0.03% | -0.24% | -0.31% | 100% | 99%
Class D | -0.02% | -0.13% | -0.34% | 100% | 100%
Class F | -0.03% | -0.01% | -0.41% | 99% | 100%
 |  |  | RandomAccess |  | 
 |  |  | Over VTM-4.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.05% | -0.48% | -0.41% | 100% | 100%
Class A2 | -0.01% | -0.13% | -0.05% | 100% | 100%
Class B | 0.01% | -0.55% | -0.74% | 100% | 100%
Class C | 0.00% | -0.18% | -0.47% | 100% | 100%
Class E |  |  |  |  | 
Overall | -0.01% | -0.35% | -0.46% | 100% | 100%
Class D | -0.01% | -0.43% | -0.62% | 100% | 101%
Class F | -0.05% | -0.16% | -0.36% | 100% | 100%

## Slide 14: CE3-1.6.1+ CE3-1.2.2
Reported the performance in JVET-N0321:
AI: -0.02%/-0.07%/-0.13%, with 100%EncT and 100%DecT
RA: 0.00%/-0.18%/-0.27%, with 100%EncT and 100%DecT

## Slide 15: Conclusion
A reduced reference sample method is proposed to use 4 reference samples for CCLM which is independent of CU size
Small coding gain can be achieved due to the 4 reference samples position design
We recommend to include the proposed method to the next version of WD and VTM.

## Slide 16
Thank you