## Slide 1: Non-CE9: Harmonization of DMVR and MMVD
Eiichi Sasaki
Tomonori Hashimoto
Takeshi Chujoh
Tomohiro Ikai
Sharp Corporation
JVET-N0145

## Slide 2: Introduction
Decoder-side Motion Vector Refinement (DMVR) has been adapted in previous meeting
Currently, DMVR is only applied to the motion vectors derived by conventional merge mode.
In this contribution, we propose a harmonization of DMVR and MMVD.
Copyright © All rights reserved, SHARP CORPORATION
If merge_triangle_flag[ xCb ][ yCb ], inter_affine_flag[ xCb ][ yCb ] and merge_subblock_flag[ xCb ][ yCb ] are all equal to 0, the following applies:
  …
  When all of the following conditions are true, dmvrFlag is set equal to 1:
    sps_dmvr_enabled_flag is equal to 1
    merge_flag[ xCb ][ yCb ] is equal to 1
    both predFlagL0[ 0 ][ 0 ] and predFlagL1[ 0 ][ 0 ] are equal to 1
    mmvd_flag[ xCb ][ yCb ] is equal to 0
    DiffPicOrderCnt( currPic, RefPicList[ 0 ][ refIdxL0 ]) is equal to DiffPicOrderCnt( RefPicList[ 1 ][ refIdxL1 ], currPic )
    cbHeight is greater than or equal to 8
    cbHeight*cbWidth is greater than or equal to 64

## Slide 3: Condition for applying DMVR to MMVD
The search area of DMVR and the distance list of MMVD are partially overlapped.
If DMVR is applied all motion vectors derived by MMVD, this redundancy causes the loss.
To reduce this redundancy, We propose the threshold by distance of MMVD and apply DMVR to MMVD when the distance of MMVD is larger than threshold.
Copyright © All rights reserved, SHARP CORPORATION
 | Random Access Main 10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.05% | -0.10% | -0.06% | 108% | 112%
Class A2 | -0.10% | -0.08% | -0.07% | 108% | 109%
Class B | 0.21% | -0.07% | -0.02% | 109% | 116%
Class C | 0.09% | 0.04% | 0.00% | 110% | 113%
Class E |  |  |  |  | 
Overall | 0.09% | -0.05% | -0.03% | 109% | 113%
Class D | 0.21% | 0.03% | 0.10% | 111% | 109%
Class F | 0.02% | -0.01% | 0.00% | 105% | 119%

## Slide 4: Experimental results
Proposed method is implemented on VTM-4.0 and simulated under CTC
According to the search range of DMVR, We use 2-pel as threshold.
Copyright © All rights reserved, SHARP CORPORATION
 | Random Access Main 10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.09% | -0.18% | -0.19% | 106% | 101%
Class A2 | -0.27% | -0.27% | -0.24% | 106% | 100%
Class B | -0.05% | -0.09% | -0.14% | 106% | 100%
Class C | -0.03% | -0.09% | -0.08% | 107% | 101%
Class E |  |  |  |  | 
Overall | -0.10% | -0.14% | -0.15% | 106% | 101%
Class D | -0.02% | -0.09% | -0.05% | 107% | 101%
Class F | -0.01% | -0.01% | -0.03% | 105% | 100%

## Slide 5: Conclusion
Harmonization of DMVR and MMVD with MMVD distance threshold is proposed.
Proposed method provide 0.10 gain in RA without increasing decoder complexity.
It is suggested study in CE.
Thank Samsung for cross-checking