## Slide 1: Non-CE6: Unification of Implicit Transform Core Selection
H. Gao, S. Esenlik, B. Wang, A. M. Kotra, J. Chen

## Slide 2
Problem Statement
In VTM 4.0, implicit transform core selection is possible, however:
For ISP mode, depending on individual intra mode
For MTS off case, shape adaptive
The implicate transform core selection is complex for ISP mode and not unified for regular intra mode.

## Slide 3
Proposed Method 1 “All DST”
Use DST7 to replace the ISP implicit table
Use DST7 to replace shape adaptive implicit
The size restriction keep unchanged.
  if width >16, DCT2 is used for horizontal transform
  if height > 16, DCT2 is used for vertical transform

## Slide 4
Proposed Method 1 “All DST”
Use DST7 to replace the ISP implicit table
Anchor: VTM-4.0
Test: Anchor + Method 1 to replace ISP table
Test condition: CTC
 |  |  | All Intra Main10 |  | 
 |  |  | Over VTM-4.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | -0.03% | 0.00% | 99% | 99%
Class A2 | -0.03% | 0.07% | -0.08% | 99% | 100%
Class B | -0.01% | 0.00% | 0.05% | 99% | 99%
Class C | 0.04% | -0.11% | -0.04% | 98% | 99%
Class E | -0.06% | -0.13% | -0.12% | 99% | 100%
Overall | -0.01% | -0.04% | -0.03% | 99% | 100%
Class D | 0.01% | -0.03% | -0.19% | 99% | 99%
Class F | 0.05% | -0.05% | -0.19% | 99% | 99%

## Slide 5
Proposed Method 1 “All DST”
Use DST7 to replace shape adaptive implicit
Anchor: VTM-4.0 (enabled shape adaptive)
Test: Anchor + Method 1 to replace shape adaptive
Test condition: CTC + -- MTS=0
 |  |  | All Intra Main10 |  | 
 |  |  | Over VTM-4.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.22% | -0.40% | -0.33% | 101% | 101%
Class A2 | -0.12% | -0.33% | -0.42% | 102% | 101%
Class B | -0.12% | -0.40% | -0.36% | 101% | 102%
Class C | 0.05% | -0.37% | -0.16% | 101% | 100%
Class E | -0.18% | -0.43% | -0.53% | 101% | 100%
Overall | -0.11% | -0.39% | -0.35% | 101% | 101%
Class D | 0.04% | -0.20% | -0.12% | 101% | 99%
Class F | -0.02% | -0.30% | -0.10% | 101% | 101%

## Slide 6
Proposed Method 2 “Ratio Adaptive”
Use “Ratio Adaptive” to replace the ISP implicit table
Use “Ratio Adaptive” to replace shape adaptive implicit
The size restriction keep unchanged.
  if width >16, DCT2 is used for horizontal transform
  if height > 16, DCT2 is used for vertical transform
Ratio adaptive:
  If the ratio of height and width is lager than 2, short edge transform uses DST7, long edge uses DCT2
  Otherwise, both edge using DST7

## Slide 7
Proposed Method 2 “Ratio Adaptive”
Use “Ratio Adaptive” to replace the ISP implicit table
Anchor: VTM-4.0
Test: Anchor + Method 1 to replace ISP table
Test condition: CTC
 |  |  | All Intra Main10 |  | 
 |  |  | Over VTM-4.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | 0.01% | -0.01% | 98% | 99%
Class A2 | -0.01% | 0.08% | -0.05% | 98% | 100%
Class B | 0.02% | 0.01% | 0.06% | 98% | 99%
Class C | 0.06% | -0.05% | 0.16% | 98% | 100%
Class E | 0.06% | 0.07% | 0.03% | 99% | 100%
Overall | 0.02% | 0.02% | 0.05% | 98% | 100%
Class D | 0.05% | -0.02% | 0.01% | 98% | 99%
Class F | 0.01% | 0.06% | 0.08% | 99% | 100%
TGM | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!

## Slide 8
Proposed Method 2 “Ratio Adaptive”
Use “Ratio Adaptive” to replace shape adaptive implicit
Anchor: VTM-4.0 (enabled shape adaptive)
Test: Anchor + Method 1 to replace shape adaptive
Test condition: CTC + -- MTS=0
 |  |  | All Intra Main10 |  | 
 |  |  | Over VTM-4.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.15% | 0.11% | 0.12% | 98% | 99%
Class A2 | 0.05% | -0.03% | -0.07% | 98% | 100%
Class B | 0.00% | -0.14% | -0.13% | 99% | 100%
Class C | -0.01% | -0.20% | -0.06% | 100% | 101%
Class E | -0.10% | -0.14% | -0.12% | 100% | 100%
Overall | 0.02% | -0.10% | -0.06% | 99% | 100%
Class D | -0.03% | -0.30% | -0.09% | 100% | 99%
Class F | -0.06% | -0.20% | -0.27% | 100% | 101%

## Slide 9
Conclusion
Method 1 to replace ISP implicate table has -0.01% AI coding gain
Method 1 to replace shape adaptive implicate table has -0.11% AI coding gain
Method 2 to replace ISP implicate table has 0.02% AI coding loss
Method 2 to replace shape adaptive implicate table has 0.02% AI coding loss
Methods are proposed to be adopted in next version of VVC draft.