## Slide 1: CE6-related: Context selection of last non-zero coefficient position coding based on reduced TU size (related to JVET-M0297 and JVET-M0251/M0257) (JVET-N0194)
Moonmo Koo, Jungah Choi, Mehdi Salehifar, Jaehyun Kim, and Seung Hwan Kim

## Slide 2: Summary
Background and problem statement
  Currently, residual coding is adjusted according to all types of zero-out.
    JVET-M0297: Zero-out of last 16 samples for 32 samples DST-7/DCT-8
    JVET-M0251/M0257: Zero-out of last 32 samples for 64 samples DCT-2 fix
  Mismatch between WD and VTM 4.0 on context selection for last coeff. position coding
    Based on reduced TU size and original one, respectively
  It was commented that the involved TU size could be decided based on experimental results.
    Consistency vs. Coding performance
Experimental results (BD-rate) with VTM 4.0 anchor
  Context selection based on reduced TU size
    i.e. 32 (64) samples DST-7/DCT-8 (DCT-2)  16 (32) samples
  0.10% (AI), 0.05% (RA), and -0.02% (LD)
  Bigger loss in high resolution sequences
    0.24% (AI) and 0.13% (RA) for Class A1
Thanks to Huawei for cross-checking

## Slide 3: Conclusion
If the coding loss is thought to be more critical over TU size consistency, it is recommended that the current working draft text should be aligned with VTM 4.0 implementation.

## Slide 4: Appendix – Related spec text in WD
residual_coding( x0, y0, log2TbWidth, log2TbHeight, cIdx ) {
if( ( tu_mts_idx[ x0 ][ y0 ] > 0 ¦ ¦ ( cu_sbt_flag && log2TbWidth < 6 && log2TbHeight < 6 ) ) && cIdx = = 0 && log2TbWidth > 4 )
log2TbWidth = 4
else
log2TbWidth = Min( log2TbWidth, 5 )
if( tu_mts_idx[ x0 ][ y0 ] > 0 ¦ ¦ ( cu_sbt_flag && log2TbWidth < 6 && log2TbHeight < 6 ) ) && cIdx = = 0 && log2TbHeight > 4 )
log2TbHeight = 4
else
log2TbHeight = Min( log2TbHeight, 5 )
if( log2TbWidth > 0 )
last_sig_coeff_x_prefix
if( log2TbHeight > 0 )
last_sig_coeff_y_prefix
if( last_sig_coeff_x_prefix > 3 )
last_sig_coeff_x_suffix
if( last_sig_coeff_y_prefix > 3 )
last_sig_coeff_y_suffix
……
9.5.4.2.4 Derivation process of ctxInc for the syntax elements last_sig_coeff_x_prefix and last_sig_coeff_y_prefix …… The variable log2TbSize is derived as follows: If the syntax element to be parsed is last_sig_coeff_x_prefix, log2TbSize is set equal to log2TbWidth. Otherwise (the syntax element to be parsed is last_sig_coeff_y_prefix), log2TbSize is set equal to log2TbHeight. The variables ctxOffset and ctxShift are derived as follows: If cIdx is equal to 0, ctxOffset is set equal to 3 * ( log2TbSize − 2 ) + ( ( log2TbSize − 1 ) >> 2 ) and ctxShift is set equal to ( log2TbSize + 1 ) >> 2. Otherwise (cIdx is greater than 0), ctxOffset is set equal to 21 and ctxShift is set equal to Clip3( 0, 2, 2log2TbSize >> 3 ). The variable ctxInc is derived as follows: ctxInc = ( binIdx >> ctxShift ) + ctxOffset (9‑31)
residual_coding( ) | last_sig_coeff_x_prefix | TR | cMax = ( log2TbWidth << 1 ) − 1, cRiceParam = 0
 | last_sig_coeff_y_prefix | TR | cMax = ( log2TbHeight << 1 ) − 1, cRiceParam = 0
 | …… | …… | ……

## Slide 5: Appendix – Related spec text aligned with VTM 4.0
residual_coding( x0, y0, log2TbWidth, log2TbHeight, cIdx ) {
if( ( tu_mts_idx[ x0 ][ y0 ] > 0 ¦ ¦ ( cu_sbt_flag && log2TbWidth < 6 && log2TbHeight < 6 ) ) && cIdx = = 0 && log2TbWidth > 4 )
log2ZoTbWidth = 4
else
log2ZoTbWidth = Min( log2TbWidth, 5 )
if( tu_mts_idx[ x0 ][ y0 ] > 0 ¦ ¦ ( cu_sbt_flag && log2TbWidth < 6 && log2TbHeight < 6 ) ) && cIdx = = 0 && log2TbHeight > 4 )
log2ZoTbHeight = 4
else
log2ZoTbHeight = Min( log2TbHeight, 5 )
if( log2TbWidth > 0 )
last_sig_coeff_x_prefix
if( log2TbHeight > 0 )
last_sig_coeff_y_prefix
if( last_sig_coeff_x_prefix > 3 )
last_sig_coeff_x_suffix
if( last_sig_coeff_y_prefix > 3 )
last_sig_coeff_y_suffix
log2TbWidth = log2ZoTbWidth
log2TbHeight = log2ZoTbHeight
……
9.5.4.2.4 Derivation process of ctxInc for the syntax elements last_sig_coeff_x_prefix and last_sig_coeff_y_prefix …… The variable log2TbSize is derived as follows: If the syntax element to be parsed is last_sig_coeff_x_prefix, log2TbSize is set equal to log2TbWidth. Otherwise (the syntax element to be parsed is last_sig_coeff_y_prefix), log2TbSize is set equal to log2TbHeight. The variables ctxOffset and ctxShift are derived as follows: If cIdx is equal to 0, ctxOffset is set equal to 3 * ( log2TbSize − 2 ) + ( ( log2TbSize − 1 ) >> 2 ) and ctxShift is set equal to ( log2TbSize + 1 ) >> 2. Otherwise (cIdx is greater than 0), ctxOffset is set equal to 21 and ctxShift is set equal to Clip3( 0, 2, 2log2TbSize >> 3 ). The variable ctxInc is derived as follows: ctxInc = ( binIdx >> ctxShift ) + ctxOffset (9‑31)
residual_coding( ) | last_sig_coeff_x_prefix | TR | cMax = ( log2ZoTbWidth << 1 ) − 1, cRiceParam = 0
 | last_sig_coeff_y_prefix | TR | cMax = ( log2ZoTbHeight << 1 ) − 1, cRiceParam = 0
 | …… | …… | ……

## Slide 6: Appendix – Experimental results
CTC
Inter MTS on
Low QP (12, 17, 22, and 27)
Config. | BD-rate |  |  | EncT | DecT
 | Y | U | V |  | 
AI | 0.10% | 0.11% | 0.06% | 101% | 101%
RA | 0.05% | 0.00% | -0.01% | 99% | 99%
LDB | -0.02% | 0.25% | 0.61% | 98% | 98%
Config. | BD-rate |  |  | EncT | DecT
 | Y | U | V |  | 
RA | 0.07% | 0.03% | 0.05% | 99% | 99%
LDB | 0.04% | 0.14% | 0.70% | 99% | 99%
Config. | BD-rate |  |  | EncT | DecT
 | Y | U | V |  | 
AI 100 frs. | 0.03% | 0.07% | 0.04% | 100% | 99%