## Slide 1: pic_struct in JVET-O042
chadfogg@gmail.com

## Slide 2: pic_struct in VVC WD 5 (JVET-N1001) [annotated]
Value | Indicated display of picture | Restrictions
0 | (progressive) Frame | field_seq_flag shall be equal to 0
1 | Top field | field_seq_flag shall be equal to 1
2 | Bottom field | field_seq_flag shall be equal to 1
3 | Top field, bottom field, in that order | field_seq_flag shall be equal to 0
4 | Bottom field, top field, in that order | field_seq_flag shall be equal to 0
5 | Top field, bottom field, top field repeated, in that order | field_seq_flag shall be equal to 0
6 | Bottom field, top field, bottom field repeated, in that order | field_seq_flag shall be equal to 0
7 | Frame doubling | field_seq_flag shall be equal to 0 fixed_pic_rate_within_cvs_flag shall be equal to 1
8 | Frame tripling | field_seq_flag shall be equal to 0 fixed_pic_rate_within_cvs_flag shall be equal to 1
9 | Top field paired with previous bottom field in output order | field_seq_flag shall be equal to 1
10 | Bottom field paired with previous top field in output order | field_seq_flag shall be equal to 1
11 | Top field paired with next bottom field in output order | field_seq_flag shall be equal to 1
12 | Bottom field paired with next top field in output order | field_seq_flag shall be equal to 1
Set used in progressive live broadcasts (dominant use case)
Set used in interlaced live field sequence broadcasts (required by DVB for HEVC)
Set theoretically used in frame sequences transport of mixed interlace/progressive content (depreciated carry-over from MPEG-2 / AVC’s PAFF)
Set theoretically used in (lazy) live-coded field sequences (disallowed by DVB since it does not specify field pairing)

## Slide 3: Pic_struct: a combination of elements
Frame/field repetition pattern
Coded field parity (top or bottom)
Field pairing indication (now required by DVB)

## Slide 4: JCT solution: JCTVC-X1004
Value | Indicated display of picture | Restrictions
0 | (progressive) frame | field_seq_flag shall be equal to 0
1 | top field | field_seq_flag shall be equal to 1
2 | bottom field | field_seq_flag shall be equal to 1
3 | top field, bottom field, in that order | field_seq_flag shall be equal to 0
4 | bottom field, top field, in that order | field_seq_flag shall be equal to 0
5 | top field, bottom field, top field repeated, in that order | field_seq_flag shall be equal to 0
6 | bottom field, top field, bottom field repeated, in that order | field_seq_flag shall be equal to 0
7 | frame doubling | field_seq_flag shall be equal to 0 fixed_pic_rate_within_cvs_flag shall be equal to 1
8 | frame tripling | field_seq_flag shall be equal to 0 fixed_pic_rate_within_cvs_flag shall be equal to 1
9 | top field paired with previous bottom field in output order | field_seq_flag shall be equal to 1
10 | bottom field paired with previous top field in output order | field_seq_flag shall be equal to 1
11 | top field paired with next bottom field in output order | field_seq_flag shall be equal to 1
12 | bottom field paired with next top field in output order | field_seq_flag shall be equal to 1
13 | frame quadrupling | field_seq_flag shall be 0 fixed_pic_rate_within_cvs_flag shall be equal to 1
14 | frame quintupling | field_seq_flag shall be 0 fixed_pic_rate_within_cvs_flag shall be equal to 1
15 | Reserved | Reserved
Parent bodies disallowed SEI message changes

## Slide 5: Limitations with current pic_struct
m35659, “Liaison Statement on HDR and WCG”, DVB Technical Module Ad-Hoc Group on Audio-Visual Content (TM-AVC), January 2015.
m38279, “Liaison Statement from DVB on HEVC frame repetition signalling,” DVB Technical Module Ad-Hoc Group on Audio-Visual Content (TM-AVC), May 2016.

## Slide 6: pic_struct (natural language) sub-elements
pic_ struct | Indicated display of picture | Frame or field | Field parity | Output behavior of decoded cropped pictures | display processing hints | Application
0 | (progressive) Frame | Frame | - | Output coded frame | Content is progressive | Non-mixed frame rate , progressive content (default)
1 | Top field | Field | Top | Output coded field | Content may be interlace or progressive (set source_scan_type appropriately) | Interlace live video (sports) where the (lazy) encoder does not identify field pairing. Disallowed by DVB
2 | Bottom field | Field | Top | Output coded field |  | 
3 | Top field, bottom field, in that order | Frame | - | Output top field of coded frame first, then output bottom field |  | Interlace, progressive, or mixed interlace-progressive content transported as frame sequences (unusual case, not commonly practiced. Not coding efficient)
4 | Bottom field, top field, in that order | Frame | - | Output bottom field of coded frame first, then output top field |  | 
5 | Top field, bottom field, top field repeated, in that order | Frame | - | Output top field of coded frame first, then output bottom field, then output (repeat) the top field again | frame is progressive, repeated field is not coded but is instead synthesized by decoder output process. | 
6 | Bottom field, top field, bottom field repeated, in that order | Frame | - | Output bottom field of coded frame first, then output top field, then output (repeat) the bottom field again. |  | 
7 | Frame doubling | Frame | - | Output coded frame twice (repeat once) | Content is progressive | Mixed 24p / 60p content where cadence alternates between one and two repetitions e.g. (48+72)/2 = 60 Hz
8 | Frame tripling | Frame | - | Output coded frame three times (repeat twice) |  | 
9 | Top field paired with previous bottom field in output order | Field | Top | Output coded field. | Can be re-interleaved with previous opposite parity field (if source_scan_type = progressive) | live video of mixed interlace, progressive content, and potentially mixed frame rate (24p / 60p) where the encoder does identify field pairing for counting/editing and/or re-interleaving purposes. Required for DVB field sequences.
10 | Bottom field paired with previous top field in output order | Field | Bot | Output coded field. |  | 
11 | Top field paired with next bottom field in output order | Field | Top | Output coded field. | Can be re-interleaved with next opposite parity field (if source_scan_type = progressive) | 
12 | Bottom field paired with next top field in output order | Field | Bot | Output coded field. |  | 

## Slide 7: Converting to explicit sub-elements
pic_ struct | Indicated display of picture | field_seq_flag | bottom_pic_flag (signaled only when field_seq_flag=1) | pic_output_period (DeltaToDivisor) | field_pairing_flag (signaled only when field_seq_flag=1)
0 | (progressive) Frame | 0 (Frame) | - | 1 | -
1 | Top field | 1 (Field) | 0 | 1 | 0
2 | Bottom field | 1 (Field) | 1 | 1 | 0
3 | Top field, bottom field, in that order | 0 (Frame) | - | 2 | -
4 | Bottom field, top field, in that order | 0 (Frame) | - | 2 | -
5 | Top field, bottom field, top field repeated, in that order | 0 (Frame) | - | 3 | -
6 | Bottom field, top field, bottom field repeated, in that order | 0 (Frame) | - | 3 | -
7 | Frame doubling | 0 (Frame) | - | 2 | -
8 | Frame tripling |  | - | 3 | -
9 | Top field paired with previous bottom field in output order | 1 (Field) | 0 | 1 | 0 (paired with previous opposite-parity field)
10 | Bottom field paired with previous top field in output order |  | 1 |  | 
11 | Top field paired with next bottom field in output order |  | 0 |  | 1 (paired with next opposite-parity field)
12 | Bottom field paired with next top field in output order |  | 1 |  | 
X | Frame repetitions > 2 | 0 (Frame) | - | pic_output_period > 3 | -
Depreciated (use pic_struct instead)
Future video support for e.g. 24 frame/sec film in 120, 240, 300 frame/sec UHD video
new elements

## Slide 8: Pic_struct semantics in VVC
pic_struct indicates whether a picture should be displayed as a frame or as one or more fields and, for the display of frames when fixed_pic_rate_within_cvs_flag is equal to 1, may indicate a frame doubling or tripling repetition period for displays that use a fixed frame refresh interval equal to DpbOutputElementalInterval[ n ] as given by Equation E‑65. The interpretation of pic_struct is specified in Table D.2. Values of pic_struct that are not listed in Table D.2 are reserved for future use by ITU-T | ISO/IEC and shall not be present in bitstreams conforming to this version of this Specification. Decoders shall ignore reserved values of pic_struct.
When present, it is a requirement of bitstream conformance that the value of pic_struct shall be constrained such that exactly one of the following conditions is true:
– The value of pic_struct is equal to 0, 7 or 8 for all pictures in the CVS.
– The value of pic_struct is equal to 1, 2, 9, 10, 11 or 12 for all pictures in the CVS.
– The value of pic_struct is equal to 3, 4, 5 or 6 for all pictures in the CVS.
When fixed_pic_rate_within_cvs_flag is equal to 1, frame doubling is indicated by pic_struct equal to 7, which indicates that the frame should be displayed two times consecutively on displays with a frame refresh interval equal to DpbOutputElementalInterval[ n ] as given by Equation E‑65, and frame tripling is indicated by pic_struct equal to 8, which indicates that the frame should be displayed three times consecutively on displays with a frame refresh interval equal to DpbOutputElementalInterval[ n ] as given by Equation E‑65.
NOTE 2 – Frame doubling can be used to facilitate the display, for example, of 25 Hz progressive-scan video on a 50 Hz progressive-scan display or 30 Hz progressive-scan video on a 60 Hz progressive-scan display. Using frame doubling and frame tripling in alternating combination on every

## Slide 9: HEVC/VVC DeltaToDivisor

## Slide 10: Role of duplicate_flag
duplicate_flag equal to 1 indicates that the current picture is indicated to be a duplicate of a previous picture in output order. duplicate_flag equal to 0 indicates that the current picture is not indicated to be a duplicate of a previous picture in output order.
NOTE 4 – The duplicate_flag should be used to mark coded pictures known to have originated from a repetition process such as 3:2 pull-down or other such duplication and picture rate interpolation methods. This flag would commonly be used when a video feed is encoded as a field sequence in a "transport pass-through" fashion, with known duplicate pictures tagged by setting duplicate_flag equal to 1.
NOTE 5 – When field_seq_flag is equal to 1 and duplicate_flag is equal to 1, this should be interpreted as an indication that the access unit contains a duplicated field of the previous field in output order with the same parity as the current field unless a pairing is otherwise indicated by the use of a pic_struct value in the range of 9 to 12, inclusive.

## Slide 11: Alternatives
Break JVET-O0041 into conditional branches where frame_field_info() SEI message has pic_struct or new elements
Only add bottom_pic_flag to slice_header()

## Slide 12: HEVC: calculating output interval
HEVC C.3.3. (Picture output):
When output, the picture is cropped, using the conformance cropping window specified in the active SPS for the picture.
When picture n is a picture that is output and is not the last picture of the bitstream that is output, the value of the variable DpbOutputInterval[ n ] is derived as follows:
  DpbOutputInterval[ n ] = DpbOutputTime[ nextPicInOutputOrder ] − DpbOutputTime[ n ] (C-16)
  where nextPicInOutputOrder is the picture that follows picture n in output order and has PicOutputFlag equal to 1.
E.3.2 HRD parameter semantics:
elemental_duration_in_tc_minus1[ i ] plus 1 (when present) specifies, when HighestTid is equal to i, the temporal distance, in clock ticks, between the elemental units that specify the HRD output times of consecutive pictures in output order as specified below. The value of elemental_duration_in_tc_minus1[ i ] shall be in the range of 0 to 2 047, inclusive.
For each picture n that is output and not the last picture in the bitstream (in output order) that is output, the value of the variable DpbOutputElementalInterval[ n ] is specified by:
DpbOutputElementalInterval[ n ] = DpbOutputInterval[ n ] ÷ DeltaToDivisor. (E-73)

## Slide 13: Why field sequences are coded
Simple transcode mapping from MPEG-2, AVC bitstreams (PAFF or field sequences)
Intra / P-field pair saves ~5% bits compared to coding first frame in GoP as an intra-frame. Content is vertically low-pass filtered for interlace ~0.65 bandpass anyway.
HEVC frame sequence coding of mixed frame/field content is not praticed

## Slide 14
DVB (ETSI TS 101 154 Feb 2018 edition) AVC 25 Hz
Field picture output units assumed, even for progressive content.
2x ratio

## Slide 15
DVB (ETSI TS 101 154 Feb 2018 edition) AVC 30 Hz
Field picture output units assumed, even for progressive content.
2x ratio

## Slide 16: DVB (ETSI TS 101 154 Feb 2018 edition) HEVC
2x ratio
1x ratio

## Slide 17: AVC DeltaTfiDivisor

## Slide 18: AVC
E.2.1 (VUI parameter semantics):
For each picture n where n indicates the n-th picture (in output order) that is output and picture n is not the last picture in the bitstream (in output order) that is output, the value of tfi,dpb( n ) is specified by
  tfi,dpb( n ) = to,dpb( n ) ÷ DeltaTfiDivisor (E-50)
Where to,dpb( n ) is specified in Equation C-13 and DeltaTfiDivisor is specified by Table E-6.
When fixed frame rate flag is equal to 1 for a coded video sequence containing picture n, the value computed for tfi,dpb( n ) shall be equal to tc as specified in Equation C-1 (using the value of tc for the coded video sequence containing picture n.
Annex C:
The variable tc is derived as follows and is called a clock tick:
  tc = num_units_in_tick ÷ time_scale
C.2.2 (Picture decoding and output)
When the decoding process specified in Clause 8 or Annex G is applied, the current picture n is a picture that is output and not the last picture of the bitstream that is output, the value of to,dpb( n ) is derived by:
  to,dpb( n ) = to,dpb( nn ) − to,dpb( n ) (C-13)