## Slide 1
CE8-3.2: Chroma Transform Skip (JVET-O0081)
T. Tsukuba, Y. Yagasaki, M. Ikeda, T. Suzuki

## Slide 2: Results of CE8-3.2 at low QP (7/12/17/22)
YUV4:2:0
YUV4:4:4

## Slide 4: Summary
Enabling chroma transform skip improves chroma BD% for ClassF/SCC/YUV444
Recommend
  Adopt chroma transform skip into the next VTM/VVC WD and enable for SCC contents.
All intra over VTM-5.0 |  |  |  |  | 
 | Y | U | V | encT | decT
class AtoE | 0.02% | 0.04% | 0.02% | 101% | 100%
class F | 0.02% | -0.10% | -0.09% | 101% | 100%
class SCC | 0.02% | -0.57% | -0.85% | 102% | 101%
YUV444 | -0.19% | -1.96% | -2.19% | 104% | 99%
RA over VTM-5.0 |  |  |  | 
Y | U | V | encT | decT
0.03% | -0.01% | 0.15% | 102% | 100%
0.05% | -0.09% | -0.11% | 102% | 100%
-0.03% | -0.72% | -0.98% | 103% | 99%
-0.43% | -2.68% | -2.77% | 103% | 100%
Normal QPs (qp=22,27,32,37)
LB over VTM-5.0 |  |  |  | 
Y | U | V | encT | decT
0.03% | -0.01% | 0.15% | 102% | 100%
0.05% | -0.09% | -0.11% | 102% | 100%
-0.03% | -0.72% | -0.98% | 103% | 99%
-0.43% | -2.68% | -2.77% | 103% | 100%
All intra over VTM-5.0 |  |  |  |  | 
 | Y | U | V | encT | decT
class AtoE | 0.03% | -0.05% | -0.08% | 102% | 100%
class F | -0.21% | -0.89% | -0.83% | 102% | 100%
class SCC | -2.21% | -4.07% | -4.05% | 103% | 98%
YUV444 | -4.35% | -6.84% | -6.81% | 107% | 96%
RA over VTM-5.0 |  |  |  | 
Y | U | V | encT | decT
0.03% | -0.10% | -0.08% | 104% | 100%
-0.19% | -1.56% | -1.33% | 103% | 100%
-6.00% | -2.88% | -2.95% | 104% | 98%
-4.23% | -8.25% | -8.24% | 105% | 98%
Low QPs (qp=2,7,12,17)
LB over VTM-5.0 |  |  |  | 
Y | U | V | encT | decT
0.07% | -0.23% | -0.36% | 102% | 100%
-0.18% | -1.55% | -1.46% | 102% | 98%
-1.48% | -2.47% | -2.61% | 106% | 98%
-4.75% | -8.07% | -7.92% | 104% | 98%

## Slide 5: Introduction
At the 13th meeting, unified Transform Type Signaling in JVET-M0464 [1] was adopt :
  Unified signaling for transform skip and MTS
  Luma transform skip size extension up to 32x32
  No chroma transform skip
  Fast transform type selection as non-normative change: limits # of candidates for RDO to 3 for Intra MTS, and 4 for inter MTS
JVET-N0123 [2] reported that “no chroma transform skip” resulted in small chroma bdrate degradation and requested to study chroma transform skip in CE.
[1] B. Bross, T. Nguyen, P. Keydel, H. Schwarz, D. Marpe, T. Wiegand , “Non-CE8: Unified Transform Type Signalling and Residual Coding for Transform Skip,” JVET-M0464, Joint Video Experts Team (JVET) of ITU-T SG 16 WP 3 and ISO/IEC JTC 1/SC 29/WG 11 13th Meeting: Marrakech, MA, 9-18 Jan. 2019
[2] T. Tsukuba, M. Ikeda, Y. Yagasaki, T. Suzuki , “AHG13/Non-CE6/CE8: Chroma Transform Skip,” JVET-N0123, Joint Video Experts Team (JVET) of ITU-T SG 16 WP 3 and ISO/IEC JTC 1/SC 29/WG 11 14th Meeting: Geneva, CH, 19-27, Mar. 2019

## Slide 6: Proposal: Support chroma transform skip
Aim:
  To overcome chroma bdrate degradation
Other aspects:
  In HEVC, transform skip can be controlled per components: Y/Cb/Cr
  To inherit design spirits of HEVC, transform skip control capability is desirable in VVC

## Slide 7: Proposal: Support chroma transform skip
Signal transform type (transform_skip_flag and mts_idx) per component with minimum changes:
  Add one context model for chroma transform skip
  No MTS for chroma
  No changes of both context model and binarization for MTS signaling
Interaction with LFNST
  Skip both primary and secondary transform when chroma transform skip is used as well as luma TS case.
Interaction TS residual coding
  Straightforwardly apply TS residual coding to chroma transform skipped block as well as luma TS case.

## Slide 8: Highlights of Syntax changes
transform_skip_flag[ x0 ][ y0 ][cIdx] specifies whether a transform is applied to the luma transform block associated with cIdx or not. The array indices x0, y0 specify the location ( x0, y0 ) of the top-left luma sample of the considered transform block relative to the top-left luma sample of the picture. transform_skip_flag[ x0 ][ y0 ][ cIdx ] equal to 1 specifies that no transform is applied to the luma associated transform block. transform_skip_flag[ x0 ][ y0 ][ cIdx ] equal to 0 specifies that the decision whether transform is applied to the luma associated transform block or not depends on other syntax elements.
When transform_skip_flag[ x0 ][ y0 ][ cIdx ] is not present, it is inferred as follows:
If BdcpmFlag[ x0 ][ x0 ] is equal to 1 and cIdx is equal to 0, transform_skip_flag[ x0 ][ y0 ][ cIdx ] is inferred to be equal to 1.
Else if Otherwise (BdcpmFlag[ x0 ][ x0 ] is equal to 0) and cIdx is equal to 0, transform_skip_flag[ x0 ][ y0 ][ cIdx ] is inferred to be equal to 0.
Otherwise (cIdx is not equal to 0), transform_skip_flag[ x0 ][ y0 ][ cIdx ] is inferred to be equal to 0.
tu_mts_idx[ x0 ][ y0 ][ cIdx ] specifies which transform kernels are applied to the residual samples along the horizontal and vertical direction of the associated transform block with cIdx. The array indices x0, y0 specify the location ( x0, y0 ) of the top-left luma sample of the considered transform block relative to the top-left luma sample of the picture.
When tu_mts_idx[ x0 ][ y0 ][cIdx] is not present, it is inferred to be equal to 0.

## Slide 9: Changes for Encoder search algorithm
Encoder search for chroma transform type selection
Similar fast transform type selection algorithm described in [1] is used for chroma TS search:
Firstly, calculate the L1 norm for all 2 candidates ( DCT-II, TS )
Secondly, TS with L1 norm greater than a specific multiple of the DCT-II L1 norm are excluded for further RDO testing.
Additionally, RDO for TS is skipped when cbf with DCT-II case is equal to zero.
Modified chroma intra mode decision
Transform-domain cost (SATD) may not match with TS efficiently since TS applies quantization and entropy coding on the spatial-domain.
Thus, minimum value between SAD and SATD described in [2] is used instead of SATD for chroma intra mode :
Firstly, derive cost per chroma intra mode candidate
  CE8-3.2: cost = min( SAD*2, SATD)
  VTM-5.0: cost = SATD
Secondly, sort cost in descending order and exclude top two modes with larger cost for further RDO testing
[1] B. Bross, T. Nguyen, P. Keydel, H. Schwarz, D. Marpe, T. Wiegand , “Non-CE8: Unified Transform Type Signalling and Residual Coding for Transform Skip,” JVET-M0464, Jan. 2019
[2] X. Zhao, X. Li, S. Liu, “CE6-related: Modified encoder decision for transform skip, ” JVET-N0363, Mar. 2019.

## Slide 10: Simulation Results (YUV420)
 | All Intra Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | 0.03% | -0.03% | 101% | 99%
Class A2 | 0.01% | -0.02% | 0.01% | 101% | 100%
Class B | 0.01% | 0.02% | 0.07% | 101% | 100%
Class C | 0.02% | 0.08% | 0.11% | 101% | 100%
Class E | 0.03% | 0.11% | -0.11% | 101% | 100%
Overall | 0.02% | 0.04% | 0.02% | 101% | 100%
Class D | 0.02% | 0.40% | 0.08% | 101% | 100%
Class F | 0.02% | -0.10% | -0.09% | 101% | 100%
Class SCC | 0.02% | -0.57% | -0.85% | 102% | 101%
 | Random access Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.04% | -0.34% | 0.27% | 101% | 100%
Class A2 | 0.06% | -0.08% | -0.07% | 102% | 100%
Class B | 0.02% | 0.17% | 0.14% | 101% | 100%
Class C | -0.01% | 0.08% | 0.22% | 102% | 100%
Class E |  |  |  |  | 
Overall | 0.03% | -0.01% | 0.15% | 102% | 100%
Class D | 0.02% | 0.19% | 0.52% | 102% | 100%
Class F | 0.05% | -0.09% | -0.11% | 102% | 100%
Class SCC | -0.03% | -0.72% | -0.98% | 103% | 99%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.03% | 0.69% | 0.09% | 101% | 100%
Class C | 0.07% | 0.71% | 0.57% | 102% | 100%
Class E | 0.11% | 1.26% | 1.65% | 100% | 99%
Overall | 0.06% | 0.84% | 0.64% | 101% | 100%
Class D | 0.09% | 1.27% | 1.40% | 101% | 99%
Class F | 0.13% | 0.19% | 0.20% | 103% | 103%
Class SCC | 0.09% | -0.76% | -1.18% | 105% | 112%
 | All Intra Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.03% | -0.01% | 100% | 99%
Class A2 | 0.00% | 0.00% | 0.00% | 103% | 101%
Class B | 0.03% | -0.07% | -0.07% | 102% | 100%
Class C | 0.02% | -0.06% | -0.10% | 104% | 102%
Class E | 0.09% | -0.07% | -0.21% | 102% | 100%
Overall | 0.03% | -0.05% | -0.08% | 102% | 100%
Class D | 0.03% | -0.14% | -0.11% | 103% | 101%
Class F | -0.21% | -0.89% | -0.83% | 102% | 100%
Class SCC | -2.21% | -4.07% | -4.05% | 103% | 98%
 | Random access Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | 0.00% | 0.03% | 104% | 100%
Class A2 | 0.02% | -0.02% | -0.01% | 104% | 99%
Class B | 0.04% | -0.14% | -0.11% | 103% | 100%
Class C | 0.03% | -0.20% | -0.18% | 104% | 100%
Class E |  |  |  |  | 
Overall | 0.03% | -0.10% | -0.08% | 104% | 100%
Class D | 0.04% | -0.21% | -0.20% | 104% | 100%
Class F | -0.19% | -1.56% | -1.33% | 103% | 100%
Class SCC | -6.00% | -2.88% | -2.95% | 104% | 98%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.07% | -0.20% | -0.17% | 103% | 100%
Class C | 0.03% | -0.19% | -0.16% | 102% | 99%
Class E | 0.10% | -0.33% | -0.93% | 101% | 99%
Overall | 0.07% | -0.23% | -0.36% | 102% | 100%
Class D | 0.06% | -0.20% | -0.04% | 103% | 99%
Class F | -0.18% | -1.55% | -1.46% | 102% | 98%
Class SCC | -1.48% | -2.47% | -2.61% | 106% | 98%
Normal QPs
Low QPs (QP=2,7,12,17 with first 100 frames)

## Slide 11: Simulation Results (YUV444)
 | All Intra Main10 |  |  |  | 
 | Over VTM-5.0 Dual Tree On |  |  |  | 
 | Y | U | V | EncT | DecT
TGM 1080p | -0.89% | -4.16% | -4.56% | 107% | 98%
TGM 720p | 0.05% | -1.64% | -2.03% | 104% | 99%
Animation | 0.07% | -0.18% | -0.18% | 102% | 100%
Mixed content | 0.09% | -1.98% | -2.08% | 104% | 100%
Camera-Captured content | 0.04% | 0.00% | 0.02% | 102% | 100%
Overall | -0.19% | -1.96% | -2.19% | 104% | 99%
 | Random access Main10 |  |  |  | 
 | Over VTM-5.0 Dual Tree On |  |  |  | 
 | Y | U | V | EncT | DecT
TGM 1080p | -1.64% | -5.29% | -5.54% | 106% | 99%
TGM 720p | -0.07% | -2.22% | -2.28% | 103% | 100%
Animation | 0.30% | -0.86% | -0.90% | 102% | 100%
Mixed content | -0.11% | -2.78% | -2.73% | 103% | 100%
Camera-Captured content | 0.03% | -0.09% | -0.13% | 102% | 100%
Overall | -0.43% | -2.68% | -2.77% | 103% | 100%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-5.0 Dual Tree On |  |  |  | 
 | Y | U | V | EncT | DecT
TGM 1080p | -1.02% | -4.60% | -5.04% | 105% | 99%
TGM 720p | 0.11% | -2.23% | -2.46% | 102% | 101%
Animation | 0.57% | -0.69% | -0.76% | 103% | 100%
Mixed content | 0.08% | -3.04% | -3.61% | 102% | 99%
Camera-Captured content | 0.08% | -0.20% | 0.03% | 102% | 100%
Overall | -0.14% | -2.55% | -2.82% | 103% | 100%
 | All Intra Main10 |  |  |  | 
 | Over VTM-5.0 DualTree On |  |  |  | 
 | Y | U | V | EncT | DecT
TGM 1080p | -9.91% | -13.53% | -13.36% | 111% | 93%
TGM 720p | -3.95% | -7.07% | -6.75% | 107% | 97%
Animation | -0.05% | -0.55% | -0.58% | 102% | 101%
Mixed content | -3.21% | -6.35% | -6.85% | 106% | 96%
Camera-Captured content | -0.01% | 0.00% | 0.01% | 102% | 99%
Overall | -4.35% | -6.84% | -6.81% | 107% | 96%
 | Random access Main10 |  |  |  | 
 | Over VTM-5.0 DualTree On |  |  |  | 
 | Y | U | V | EncT | DecT
TGM 1080p | -10.19% | -16.14% | -16.00% | 108% | 96%
TGM 720p | -3.34% | -6.94% | -6.52% | 105% | 100%
Animation | -1.79% | -6.63% | -6.25% | 105% | 98%
Mixed content | -1.91% | -5.93% | -6.70% | 104% | 97%
Camera-Captured content | -0.04% | -0.18% | -0.49% | 103% | 100%
Overall | -4.23% | -8.25% | -8.24% | 105% | 98%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-5.0 DualTree On |  |  |  | 
 | Y | U | V | EncT | DecT
TGM 1080p | -12.36% | -16.13% | -15.69% | 106% | 96%
TGM 720p | -3.02% | -6.82% | -6.08% | 104% | 98%
Animation | -2.12% | -5.31% | -5.10% | 104% | 96%
Mixed content | -1.79% | -6.12% | -6.97% | 104% | 98%
Camera-Captured content | -0.04% | -0.14% | -0.28% | 102% | 101%
Overall | -4.75% | -8.07% | -7.92% | 104% | 98%
Normal QPs
Low QPs (QP=2,7,12,17 with first 100 frames)

## Slide 12: Conclusion
Enabling chroma transform skip improves chroma BD% for ClassF/SCC/YUV444
Recommend
  Adopt chroma transform skip into the next VTM/VVC WD and enable for SCC contents.
Thanks HHI for cross-checking
All intra over VTM-5.0 |  |  |  |  | 
 | Y | U | V | encT | decT
class AtoE | 0.02% | 0.04% | 0.02% | 101% | 100%
class F | 0.02% | -0.10% | -0.09% | 101% | 100%
class SCC | 0.02% | -0.57% | -0.85% | 102% | 101%
YUV444 | -0.19% | -1.96% | -2.19% | 104% | 99%
RA over VTM-5.0 |  |  |  | 
Y | U | V | encT | decT
0.03% | -0.01% | 0.15% | 102% | 100%
0.05% | -0.09% | -0.11% | 102% | 100%
-0.03% | -0.72% | -0.98% | 103% | 99%
-0.43% | -2.68% | -2.77% | 103% | 100%
Normal QPs (qp=22,27,32,37)
LB over VTM-5.0 |  |  |  | 
Y | U | V | encT | decT
0.03% | -0.01% | 0.15% | 102% | 100%
0.05% | -0.09% | -0.11% | 102% | 100%
-0.03% | -0.72% | -0.98% | 103% | 99%
-0.43% | -2.68% | -2.77% | 103% | 100%
All intra over VTM-5.0 |  |  |  |  | 
 | Y | U | V | encT | decT
class AtoE | 0.03% | -0.05% | -0.08% | 102% | 100%
class F | -0.21% | -0.89% | -0.83% | 102% | 100%
class SCC | -2.21% | -4.07% | -4.05% | 103% | 98%
YUV444 | -4.35% | -6.84% | -6.81% | 107% | 96%
RA over VTM-5.0 |  |  |  | 
Y | U | V | encT | decT
0.03% | -0.10% | -0.08% | 104% | 100%
-0.19% | -1.56% | -1.33% | 103% | 100%
-6.00% | -2.88% | -2.95% | 104% | 98%
-4.23% | -8.25% | -8.24% | 105% | 98%
Low QPs (qp=2,7,12,17)
LB over VTM-5.0 |  |  |  | 
Y | U | V | encT | decT
0.07% | -0.23% | -0.36% | 102% | 100%
-0.18% | -1.55% | -1.46% | 102% | 98%
-1.48% | -2.47% | -2.61% | 106% | 98%
-4.75% | -8.07% | -7.92% | 104% | 98%